Name:									Id#

COE 405, Term 021

Design & Modeling of Digital Systems

Quiz# 2

Date: Monday, October 21, 2002

# It is required to design a 3-bit register that has the capability to count up, count down, shift left logically, or shift right logically based on a 2-input select. The interface description of the 3-bit register is shown below, where sel determines the operation. When sel=00, the register will count up, when sel=01, it will count down, when sel=10, it will shift left logically, and when sel =11, it will shift right logically. The reset is a synchronous reset and the register is rising-edge triggered.

## Describe an Entity CS3 for the 3-bit register using type BIT and BIT_VECTOR for the interface signals.

## Model a behavioral Architecture Behave for this 3-bit register.

# Text boxes

clk

clk

Sel1Sel0

reset

C2-C0

3-bit Special Register