Name:									Id#

COE 405, Term 162

Design & Modeling of Digital Systems

Quiz# 3  Solution

Date: Thursday, April 13, 2017

# It is required to design a circuit that counts the number of 3-equal consecutive bits (i.e. 000 or 111) through a stream of 64 bit data. The data is applied serially through an input X once the user presses a Start button, where the first bit is transmitted in the same cycle the Start button is asserted. Once the computation is finished the machine asserts a Done signal which remains asserted until the user presses the Start button again or resets the machine. Assume that the machine has Asynchronous Reset input.

## Show the Data path components needed for designing this circuit along with their control signals.

## Show the ASMD chart for control unit of the circuit.