Jan. 20, 2006

COMPUTER ENGINEERING DEPARTMENT

COE 561

Digital System Design and Synthesis

Final Exam

(Open Book Exam)

First Semester (061)

Time: 7:00-10:00 PM

Student Name : ______________________________________________

Student ID.     : ______________________________________________

| Question | Max Points | Score |
| --- | --- | --- |
| Q1 | 25 |  |
| Q2 | 25 |  |
| Q3 | 10 |  |
| Q4 | 40 |  |
| Total | 100 |  |

[25 Points]

# (Q1) Consider a technology library containing the following cells:

| Cell | Area Cost |
| --- | --- |
| INV(x1)=x1’ | 1 |
| NAND2(x1,x2)=(x1 x2)’ | 2 |
| NAND3(x1m x2, x3) = (x1 x2 x3)’ | 3 |
| NOR2(x1,x2)=(x1 + x2)’ | 2 |
| AOI21(x1, x2, x3) = ((x1 x2) + x3)’ | 3 |
| OAI21(x1, x2, x3) = ((x1+x2) x3)’ | 3 |

## Show the pattern trees of the library cells using NAND2 and INV as base functions. Assume that symmetric representations do not need to be stored.

## (ii) Decompose the function f = a + b’ + c using NAND2 and INV as base functions into all possible non-symmetric decompositions. Then, map the decomposed circuits using the given library and determine the decomposition that leads to a lower area cost.

## (iii) Using the dynamic programming approach, map the circuit given below using the given library into the minimum area cost solution.  Inputs are {a, b, c, d, e, f, g} and output is {Z}.

## (iv) Assuming Boolean matching, determine the number of ROBDD’s that need to be stored in the cell library for each of the following cells. Justify your answer.

- f = a b + a c + b c

- f = a b c + a’ b’ d

# [25 Points]

# (Q2) Consider the incompletely-specified FSM that has 4 states, two inputs and two outputs, represented by the following state table:

| Product | Input | Present State | Next State | Output |
| --- | --- | --- | --- | --- |
| P1 | 10 | S1 | S2 | 11 |
| P2 | 00 | S2 | S2 | 11 |
| P3 | 01 | S2 | S2 | 00 |
| P4 | 00 | S3 | S2 | 00 |
| P5 | 10 | S2 | S1 | 11 |
| P6 | 10 | S3 | S1 | 11 |
| P7 | 00 | S1 | S1 | – – |
| P8 | 01 | S3 | S0 | 00 |
| P9 | 11 | S1 | S1 | 10 |
| P10 | 11 | S3 | S3 | 01 |
| P11 | 11 | S0 | S0 | 11 |

## Assuming the following constraints, S0 = S1 OR S3, and that the code of S2 is covered by all other state codes, the state table can be reduced into the table shown below. Using implicant merging, covering and disjunctive relations show step by step how you can obtain the reduced state stable given below.

| Input | Present State | Next State | Output |
| --- | --- | --- | --- |
| –0 | S1, S2 | S2 | 11 |
| 10 | S2, S3 | S1 | 11 |
| 00 | S1 | S1 | – – |
| 01 | S3 | S0 | 00 |
| 11 | S0, S1 | S1 | 10 |
| 11 | S0, S3 | S3 | 01 |

## Show the encoding constraint matrix and compute all the seed dichotomies of the encoding constraint matrix. Then, eliminate seed dichotomies that violate the given covering and disjunctive constraints.

## Compute all the prime dichotomies and eliminate those that violate the disjunctive constraints.

## Find a state encoding satisfying the given constraints. Verify that your encoding satisfies all the constraints.

[10 Points]

# (Q3) Assume that the delay of an Inverter is 1 unit delay, the delay of a 2-input AND gate is 2 unit delays, and the delay of a 2-input OR gate is 2 unit delays. Consider the circuit given below:

# (i) Determine the critical path of this circuit and the maximum propagation delay.

## (ii) Using only the Retiming transformation, reduce the critical path of this circuit with the minimum number of flip-flops possible.

[40 Points]

# (Q4) Consider the equation given below for y:

# [1]= a * b;		[2]=c+d;	[3]=e*f;	[4]=f+g

# [5]= [1]+[2];		[6]=[5]-[3];	y=[6]+[4];

# Inputs are {a, b, c, d, e, f, g} and output is {y}.  Assume that the delay of Multiplier is 50 ns and that of an Adder is 10ns. Assume that the cycle length is 55ns.

# (i) Draw the sequencing graph for the above equation.

## (ii) Show the ASAP and ALAP scheduling of the sequencing graph. Compute the mobility of each operation.

## (iii) Using List Scheduling algorithm LIST_L, schedule the sequencing graph into the minimum number of cycles under the resource constraints of one multiplier and one adder. Show the details of the algorithm step by step and the resulting scheduled sequencing graph.

## (iv) Show an Integer Linear Programming (ILP) model for scheduling the sequencing graph into the minimum number of cycles under the resource constraints of one multiplier and one adder. Assume an upper latency bound of five clock cycles.

## (v) Consider the scheduled sequencing graph based on ALAP scheduling. Assume that the input values will be available to the circuit for only one clock cycle.

- Show the life-time of all intermediate variables.

- Determine the minimum number of registers that are required to store all the temporary variables. Show the mapping of variables to registers. Select a mapping that minimizes the number of multiplexers and interconnect area as much as possible. Assume that operations [1] and [3] are bound to the same multiplier, operations [2], [5], and [6] are bound to the same adder, and operations [4] and y are assigned to the same adder.

- Draw the data-path implementing the ALAP scheduled sequencing graph based on the variable-register mapping that you obtained in (b).