## Slide 1: Floating Point Arithmetic
COE 301 Computer Organization
ICS 233 Computer Architecture and Assembly Language
Dr. Marwan Abu-Amara
College of Computer Sciences and Engineering
King Fahd University of Petroleum and Minerals
[Adapted from slides of Dr. M. Mudawar and Dr. A. El-Maleh, KFUPM]

## Slide 2: Outline
Floating-Point Numbers
IEEE 754 Floating-Point Standard
Floating-Point Addition and Subtraction
Floating-Point Multiplication
Extra Bits and Rounding
MIPS Floating-Point Instructions

## Slide 3: The World is Not Just Integers
Programming languages support numbers with fraction
  Called floating-point numbers
  Examples:
  3.14159265… (π)
  2.71828… (e)
  0.000000001 or 1.0 × 10–9 (seconds in a nanosecond)
  86,400,000,000,000 or 8.64 × 1013 (nanoseconds in a day)
  last number is a large integer that cannot fit in a 32-bit integer
We use a scientific notation to represent
  Very small numbers (e.g. 1.0 × 10–9)
  Very large numbers (e.g. 8.64 × 1013)
  Scientific notation: ± d . f1f2f3f4 … × 10 ± e1e2e3

## Slide 4: Floating-Point Numbers
Examples of floating-point numbers in base 10 …
  5.341×103 , 0.05341×105 , –2.013×10–1 , –201.3×10–3
Examples of floating-point numbers in base 2 …
  1.00101×223 , 0.0100101×225 , –1.101101×2–3 , –1101.101×2–6
  Exponents are kept in decimal for clarity
  The binary number (1101.101)2 = 23+22+20+2–1+2–3 = 13.625
Floating-point numbers should be normalized
  Exactly one non-zero digit should appear before the point
    In a decimal number, this digit can be from 1 to 9
    In a binary number, this digit should be 1
  Normalized FP Numbers: 5.341×103 and –1.101101×2–3
  NOT Normalized: 0.05341×105 and –1101.101×2–6
decimal point
binary point

## Slide 5: Floating-Point Representation
A floating-point number is represented by the triple
  S is the Sign bit (0 is positive and 1 is negative)
    Representation is called sign and magnitude
  E is the Exponent field (signed)
    Very large numbers have large positive exponents
    Very small close-to-zero numbers have negative exponents
    More bits in exponent field increases range of values
  F is the Fraction field (fraction after binary point)
    More bits in fraction field improves the precision of FP numbers
Value of a floating-point number = (-1)S × val(F) × 2val(E)
S
Exponent
Fraction

## Slide 6: Next . . .
Floating-Point Numbers
IEEE 754 Floating-Point Standard
Floating-Point Addition and Subtraction
Floating-Point Multiplication
Extra Bits and Rounding
MIPS Floating-Point Instructions

## Slide 7: IEEE 754 Floating-Point Standard
Found in virtually every computer invented since 1980
  Simplified porting of floating-point numbers
  Unified the development of floating-point algorithms
  Increased the accuracy of floating-point numbers
Single Precision Floating Point Numbers (32 bits)
  1-bit sign + 8-bit exponent + 23-bit fraction
Double Precision Floating Point Numbers (64 bits)
  1-bit sign + 11-bit exponent + 52-bit fraction
S
Exponent8
Fraction23
S
Exponent11
Fraction52
(continued)

## Slide 8: Normalized Floating Point Numbers
For a normalized floating point number (S, E, F)
Significand is equal to (1.F)2 = (1.f1f2f3f4…)2
  IEEE 754 assumes hidden 1. (not stored) for normalized numbers
  Significand is 1 bit longer than fraction
Value of a Normalized Floating Point Number is
(–1)S × (1.F)2 × 2val(E)
(–1)S × (1.f1f2f3f4 …)2 × 2val(E)
(–1)S × (1 + f1×2-1 + f2×2-2 + f3×2-3 + f4×2-4 …)2 × 2val(E)
(–1)S is 1 when S is 0 (positive), and –1 when S is 1 (negative)
S
E
F = f1 f2 f3 f4 …

## Slide 9: Biased Exponent Representation
How to represent a signed exponent? Choices are …
  Sign + magnitude representation for the exponent
  Two’s complement representation
  Biased representation
IEEE 754 uses biased representation for the exponent
  Value of exponent = val(E) = E – Bias (Bias is a constant)
Recall that exponent field is 8 bits for single precision
  E can be in the range 0 to 255
  E = 0 and E = 255 are reserved for special use (discussed later)
  E = 1 to 254 are used for normalized floating point numbers
  Bias = 127 (half of 254), val(E) = E – 127
  val(E=1) = –126, val(E=127) = 0, val(E=254) = 127

## Slide 10: Biased Exponent – Cont’d
For double precision, exponent field is 11 bits
  E can be in the range 0 to 2047
  E = 0 and E = 2047 are reserved for special use
  E = 1 to 2046 are used for normalized floating point numbers
  Bias = 1023 (half of 2046), val(E) = E – 1023
  val(E=1) = –1022, val(E=1023) = 0, val(E=2046) = 1023
Value of a Normalized Floating Point Number is
(–1)S × (1.F)2 × 2E – Bias
(–1)S × (1.f1f2f3f4 …)2 × 2E – Bias
(–1)S × (1 + f1×2-1 + f2×2-2 + f3×2-3 + f4×2-4 …)2 × 2E – Bias

## Slide 11: Examples of Single Precision Float
What is the decimal value of this Single Precision float?
Solution:
  Sign = 1 is negative
  Exponent = (01111100)2 = 124  val(E) = E – bias = 124 – 127 = –3
  Significand = (1.0100 … 0)2 = 1 + 2-2 = 1.25 (1. is implicit)
  Value in decimal = –1.25 × 2–3 = –0.15625
What is the decimal value of?
Solution:
  Value in decimal = +(1.01001100 … 0)2 × 2130–127 =
  (1.01001100 … 0)2 × 23 = (1010.01100 … 0)2 = 10.375
1
0
1
1
1
1
1
0
0
0
1
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
1
0
0
0
0
0
1
0
0
1
0
0
1
1
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
implicit

## Slide 12: Examples of Double Precision Float
What is the decimal value of this Double Precision float ?
Solution:
  Value of exponent = (10000000101)2 – Bias = 1029 – 1023 = 6
  Value of double float = (1.00101010 … 0)2 × 26 (1. is implicit) =
  (1001010.10 … 0)2 = 74.5
What is the decimal value of ?
Do it yourself! (answer should be –1.5 × 2–7 = –0.01171875)
0
1
0
0
0
0
0
0
0
1
0
1
0
0
1
0
1
0
1
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
1
0
1
1
1
1
1
1
1
0
0
0
1
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0

## Slide 13: Converting FP Decimal to Binary
Convert –0.8125 to binary in single and double precision
Solution:
  Fraction bits can be obtained using multiplication by 2
    0.8125 × 2 = 1.625
    0.625 × 2 = 1.25
    0.25 × 2 = 0.5
    0.5 × 2 = 1.0
    Stop when fractional part is 0
  Fraction = (0.1101)2 = (1.101)2 × 2 –1 (Normalized)
  Exponent = –1 + Bias = 126 (single precision) and 1022 (double)
0.8125 = (0.1101)2 = ½ + ¼ + 1/16 = 13/16
1
0
1
1
1
1
1
1
0
1
0
1
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
1
0
1
1
1
1
1
1
1
1
1
0
1
0
1
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
Single Precision
Double Precision

## Slide 14: Largest Normalized Float
What is the Largest normalized float?
Solution for Single Precision:
  Exponent – bias = 254 – 127 = 127 (largest exponent for SP)
  Significand = (1.111 … 1)2 = almost 2
  Value in decimal ≈ 2 × 2127 ≈ 2128 ≈ 3.4028 … × 1038
Solution for Double Precision:
  Value in decimal ≈ 2 × 21023 ≈ 21024 ≈ 1.79769 … × 10308
Overflow: exponent is too large to fit in the exponent field
0
1
1
1
1
1
1
1
0
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
0
1
1
1
1
1
1
1
1
1
1
0
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1

## Slide 15: Smallest Normalized Float
What is the smallest (in absolute value) normalized float?
Solution for Single Precision:
  Exponent – bias = 1 – 127 = –126 (smallest exponent for SP)
  Significand = (1.000 … 0)2 = 1
  Value in decimal = 1 × 2–126 = 1.17549 … × 10–38
Solution for Double Precision:
  Value in decimal = 1 × 2–1022 = 2.22507 … × 10–308
Underflow: exponent is too small to fit in exponent field
0
0
0
0
0
0
0
0
1
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
1
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0

## Slide 16: Zero, Infinity, and NaN
Zero
  Exponent field E = 0 and fraction F = 0
  +0 and –0 are possible according to sign bit S
Infinity
  Infinity is a special value represented with maximum E and F = 0
    For single precision with 8-bit exponent: maximum E = 255
    For double precision with 11-bit exponent: maximum E = 2047
  Infinity can result from overflow or division by zero
  +∞ and –∞ are possible according to sign bit S
NaN (Not a Number)
  NaN is a special value represented with maximum E and F ≠ 0
  Result from exceptional situations, such as 0/0 or sqrt(negative)
  Operation on a NaN results is NaN: Op(X, NaN) = NaN

## Slide 17: Denormalized Numbers
IEEE standard uses denormalized numbers to …
  Fill the gap between 0 and the smallest normalized float
  Provide gradual underflow to zero
Denormalized: exponent field E is 0 and fraction F ≠ 0
  Implicit 1. before the fraction now becomes 0. (not normalized)
Value of denormalized number ( S, 0, F )
Single precision: (–1) S × (0.F)2 × 2–126
Double precision: (–1) S × (0.F)2 × 2–1022
Denorm
Denorm
+∞
Positive
Overflow
-∞
Negative
Overflow
Negative
Underflow
Positive
Underflow
Normalized (–ve)
Normalized (+ve)
2–126
2128
0
-2128
-2–126

## Slide 18: Special Value Rules
Operation | Result
n /  | 0
 x  | 
nonzero / 0 | 
 +  |  (similar for -)
0 / 0 | NaN
 -  | NaN (similar for -)
 /  | NaN
 x 0 | NaN
NaN op anything | NaN

## Slide 19: Floating-Point Comparison
IEEE 754 floating point numbers are ordered
  Because exponent uses a biased representation …
    Exponent value and its binary representation have same ordering
  Placing exponent before the fraction field orders the magnitude
    Larger exponent  larger magnitude
    For equal exponents, Larger fraction  larger magnitude
    0 < (0.F)2 × 2Emin < (1.F)2 × 2E–Bias < ∞ (Emin = 1 – Bias)
  Because sign bit is most significant  quick test of signed <
Integer comparator can compare magnitudes
Integer
Magnitude
Comparator
X < Y
X = Y
X > Y
X = (EX , FX)
Y = (EY , FY)

## Slide 20: Summary of IEEE 754 Encoding
Single-Precision | Exponent = 8 | Fraction = 23 | Value
Normalized Number | 1 to 254 | Anything | ± (1.F)2 × 2E – 127
Denormalized Number | 0 | nonzero | ± (0.F)2 × 2–126
Zero | 0 | 0 | ± 0
Infinity | 255 | 0 | ± ∞
NaN | 255 | nonzero | NaN
Double-Precision | Exponent = 11 | Fraction = 52 | Value
Normalized Number | 1 to 2046 | Anything | ± (1.F)2 × 2E – 1023
Denormalized Number | 0 | nonzero | ± (0.F)2 × 2–1022
Zero | 0 | 0 | ± 0
Infinity | 2047 | 0 | ± ∞
NaN | 2047 | nonzero | NaN

## Slide 21: Next . . .
Floating-Point Numbers
IEEE 754 Floating-Point Standard
Floating-Point Addition and Subtraction
Floating-Point Multiplication
Extra Bits and Rounding
MIPS Floating-Point Instructions

## Slide 22: Floating Point Addition Example
Consider adding: (1.111)2 × 2–1 + (1.011)2 × 2–3
  For simplicity, we assume 4 bits of precision (or 3 bits of fraction)
Cannot add significands … Why?
  Because exponents are not equal
How to make exponents equal?
  Shift the significand of the lesser exponent right
  until its exponent matches the larger number
(1.011)2 × 2–3 = (0.1011)2 × 2–2 = (0.01011)2 × 2–1
  Difference between the two exponents = –1 – (–3) = 2
  So, shift right by 2 bits
Now, add the significands:
Carry
1.111
0.01011
10.00111
+

## Slide 23: Addition Example – cont’d
So, (1.111)2 × 2–1 + (1.011)2 × 2–3 = (10.00111)2 × 2–1
However, result (10.00111)2 × 2–1 is NOT normalized
Normalize result: (10.00111)2 × 2–1 = (1.000111)2 × 20
  In this example, we have a carry
  So, shift right by 1 bit and increment the exponent
Round the significand to fit in appropriate number of bits
  We assumed 4 bits of precision or 3 bits of fraction
Round to nearest: (1.000111)2 ≈ (1.001)2
  Renormalize if rounding generates a carry
Detect overflow / underflow
  If exponent becomes too large (overflow) or too small (underflow)
1.000 111
1
1.001
+

## Slide 24: Floating Point Subtraction Example
Consider: (1.000)2 × 2–3 – (1.000)2 × 22
  We assume again: 4 bits of precision (or 3 bits of fraction)
Shift significand of the lesser exponent right
  Difference between the two exponents = 2 – (–3) = 5
  Shift right by 5 bits: (1.000)2 × 2–3 = (0.00001000)2 × 22
Convert subtraction into addition to 2's complement
+ 0.00001 × 22
– 1.00000 × 22
0 0.00001 × 22
1 1.00000 × 22
1 1.00001 × 22
Sign
Since result is negative, convert result from 2's complement to sign-magnitude
2’s Complement
– 0.11111 × 22
2’s Complement

## Slide 25: Subtraction Example – cont’d
So, (1.000)2 × 2–3 – (1.000)2 × 22 = – 0.111112 × 22
Normalize result: – 0.111112 × 22 = – 1.11112 × 21
  For subtraction, we can have leading zeros
  Count number z of leading zeros (in this case z = 1)
  Shift left and decrement exponent by z
Round the significand to fit in appropriate number of bits
  We assumed 4 bits of precision or 3 bits of fraction
Round to nearest: (1.1111)2 ≈ (10.000)2
Renormalize: rounding generated a carry
–1.11112 × 21 ≈ –10.0002 × 21 = –1.0002 × 22
  Result would have been accurate if more fraction bits are used
1.111 1
1
10.000
+

## Slide 26: Floating Point Addition / Subtraction
1. Compare the exponents of the two numbers. Shift the smaller number to the right until its exponent would match the larger exponent.
2. Add / Subtract the significands according to the sign bits.
3. Normalize the sum, either shifting right and incrementing the exponent or shifting left and decrementing the exponent
4. Round the significand to the appropriate number of bits, and renormalize if rounding generates a carry
Start
Done
Overflow or
underflow?
Exception
yes
no
Shift significand right by
d = | EX – EY |
Add significands when signs
of X and Y are identical,
Subtract when different
X – Y becomes X + (–Y)
Normalization shifts right by 1 if there is a carry, or shifts left by the number of leading zeros in the case of subtraction
Rounding either truncates fraction, or adds a 1 to least significant fraction bit

## Slide 27: Floating Point Adder Block Diagram
c
z
EZ
EX
FX
Shift Right / Left
Inc / Dec
EY
Swap
FY
Shift Right
Exponent
Subtractor
Significand
Adder/Subtractor
1
1
sign
Sign
Computation
d = | EX – EY |
max ( EX , EY )
add / subtract
Rounding Logic
sign
SY
add/sub
FZ
SZ
c
SX
z
Detect carry, or
Count leading 0’s
c
0 1

## Slide 28: Next . . .
Floating-Point Numbers
IEEE 754 Floating-Point Standard
Floating-Point Addition and Subtraction
Floating-Point Multiplication
Extra Bits and Rounding
MIPS Floating-Point Instructions

## Slide 29: Floating Point Multiplication Example
Consider multiplying: 1.0102 × 2–1 by –1.1102 × 2–2
  As before, we assume 4 bits of precision (or 3 bits of fraction)
Unlike addition, we add the exponents of the operands
  Result exponent value = (–1) + (–2) = –3
Using the biased representation: EZ = EX + EY – Bias
  EX = (–1) + 127 = 126 (Bias = 127 for SP)
  EY = (–2) + 127 = 125
  EZ = 126 + 125 – 127 = 124 (value = –3)
Now, multiply the significands:
(1.010)2 × (1.110)2 = (10.001100)2
1.010
1.110
0000
1010
1010
1010
10001100
×
3-bit fraction
3-bit fraction
6-bit fraction

## Slide 30: Multiplication Example – cont’d
Since sign SX ≠ SY, sign of product SZ = 1 (negative)
So, 1.0102 × 2–1 × –1.1102 × 2–2 = –10. 0011002 × 2–3
However, result: –10. 0011002 × 2–3 is NOT normalized
Normalize: 10. 0011002 × 2–3 = 1.00011002 × 2–2
  Shift right by 1 bit and increment the exponent
  At most 1 bit can be shifted right … Why?
Round the significand to nearest:
1.00011002 ≈ 1.0012 (3-bit fraction)
Result ≈ –1. 0012 × 2–2 (normalized)
Detect overflow / underflow
  No overflow / underflow because exponent is within range
1.000 1100
1
1.001
+

## Slide 31: Floating Point Multiplication
1. Add the biased exponents of the two numbers, subtracting the bias from the sum to get the new biased exponent
Multiply the significands. Set the result sign to positive if operands have same sign, and negative otherwise
3. Normalize the product if necessary, shifting its significand right and incrementing the exponent
4. Round the significand to the appropriate number of bits, and renormalize if rounding generates a carry
Start
Done
Overflow or
underflow?
Exception
yes
no
Biased Exponent Addition
EZ = EX + EY – Bias
Result sign SZ = SX xor SY can be computed independently
Since the operand significands 1.FX and 1.FY are ≥ 1 and < 2, their product is ≥ 1 and < 4.
To normalize product, we need to shift right by 1 bit only and increment exponent
Rounding either truncates fraction, or adds a 1 to least significant fraction bit

## Slide 32: Next . . .
Floating-Point Numbers
IEEE 754 Floating-Point Standard
Floating-Point Addition and Subtraction
Floating-Point Multiplication
Extra Bits and Rounding
MIPS Floating-Point Instructions

## Slide 33: Extra Bits to Maintain Precision
Floating-point numbers are approximations for …
  Real numbers that they cannot represent
Infinite variety of real numbers exist between 1.0 and 2.0
  However, exactly 223 fractions can be represented in SP, and
  Exactly 252 fractions can be represented in DP (double precision)
Extra bits are generated in intermediate results when …
  Shifting and adding/subtracting a p-bit significand
  Multiplying two p-bit significands (product can be 2p bits)
But when packing result fraction, extra bits are discarded
We only need few extra bits in an intermediate result
  Minimizing hardware but without compromising precision

## Slide 34: Extra Bits Needed
Three bits are added called Guard, Round, Sticky
  Reduce the hardware and still achieve accurate arithmetic
  As if result significand was computed exactly and rounded
Internal Representation:

## Slide 35: Guard (G) Bit
Guard bit: guards against loss of a significant bit
  Only one guard bit is needed to maintain accuracy of result
  Shifted left (if needed) during normalization as last fraction bit
Example on the need of a guard bit:
1.00000000101100010001101 × 25
– 1.00000000000000011011010 × 2-2 (subtraction)
1.00000000101100010001101 × 25
– 0.00000010000000000000001 1011010 × 25 (shift right 7 bits)
1.00000000101100010001101 × 25
1 1.11111101111111111111110 0 100110 × 25 (2's complement)
0 0.11111110101100010001011 0 100110 × 25 (add significands)
+ 1.11111101011000100010110 1 001100 × 24 (normalized)
Guard bit – do not discard

## Slide 36: Round (R) and Sticky (S) Bits
Two extra bits are needed for rounding
  Rounding performed after normalizing a result significand
  Round bit: appears after the guard bit
  Sticky bit: appears after the round bit (OR of all additional bits)
    Once set to 1 it remains set to 1 (“sticks” to 1)
Consider the same example of previous slide:
1.00000000101100010001101 × 25
1 1.11111101111111111111110 0 1 00110 × 25 (2's complement)
0 0.11111110101100010001011 0 1 1 × 25 (sum)
+ 1.11111101011000100010110 1 1 1 × 24 (normalized)
Round bit
Sticky bit
OR-reduce
Guard bit

## Slide 37: If the three Extra Bits not Used
1.00000000101100010001101 × 25
– 1.00000000000000011011010 × 2-2 (subtraction)
1.00000000101100010001101 × 25
– 0.00000010000000000000001 1011010 × 25 (shift right 7 bits)
1.00000000101100010001101 × 25
1 1.11111101111111111111111 × 25 (2's complement)
0 0.11111110101100010001100 × 25 (add significands)
+ 1.11111101011000100011000 × 24 (normalized without GRS)
+ 1.11111101011000100010110 × 24 (normalized with GRS)
+ 1.11111101011000100010111 × 24 (With GRS after rounding)

## Slide 38: Four Rounding Modes
Normalized result has the form: 1. f1 f2 … fl g r s
  The guard bit g, round bit r and sticky bit s appear after the last fraction bit fl
IEEE 754 standard specifies four modes of rounding
Round to Nearest Even: default rounding mode
  Increment result if: (g=1 and r or s = ‘1’) or (g=1 and r s = “00” and fl = ‘1’)
  Otherwise, truncate result significand to 1. f1 f2 … fl
Round toward +∞: result is rounded up
  Increment result if sign is positive and g or r or s = ‘1’
Round toward –∞: result is rounded down
  Increment result if sign is negative and g or r or s = ‘1’
Round toward 0: always truncate result

## Slide 39: Example on Rounding (1)
Round following result using IEEE 754 rounding modes:
–1.11111111111111111111111 0 0 1 × 2-7
Round to Nearest Even:
  Truncate result since g = ‘0’
  Truncated Result: –1.11111111111111111111111 × 2-7
Round towards +∞:
Round towards –∞:
  Incremented result: –10.00000000000000000000000 × 2-7
  Renormalize and increment exponent (because of carry)
  Final rounded result: –1.00000000000000000000000 × 2-6
Round towards 0:
Guard Bit
Round Bit
Truncate result since negative
Increment since negative and s = ‘1’
Truncate always

## Slide 40: Example on Rounding (2)
Round following result using IEEE 754 rounding modes:
–1.11111111111111111111111 1 0 0 × 2-7
Round to Nearest Even:
  Increment result since grs = “100” and LSB of fraction is 1
  Incremented Result: –10.00000000000000000000000 × 2-7
  Renormalize and increment exponent (because of carry)
Round towards +∞:
Round towards –∞:
  Incremented result: –10.00000000000000000000000 × 2-7
  Renormalize and increment exponent (because of carry)
Round towards 0:
Guard Bit
Round Bit
Truncate result since negative
Increment since negative and g = ‘1’
Truncate always

## Slide 41: FP Subtraction w/ Rounding Example
Perform the following floating-point operation rounding the result to the nearest even
0100 0001 1000 0000 0000 0000 0000 0100
- 0100 0011 1000 0000 0000 0000 0000 0000
We add three bits for each operand representing G, R, S bits as follows:
1.000 0000 0000 0000 0000 0100 000 x 24
- 1.000 0000 0000 0000 0000 0000 000 x 28
= 0 0.000 1000 0000 0000 0000 0000 010 x 28
- 0 1.000 0000 0000 0000 0000 0000 000 x 28
GRS
0
0

## Slide 42: FP Subtraction w/ Rounding Example
= 00.000 1000 0000 0000 0000 0000 010 x 28
+ 11.000 0000 0000 0000 0000 0000 000 x 28
= 11.000 1000 0000 0000 0000 0000 010 x 28
= -0.111 0111 1111 1111 1111 1111 110 x 28
Normalizing the result:
= -1.110 1111 1111 1111 1111 1111 100 x 27
Rounding to nearest even:
= -1.111 0000 0000 0000 0000 0000 x 27
GRS

## Slide 43: Advantages of IEEE 754 Standard
Used predominantly by the industry
Encoding of exponent and fraction simplifies comparison
  Integer comparator used to compare magnitude of FP numbers
Includes special exceptional values: NaN and ±∞
  Special rules are used such as:
    0/0 is NaN, sqrt(–1) is NaN, 1/0 is ∞, and 1/∞ is 0
  Computation may continue in the face of exceptional conditions
Denormalized numbers to fill the gap
  Between smallest normalized number 1.0 × 2Emin and zero
  Denormalized numbers, values 0.F × 2Emin , are closer to zero
  Gradual underflow to zero

## Slide 44: Floating Point Complexities
Operations are somewhat more complicated
In addition to overflow we can have underflow
Accuracy can be a big problem
  Extra bits to maintain precision: guard, round, and sticky
  Four rounding modes
  Division by zero yields Infinity
  Zero divide by zero yields Not-a-Number
  Other complexities
Implementing the standard can be tricky
  See text for description of 80x86 and Pentium bug!
Not using the standard can be even worse

## Slide 45: Accuracy can be a Big Problem
Value1 | Value2 | Value3 | Value4 | Sum
1.0E+30 | -1.0E+30 | 9.5 | -2.3 | 7.2
1.0E+30 | 9.5 | -1.0E+30 | -2.3 | -2.3
1.0E+30 | 9.5 | -2.3 | -1.0E+30 | 0
Adding double-precision floating-point numbers (Excel)
Floating-Point addition is NOT associative
Produces different sums for the same data values
Rounding errors when the difference in exponent is large

## Slide 46: Next . . .
Floating-Point Numbers
IEEE 754 Floating-Point Standard
Floating-Point Addition and Subtraction
Floating-Point Multiplication
Extra Bits and Rounding
MIPS Floating-Point Instructions

## Slide 47: MIPS Floating Point Coprocessor
Called Coprocessor 1 or the Floating Point Unit (FPU)
32 separate floating point registers: $f0, $f1, …, $f31
FP registers are 32 bits for single precision numbers
Even-odd register pair form a double precision register
Use the even number for double precision registers
  $f0, $f2, $f4, …, $f30 are used for double precision
Separate FP instructions for single/double precision
  Single precision: add.s, sub.s, mul.s, div.s (.s extension)
  Double precision: add.d, sub.d, mul.d, div.d (.d extension)
FP instructions are more complex than the integer ones
  Take more cycles to execute

## Slide 48: The MIPS Processor
Memory
Up to 232 bytes = 230 words
4 bytes per word
$0
$1
$2
$31
Hi
Lo
ALU
F0
F1
F2
F31
FP
Arith
EPC
Cause
BadVaddr
Status
EIU
FPU
TMU
Execution &
Integer Unit
(Main proc)
Floating
Point Unit
(Coproc 1)
Trap &
Memory Unit
(Coproc 0)
. . .
. . .
Integer
mul/div
Arithmetic &
Logic Unit
32 General
Purpose
Registers
Integer Multiplier/Divider
32 Floating-Point
Registers
Floating-Point
Arithmetic Unit

## Slide 49: FP Arithmetic Instructions
Instruction | Meaning | Format |  |  |  |  | 
add.s fd, fs, ft | (fd) = (fs) + (ft) | 0x11 | 0 | ft5 | fs5 | fd5 | 0
add.d fd, fs, ft | (fd) = (fs) + (ft) | 0x11 | 1 | ft5 | fs5 | fd5 | 0
sub.s fd, fs, ft | (fd) = (fs) – (ft) | 0x11 | 0 | ft5 | fs5 | fd5 | 1
sub.d fd, fs, ft | (fd) = (fs) – (ft) | 0x11 | 1 | ft5 | fs5 | fd5 | 1
mul.s fd, fs, ft | (fd) = (fs) × (ft) | 0x11 | 0 | ft5 | fs5 | fd5 | 2
mul.d fd, fs, ft | (fd) = (fs) × (ft) | 0x11 | 1 | ft5 | fs5 | fd5 | 2
div.s fd, fs, ft | (fd) = (fs) / (ft) | 0x11 | 0 | ft5 | fs5 | fd5 | 3
div.d fd, fs, ft | (fd) = (fs) / (ft) | 0x11 | 1 | ft5 | fs5 | fd5 | 3
sqrt.s fd, fs | (fd) = sqrt (fs) | 0x11 | 0 | 0 | fs5 | fd5 | 4
sqrt.d fd, fs | (fd) = sqrt (fs) | 0x11 | 1 | 0 | fs5 | fd5 | 4
abs.s fd, fs | (fd) = abs (fs) | 0x11 | 0 | 0 | fs5 | fd5 | 5
abs.d fd, fs | (fd) = abs (fs) | 0x11 | 1 | 0 | fs5 | fd5 | 5
neg.s fd, fs | (fd) = – (fs) | 0x11 | 0 | 0 | fs5 | fd5 | 7
neg.d fd, fs | (fd) = – (fs) | 0x11 | 1 | 0 | fs5 | fd5 | 7

## Slide 50: FP Load/Store Instructions
Separate floating point load/store instructions
  lwc1: load word coprocessor 1
  ldc1: load double coprocessor 1
  swc1: store word coprocessor 1
  sdc1: store double coprocessor 1
Better names can be used for the above instructions
  l.s = lwc1 (load FP single), l.d = ldc1 (load FP double)
  s.s = swc1 (store FP single), s.d = sdc1 (store FP double)
Instruction | Meaning | Format |  |  | 
lwc1 $f2, 40($t0) | ($f2) = Mem[($t0)+40] | 0x31 | $t0 | $f2 | im16 = 40
ldc1 $f2, 40($t0) | ($f3$f2) = Mem[($t0)+40] | 0x35 | $t0 | $f2 | im16 = 40
swc1 $f2, 40($t0) | Mem[($t0)+40] = ($f2) | 0x39 | $t0 | $f2 | im16 = 40
sdc1 $f2, 40($t0) | Mem[($t0)+40] = ($f3$f2) | 0x3d | $t0 | $f2 | im16 = 40
General purpose register is used as the base register

## Slide 51: FP Data Movement Instructions
Moving data between general purpose and FP registers
  mfc1: move from coprocessor 1 (to general purpose register)
  mtc1: move to coprocessor 1 (from general purpose register)
Moving data between FP registers
  mov.s: move single precision float
  mov.d: move double precision float = even/odd pair of registers
Instruction | Meaning | Format |  |  |  |  | 
mfc1 $t0, $f2 | ($t0) = ($f2) | 0x11 | 0 | $t0 | $f2 | 0 | 0
mtc1 $t0, $f2 | ($f2) = ($t0) | 0x11 | 4 | $t0 | $f2 | 0 | 0
mov.s $f4, $f2 | ($f4) = ($f2) | 0x11 | 0 | 0 | $f2 | $f4 | 6
mov.d $f4, $f2 | ($f5$f4)=($f3$f2) | 0x11 | 1 | 0 | $f2 | $f4 | 6

## Slide 52: FP Convert Instructions
Instruction | Meaning | Format |  |  |  |  | 
cvt.s.w fd, fs | to single from integer | 0x11 | 0 | 0 | fs5 | fd5 | 0x20
cvt.s.d fd, fs | to single from double | 0x11 | 1 | 0 | fs5 | fd5 | 0x20
cvt.d.w fd, fs | to double from integer | 0x11 | 0 | 0 | fs5 | fd5 | 0x21
cvt.d.s fd, fs | to double from single | 0x11 | 1 | 0 | fs5 | fd5 | 0x21
cvt.w.s fd, fs | to integer from single | 0x11 | 0 | 0 | fs5 | fd5 | 0x24
cvt.w.d fd, fs | to integer from double | 0x11 | 1 | 0 | fs5 | fd5 | 0x24
Convert instruction: cvt.x.y
  Convert to destination format x from source format y
Supported formats
  Single precision float = .s (single precision float in FP register)
  Double precision float = .d (double float in even-odd FP register)
  Signed integer word = .w (signed integer in FP register)
Different than “move” instructions from previous slide!

## Slide 53: FP Compare and Branch Instructions
Instruction | Meaning | Format |  |  |  |  | 
c.eq.s fs, ft | cflag = ((fs) == (ft)) | 0x11 | 0 | ft5 | fs5 | 0 | 0x32
c.eq.d fs, ft | cflag = ((fs) == (ft)) | 0x11 | 1 | ft5 | fs5 | 0 | 0x32
c.lt.s fs, ft | cflag = ((fs) <= (ft)) | 0x11 | 0 | ft5 | fs5 | 0 | 0x3c
c.lt.d fs, ft | cflag = ((fs) <= (ft)) | 0x11 | 1 | ft5 | fs5 | 0 | 0x3c
c.le.s fs, ft | cflag = ((fs) <= (ft)) | 0x11 | 0 | ft5 | fs5 | 0 | 0x3e
c.le.d fs, ft | cflag = ((fs) <= (ft)) | 0x11 | 1 | ft5 | fs5 | 0 | 0x3e
bc1f Label | branch if (cflag == 0) | 0x11 | 8 | 0 | im16 |  | 
bc1t Label | branch if (cflag == 1) | 0x11 | 8 | 1 | im16 |  | 
FP unit (co-processor 1) has a condition flag
  Set to 0 (false) or 1 (true) by any comparison instruction
Three comparisons: equal, less than, less than or equal
Two branch instructions based on the condition flag

## Slide 54: FP Data Directives
.FLOAT Directive
  Stores the listed values as single-precision floating point
.DOUBLE Directive
  Stores the listed values as double-precision floating point
Examples
  var1: .FLOAT 12.3, -0.1
  var2: .DOUBLE 1.5e-10
  pi: .DOUBLE 3.1415926535897924

## Slide 55
Syscall Services
Service | $v0 | Arguments / Result
Print Integer | 1 | $a0 = integer value to print
Print Float | 2 | $f12 = float value to print
Print Double | 3 | ($f13$f12) = double value to print
Print String | 4 | $a0 = address of null-terminated string
Read Integer | 5 | $v0 = integer read
Read Float | 6 | $f0 = float read
Read Double | 7 | ($f1$f0) = double read
Read String | 8 | $a0 = address of input buffer $a1 = maximum number of characters to read
Exit Program | 10 | 
Print Char | 11 | $a0 = character to print
Read Char | 12 | $a0 = character read
Supported by MARS

## Slide 56: Example 1: Area of a Circle
.data
pi: .double 3.1415926535897924
msg: .asciiz "Circle Area = "
.text
main:
ldc1 $f2, pi # $f3f2 = pi
li $v0, 7 # read double (radius)
syscall # $f0,1 = radius
mul.d $f12, $f0, $f0 # $f13f12 = radius*radius
mul.d $f12, $f2, $f12 # $f13f12= area
la $a0, msg
li $v0, 4 # print string (msg)
syscall
li $v0, 3 # print double (area)
syscall # print $f13f12

## Slide 57: Example 2: Matrix Multiplication
void mm (int n, double x[n][n], y[n][n], z[n][n]) {
for (int i=0; i!=n; i=i+1)
for (int j=0; j!=n; j=j+1) {
double sum = 0.0;
for (int k=0; k!=n; k=k+1)
sum = sum + y[i][k] * z[k][j];
x[i][j] = sum;
}
}
Matrices x, y, and z are n×n double precision float
Matrix size is passed in $a0 = n
Array addresses are passed in $a1, $a2, and $a3
What is the MIPS assembly code for the procedure?

## Slide 58: Address Calculation for 2D Arrays
×
=
X[i][j]
Y[i][k]
Z[k][j]
Matrix X is accessed by row.
Matrix Y is accessed by row.
Matrix Z accessed by column.
&X[i][j] = &X + (i*n + j)* 8 = &X[i][j-1] + 8
&Y[i][k] = &Y + (i*n + k)* 8 = &Y[i][k-1] + 8
&Z[k][j] = &Z + (k*n + j)* 8 = &Z[k-1][j] + 8*n
since X is double precision array

## Slide 59: Matrix Multiplication Procedure – 1/3
Initialize Loop Variables
mm: addu $t1, $0, $0 # $t1 = i = 0; for 1st loop
L1: addu $t2, $0, $0 # $t2 = j = 0; for 2nd loop
L2: addu $t3, $0, $0 # $t3 = k = 0; for 3rd loop
sub.d $f0, $f0, $f0 # $f0 = sum = 0.0
Calculate address of y[i][k] and load it into $f2,$f3
Skip i rows (i×n) and add k elements
L3: multu $t1, $a0 # i*size(row) = i*n
mflo $t4 # $t4 = i*n
addu $t4, $t4, $t3 # $t4 = i*n + k
sll $t4, $t4, 3 # $t4 =(i*n + k)*8
addu $t4, $a2, $t4 # $t4 = address of y[i][k]
ldc1 $f2, 0($t4) # $f2 = y[i][k]

## Slide 60: Matrix Multiplication Procedure – 2/3
Similarly, calculate address and load value of z[k][j]
Skip k rows (k×n) and add j elements
multu $t3, $a0 # k*size(row) = k*n
mflo $t5 # $t5 = k*n
addu $t5, $t5, $t2 # $t5 = k*n + j
sll $t5, $t5, 3 # $t5 =(k*n + j)*8
addu $t5, $a3, $t5 # $t5 = address of z[k][j]
ldc1 $f4, 0($t5) # $f4 = z[k][j]
Now, multiply y[i][k] by z[k][j] and add it to $f0
mul.d $f6, $f2, $f4 # $f6 = y[i][k]*z[k][j]
add.d $f0, $f0, $f6 # $f0 = sum
addiu $t3, $t3, 1 # k = k + 1
bne $t3, $a0, L3 # loop back if (k != n)

## Slide 61: Matrix Multiplication Procedure – 3/3
Calculate address of x[i][j] and store sum
multu $t1, $a0 # i*size(row) = i*n
mflo $t6 # $t6 = i*n
addu $t6, $t6, $t2 # $t6 = i*n + j
sll $t6, $t6, 3 # $t6 =(i*n + j)*8
addu $t6, $a1, $t6 # $t6 = address of x[i][j]
sdc1 $f0, 0($t6) # x[i][j] = sum
Repeat outer loops: L2 (for j = …) and L1 (for i = …)
addiu $t2, $t2, 1 # j = j + 1
bne $t2, $a0, L2 # loop L2 if (j != n)
addiu $t1, $t1, 1 # i = i + 1
bne $t1, $a0, L1 # loop L1 if (i != n)
Return:
jr $ra # return