## Slide 1: ALU Design: Shifter Details
COE 301 Computer Organization
ICS 233 Computer Architecture and Assembly Language
Dr. Marwan Abu-Amara
College of Computer Sciences and Engineering
King Fahd University of Petroleum and Minerals
[Adapted from slides of Dr. M. Mudawar and Dr. A. El-Maleh, KFUPM]

## Slide 2: Building a Multifunction ALU
0
1
2
3
0
1
2
3
Logic Unit
2
AND = 00
OR = 01
NOR = 10
XOR = 11
Logical
Operation
Shifter
2
SLL = 00
SRL = 00
SRA = 01
ROR = 11
Shift/Rotate
Operation
A
32
32
B
A
d
d
e
r
c0
32
32
ADD = 0
SUB = 1
Arithmetic
Operation
Shift = 00
SLT = 01
Arith = 10
Logic = 11
ALU
Selection
32
2
Shift Amount
ALU Result
5
sign
≠
zero
overflow
SLT: ALU does a SUB and check the sign and overflow

## Slide 3: Details of the Shifter
Implemented with multiplexers and wiring
Shift Operation can be: SLL, SRL, SRA, or ROR
Input Data is extended to 63 bits according to Shift Op
The 63 bits are shifted right according to S4S3S2S1S0
S0
32
31
31
1
31
1
split
33
1
1
S1
31
2
31
2
split
35
2
31
2
S2
4
31
4
31
4
split
39
4
31
S3
8
31
8
31
8
split
47
8
31
S4
16
31
16
31
16
0
1
mux
split
63
16
31
Shift Right
0 or 16 bits
Shift Right
0 or 8 bits
Shift Right
0 or 4 bits
Shift Right
0 or 2 bits
Shift Right
0 or 1 bit
0
1
mux
0
1
mux
0
1
mux
0
1
mux
Extender
32
Shift
op
2
Data
Data_out
5
sa
SLL

## Slide 4: Details of the Shifter – cont’d
Input data is extended from 32 to 63 bits as follows:
  If shift op = SRL then ext_data[62:0] = 031 || data[31:0]
  If shift op = SRA then ext_data[62:0] = data[31]31 || data[31:0]
  If shift op = ROR then ext_data[62:0] = data[30:0] || data[31:0]
  If shift op = SLL then ext_data[62:0] = data[31:0] || 031
For SRL, the 32-bit input data is zero-extended to 63 bits
For SRA, the 32-bit input data is sign-extended to 63 bits
For ROR, 31-bit extension = lower 31 bits of data
Then, shift right according to the shift amount
As the extended data is shifted right, the upper bits will be: 0 (SRL), sign-bit (SRA), or lower bits of data (ROR)

## Slide 5: Implementing Shift Left Logical
The wiring of the above shifter dictates a right shift
However, we can convert a left shift into a right shift
For SLL, 31 zeros are appended to the right of data
  To shift left by 0 is equivalent to shifting right by 31
  To shift left by 1 is equivalent to shifting right by 30
  To shift left by 31 is equivalent to shifting right by 0
  Therefore, for SLL use the 1’s complement of the shift amount
ROL is equivalent to ROR if we use (32 – rotate amount)
ROL by 10 bits is equivalent to ROR by (32–10) = 22 bits
Therefore, software can convert ROL to ROR