## Slide 1: COE 202: Digital Logic Design Number Systems Part 3
Courtesy of Dr. Ahmad Almulhem

## Slide 2: Objectives
Binary codes
  Binary coded decimal (BCD)
  Other Decimal Codes
  Gray Code
  ASCII Code
  Error Detecting Code

## Slide 3: Binary Codes
A n-bit binary code is a binary string of 0s and 1s of size n.
It can represent 2n different elements.
  4 elements can be coded using 2 bits
  8 elements can be coded using 3 bits
Given the number of elements to be coded, there is a minimum number of bits, but no maximum !

## Slide 4: Binary Coded Decimal (BCD)
Human communicating with computers
  Humans understand decimal
  Computers understands binary
Solution: Convert Decimal-Binary-Decimal
Need to store decimal numbers as binary codes

## Slide 5: Binary Coded Decimal (BCD)
BCD Code uses 4 bits to represent the 10 decimal digits {0 to 9}
6 BCD codes unused
The weights of the individual positions of the bits of a BCD code are: 23=8, 22=4, 21=2, 20=1

## Slide 6: Other Decimal Codes
4 bits = 16 different codes
Only 10 needed to represent the 10 decimal digits.
Many possible codes!
2421 and excess-3 are self-complementing (9’s complement can be obtained by inverting bits)
src: Mano’s book

## Slide 7: Gray Code
Gray code represents decimal numbers 0 to 15 using 16 4-bit codes
Gray codes of two adjacent decimal numbers differ by only one bit
Example:
  (5)10 = 0111
  (6)10 = 0101
  (7)10 = 0100

## Slide 8: ASCII Character Code
ASCII an abbreviation of “American Standard Code for Information Interchange”
A 7-bit code (128 characters)
  94 printable, 34 non-printable (control)
    2x26 English letters (A,…Z, a,…z)
    10 decimal digits (0,1,…9)
    32 Special Characters such as %, *, $, … etc.
Usually stored as a byte (8 bits)
  The extra bit is used for other purposes

## Slide 9: ASCII Character Code

## Slide 10: ASCII Character Code
capital vs small
A difference of
(20)16 = 3210

## Slide 11: Error Detecting Code
In data communication, errors may happen
  One code change into another code
  How to detect errors?
Add an extra bit called a parity bit such that
  Number of 1’s is even (even parity) or odd (odd parity)

## Slide 12: Error Detecting Code
ASCII A =
ASCII T =

## Slide 13: Conclusions
Bits are bits
  Modern digital devices represent everything as collections of bits
  A computer is one such digital device
You can encode anything with sufficient 1’s and 0’s
  Binary codes (BCD, gray code)
  Text (ASCII)
  Sound (.wav, .mp3, ...)
  Pictures (.jpg, .gif, .tiff)