## Slide 1: COE 202: Digital Logic Design Combinational Circuits Part 1
Courtesy of Dr. Ahmad Almulhem

## Slide 2: Objectives
Types of Logic Circuits
  Combinational
  Sequential
Designing Combinational Circuits
  Procedure
  Examples

## Slide 3: Combinational Circuits
Two classes of logic circuits:
  Combinational Circuits
  Sequential Circuits
A Combinational circuit consists of logic gates
  Output depends only on input
A Sequential circuit consists of logic gates and memory
  Output depends on current inputs and previous ones (stored in memory)
  Memory defines the state of the circuit.

## Slide 4: Combinational Circuits
A combinational circuit has:
  n Boolean inputs (1 or more),
  m Boolean outputs (1 or more)
  logic gates mapping the inputs to the outputs
Combinational
Circuits
n inputs
m outputs

## Slide 5: Designing Combinational Circuits
How to design a combinational circuit?
  Use all the information and tools you learned
    Binary system, Boolean Algebra, K-Maps, etc.
  Follow the step-by-step procedure given next

## Slide 6: Design Procedure
Specification
  Write a specification for the circuit if one is not already available
  Specify/Label input and output
Formulation
  Derive a truth table or initial Boolean equations that define the required relationships between the inputs and outputs, if not in the specification
  Apply hierarchical design if appropriate
Optimization
  Apply 2-level and multiple-level optimization (Boolean Algebra, K-Map, software)
  Draw a logic diagram or provide a netlist for the resulting circuit using ANDs, ORs, and inverters

## Slide 7: Design Procedure (Cont.)
Technology Mapping
  Map the logic diagram or netlist to the implementation technology selected (e.g. map into NANDs)
Verification
  Verify the correctness of the final design manually or using simulation
Practical Considerations:
Cost of gates (Number)
Maximum allowed delay
Fanin/Fanout

## Slide 8: Example 1
Question: Design a circuit that has a 3-bit input and a single output (F) specified as follows:
  F = 0, when the input is less than (5)10
  F = 1, otherwise
Solution:
Step 1 (Specification):
Label the inputs (3 bits) as X, Y, Z
  X is the most significant bit, Z is the least significant bit
The output (1 bit) is F:
  F = 1  (101)2, (110)2, (111)2
  F = 0  other inputs

## Slide 9: Example 1 (cont.)
Question: Design a circuit that has a 3-bit input and a single output (F) specified as follows:
  F = 0, when the input is less than (5)10
  F = 1, otherwise
Solution:
Step 1 (Specification):
Label the inputs (3 bits) as X, Y, Z
  X is the most significant bit, Z is the least significant bit
The output (1 bit) is F:
  F = 1  (101)2, (110)2, (111)2
  F = 0  other inputs

## Slide 10: Example 1 (cont.)
Step 2 (Formulation)
Obtain Truth table
X | Y | Z | F
0 | 0 | 0 | 0
0 | 0 | 1 | 0
0 | 1 | 0 | 0
0 | 1 | 1 | 0
1 | 0 | 0 | 0
1 | 0 | 1 | 1
1 | 1 | 0 | 1
1 | 1 | 1 | 1
X
YZ
0
1
00 01 11 10
0 0 0 0
0 1 1 1
Step 3 (Optimization)
F = XZ + XY
X
Z
X
Y
F
Circuit Diagram

## Slide 11: Example 2
Question (BCD to Excess-3 Code Converter)
Code converters convert from one code to another (BCD to Excess-3 in this example)
The inputs are defined by the code that is to be converted (BCD in this example)
The outputs are defined by the converted code (Excess-3 in this example)
Recall Excess-3 code is a decimal digit plus three converted into binary, i.e. 0 is 0011, 1 is 0100, etc.

## Slide 12: Example 2 (cont.)
 | BCD Input |  |  |  | Excess 3 Output |  |  | 
Decimal | A | B | C | D | W | X | Y | Z
0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1
1 | 0 | 0 | 0 | 1 | 0 | 1 | 0 | 0
2 | 0 | 0 | 1 | 0 | 0 | 1 | 0 | 1
3 | 0 | 0 | 1 | 1 | 0 | 1 | 1 | 0
4 | 0 | 1 | 0 | 0 | 0 | 1 | 1 | 1
5 | 0 | 1 | 0 | 1 | 1 | 0 | 0 | 0
6 | 0 | 1 | 1 | 0 | 1 | 0 | 0 | 1
7 | 0 | 1 | 1 | 1 | 1 | 0 | 1 | 0
8 | 1 | 0 | 0 | 0 | 1 | 0 | 1 | 1
9 | 1 | 0 | 0 | 1 | 1 | 1 | 0 | 0
10-15 | All other inputs |  |  |  | X | X | X | X
Step 1 (Specification)
4-bit BCD input (A,B,C,D)
4-bit E-3 output (W,X,Y,Z)
Step 2 (Formulation)
Obtain Truth table

## Slide 13: Example 2 (cont.)
 | BCD Input |  |  |  | Excess 3 Output |  |  | 
Decimal | A | B | C | D | W | X | Y | Z
0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1
1 | 0 | 0 | 0 | 1 | 0 | 1 | 0 | 0
2 | 0 | 0 | 1 | 0 | 0 | 1 | 0 | 1
3 | 0 | 0 | 1 | 1 | 0 | 1 | 1 | 0
4 | 0 | 1 | 0 | 0 | 0 | 1 | 1 | 1
5 | 0 | 1 | 0 | 1 | 1 | 0 | 0 | 0
6 | 0 | 1 | 1 | 0 | 1 | 0 | 0 | 1
7 | 0 | 1 | 1 | 1 | 1 | 0 | 1 | 0
8 | 1 | 0 | 0 | 0 | 1 | 0 | 1 | 1
9 | 1 | 0 | 0 | 1 | 1 | 1 | 0 | 0
10-15 | All other inputs |  |  |  | x | x | x | x
Step 1 (Specification)
4-bit BCD input (A,B,C,D)
4-bit E-3 output (W,X,Y,Z)
Step 2 (Formulation)
Obtain Truth table

## Slide 14: Example 2 (cont.)
src: online CD
src: Mano’s book
Step 3 (Optimization)

## Slide 15: Example 3
A seven-segment display is digital readout found in electronic devices like clocks, TVs, etc.
  Made of seven light-emitting diodes (LED) segments; each segment is controlled separately.
A BCD-to-Seven-Segment decoder is a combinational circuit
  Accepts a decimal digit in BCD (input)
  Generates appropriate outputs for the segments to display the input decimal digit (output)
Question (BCD-to-Seven-Segment Decoder)
src: Mano’s book

## Slide 16: Example 3 (cont.)
Step 1 (Specification):
  4 inputs (A, B, C, D)
  7 outputs (a, b, c, d, e, f, g)
BCD-to-Seven-Segment
Decoder
A
B
C
D
a b c d e f g

## Slide 17: Example 3 (cont.)
 | BCD Input |  |  |  | 7 Segment Decoder |  |  |  |  |  | 
Decimal | A | B | C | D | a | b | c | d | e | f | g
0 | 0 | 0 | 0 | 0 | 1 | 1 | 1 | 1 | 1 | 1 | 0
1 | 0 | 0 | 0 | 1 | 0 | 1 | 1 | 0 | 0 | 0 | 0
2 | 0 | 0 | 1 | 0 | 1 | 1 | 0 | 1 | 1 | 0 | 1
3 | 0 | 0 | 1 | 1 | 1 | 1 | 1 | 1 | 0 | 0 | 1
4 | 0 | 1 | 0 | 0 | 0 | 1 | 1 | 0 | 0 | 1 | 1
5 | 0 | 1 | 0 | 1 | 1 | 0 | 1 | 1 | 0 | 1 | 1
6 | 0 | 1 | 1 | 0 | 1 | 0 | 1 | 1 | 1 | 1 | 1
7 | 0 | 1 | 1 | 1 | 1 | 1 | 1 | 0 | 0 | 0 | 0
8 | 1 | 0 | 0 | 0 | 1 | 1 | 1 | 1 | 1 | 1 | 1
9 | 1 | 0 | 0 | 1 | 1 | 1 | 1 | 0 | 0 | 1 | 1
10-15 | All Other Inputs |  |  |  | 0 | 0 | 0 | 0 | 0 | 0 | 0
Step 2 (Formulation)
Invalid BCD codes
=
No Light

## Slide 18: Example 3 (cont.)
a
b
c
d
e
f
g
Step 3 (Optimization)

## Slide 19: Example 3 (cont.)
a = A’C + A’BD + AB’C’ + B’C’D’
b = A’B’ + A’C’D’ + A’CD + B’C’
c = A’B + B’C’ + A’C’ + A’D
d = A’CD’ + A’B’C + B’C’D’+AB’C’+A’BC’D
e = A’CD’ + B’C’D’
f = A’BC’ + A’C’D’ + A’BD’ + AB’C’
g = A’CD’ + A’B’C + A’BC’ + AB’C’
Exercise: Draw the circuit
Step 3 (Optimization) (cont.)

## Slide 20: Conclusion
There are two types of logic circuits
  Combinational
  Sequential
Design Procedure
  Specification *
  Formulation *
  Optimization *
  Technology Mapping
  Verification
Examples