## Slide 1: COE 202: Digital Logic Design Combinational Circuits Part 4
Courtesy of Dr. Ahmad Almulhem

## Slide 2: Objectives
Magnitude comparator
  Design of 4-bit magnitude comparator
Design Examples using MSI components
  Adding Three 4-bit numbers
  Building 4-to-16 Decoders with 2-to-4 Decoders
  Getting the larger of 2 numbers (Maximum)
  Excess-3 Code Converter

## Slide 3: Magnitude Comparator
Definition: A magnitude comparator is a combinational circuit that compares two numbers A & B to determine whether:
  A > B, or
  A = B, or
  A < B
Inputs
  First n-bit number A
  Second n-bit number B
Outputs
  3 output signals (GT, EQ, LT), where:
    GT = 1 IFF A > B
    EQ = 1 IFF A = B
    LT = 1 IFF A < B
Note: Exactly One of these 3 outputs equals 1, while the other 2 outputs are 0`s
n-bit input
n-bit input
GT
EQ
LT
n-bit magnitude
comparator
A
B

## Slide 4: Example 1: Magnitude Comparator (4-bit)
Problem: Design a magnitude comparator that compares 2 4-bit numbers A and B and determines whether:
  A > B, or
  A = B, or
  A < B
4-bit input
4-bit input
GT
EQ
LE
4-bit magnitude
comparator
A
B

## Slide 5: Example 1: Magnitude Comparator (4-bit)
Solution:
Inputs: 8-bits (A ⇒ 4-bits , B ⇒ 4-bits)
  A and B are two 4-bit numbers
Let A = A3A2A1A0 , and
Let B = B3B2B1B0
Inputs have 28 (256) possible combinations (size of truth table and K-map?)
Not easy to design using conventional techniques
4-bit input
4-bit input
GT
EQ
LE
4-bit magnitude
comparator
A
B
The circuit possesses certain amount of regularity
⇒ can be designed algorithmically.

## Slide 6: Example 1: Magnitude Comparator (4-bit)
Designing EQ:
Define Xi = Ai xnor Bi = Ai Bi + Ai’ Bi’
   Xi = 1 IFF Ai = Bi ∀ i =0, 1, 2 and 3
   Xi = 0 IFF Ai ≠ Bi
Therefore the condition for A = B or EQ=1 IFF
  A3= B3 → (X3 = 1), and
  A2= B2 → (X2 = 1), and
  A1= B1 → (X1 = 1), and
  A0= B0 → (X0 = 1).
Thus, EQ=1 IFF X3 X2 X1 X0 = 1. In other words,
EQ = X3 X2 X1 X0

## Slide 7: Example 1: Magnitude Comparator (4-bit)
Designing GT and LT:
GT = 1 if A > B:
If A3 > B3  A3 = 1 and B3 = 0
If A3 = B3 and A2 > B2
If A3 = B3 and A2 = B2 and A1 > A1
If A3 = B3 and A2 = B2 and A1 = B1 and A0 > B0
Therefore,
  GT = A3B3‘ + X3 A2 B2‘ + X3 X2 A1 B1‘ + X3 X2 X1A0 B0‘
  Similarly, LT = A3’B3 + X3 A2‘B2 + X3 X2 A1’B1 + X3 X2 X1A0’ B0

## Slide 8: Example 1: Magnitude Comparator (4-bit)
EQ = X3 X2 X1 X0
GT = A3B3’ + X3A2B2’ + X3X2A1B1’ + X3X2X1A0B0’
LT = B3A3’ + X3B2A2’ + X3X2B1A1’ + X3X2X1B0A0’
4-bit magnitude comparator

## Slide 9: Example 1: Magnitude Comparator (4-bit)
Do you need all three outputs?
Two outputs can tell about the third one
  Example: when A is NOT GREATER THAN B, and A is NOT LESS THAN B THEN A is EQUAL TO B
Therefore, we can save some logic gates:
EQ
4-bit input
4-bit input
GT
EQ
LT
4-bit magnitude
comparator
A
B

## Slide 10: Example 2: Adding three 4-bit numbers
Problem: Add three 4-bit numbers using standard MSI combinational components
Solution:
Let the numbers be X3X2X1X0, Y3Y2Y1Y0, Z3Z2Z1Z0 ,
X3X2X1X0
+ Y3Y2Y1Y0
-------------------
C4 S3S2S1S0
S3S2S1S0
+ Z3Z2Z1Z0
-------------------
D4 F3F2F1F0
Note: C4 and D4 is generated in position 4. They must be added to generate the most significant bits of the result

## Slide 11: Example 2: Adding three 4-bit numbers
Problem: Add three 4-bit numbers using standard MSI combinational components
Solution:
Let the numbers be X3X2X1X0, Y3Y2Y1Y0, Z3Z2Z1Z0 ,
X3X2X1X0
+ Y3Y2Y1Y0
-------------------
C4 S3S2S1S0
S3S2S1S0
+ Z3Z2Z1Z0
-------------------
D4 F3F2F1F0
Note: C4 and D4 is generated in position 4. They must be added to generate the most significant bits of the result

## Slide 12: Example 2: Adding three 4-bit numbers

## Slide 13: Example 3: 4-to-16 Decoder
Problem: Design a 4x16 Decoder using 2x4 Decoders
Solution:
Each group combination holds a unique value for A3A2
- One Decoder can be therefore used with inputs: A3A2
- Four more decoders are needed for representing each individual color combination
A3 | A2 | A1 | A0 | Output
0 | 0 | 0 | 0 | D0
0 | 0 | 0 | 1 | D1
0 | 0 | 1 | 0 | D2
0 | 0 | 1 | 1 | D3
0 | 1 | 0 | 0 | D4
0 | 1 | 0 | 1 | D5
0 | 1 | 1 | 0 | D6
0 | 1 | 1 | 1 | D7
1 | 0 | 0 | 0 | D8
1 | 0 | 0 | 1 | D9
1 | 0 | 1 | 0 | D10
1 | 0 | 1 | 1 | D11
1 | 1 | 0 | 0 | D12
1 | 1 | 0 | 1 | D13
1 | 1 | 1 | 0 | D14
1 | 1 | 1 | 1 | D15
A3A2 = 00
A3A2 = 01
A3A2 = 10
A3A2 = 11

## Slide 14: Example 3: 4-to-16 Decoder
2x4 Decoder
D0 D1 D2 D3
A0 A1
2x4 Decoder
D4 D5 D6 D7
A0 A1
2x4 Decoder
D8 D9 D10 D11
A0 A1
2x4 Decoder
D12 D13 D14 D15
A0 A1
2x4 Decoder
A2 A3

## Slide 15: Example 4: The larger of 2 numbers
Problem: Given two 4-bit unsigned numbers, design a circuit such that the output is the larger of the two numbers
Solution: We will use a magnitude comparator and a Quad 2x1 MUX. How?

## Slide 16: Example 4: The larger of 2 numbers
A0
A1
A2
A3
B0
B1
B2
B3
GT
LT
EQ
4-bit
Magnitude
Comparator
S0
A0
A1
A2
A3
B0
B1
B2
B3
Y0
Y1
Y2
Y3
QUAD
2X1
MUX
A>B
A<B
A=B
For So=1, A is selected,
For So=0, B is selected

## Slide 17: Example 5: Excess-3 Code Converter
Problem: Design an excess-3 code converter that takes as input a BCD number, and generates an excess-3 output.
Solution: Use decoders and encoders
W | X | Y | Z | A | B | C | D
0 | 0 | 0 | 0 | 0 | 0 | 1 | 1
0 | 0 | 0 | 1 | 0 | 1 | 0 | 0
0 | 0 | 1 | 0 | 0 | 1 | 0 | 1
0 | 0 | 1 | 1 | 0 | 1 | 1 | 0
0 | 1 | 0 | 0 | 0 | 1 | 1 | 1
0 | 1 | 0 | 1 | 1 | 0 | 0 | 0
0 | 1 | 1 | 0 | 1 | 0 | 0 | 1
0 | 1 | 1 | 1 | 1 | 0 | 1 | 0
1 | 0 | 0 | 0 | 1 | 0 | 1 | 1
1 | 0 | 0 | 1 | 1 | 1 | 0 | 0

## Slide 18: Example 5: Excess-3 Code Converter
16-to-4 line Encoder
I0
I1
I2
I3
I4
I5
I6
I7
I8
I9
I10
I11
I12
I13
I14
I15
D0
D1
D2
D3
4-to-16 line Decoder
O0
O1
O2
O3
O4
O5
O6
O7
O8
O9
O10
O11
O12
O13
O14
O15
D0
D1
D2
D3
Z
Y
X
W
?
?
?
?
What will be the output?

## Slide 19: Example 5: Excess-3 Code Converter
A decoder can be used with the inputs being W,X,Y,Z
  It will be a 4x16 decoder, with only a single output bit equal to 1 for any input combination
An encoder (16x4) will take as input the 16 bit output from the decoder, and will generate the appropriate output in excess-3 format
For this to function correctly, the output from the decoder must be displaced 3 places while being connected to the encoder input
It may be noted that outputs 10,11,12,13,14,15 of the decoder are not used – since we are dealing with BCD

## Slide 20: Summary
Design = Different possibilities
Better designer = more practice
More design examples in the textbook