## Slide 1: COE 202: Digital Logic Design Sequential Circuits Part 1
Courtesy of Dr. Ahmad Almulhem

## Slide 2: Objectives
Sequential Circuits
Storage Elements (Memory)
  Latches
  Flip-Flops

## Slide 3: Combinational vs Sequential
A combinational circuit:
At any time, outputs depends only on inputs
  Changing inputs changes outputs
No regard for previous inputs
  No memory (history)
Time is ignored !
Combinational
Circuits
inputs X
outputs Z

## Slide 4: Combinational vs Sequential
A sequential circuit:
A combinational circuit with feedback through memory
  The stored information at any time defines a state
Outputs depend on current inputs and previous inputs
  Previous inputs are stored as binary information into memory
Next state depends on current inputs and present state
Combinational
Circuits
inputs X
outputs Z
Memory
next state
present state

## Slide 5: Examples of sequential systems
Traffic light
Vending machine
ATM
What is common between these systems?

## Slide 6: Combinational Adder
4-bit adder (ripple-carry)
  Notice how carry-out propagates
  One adder is active at a time
4 full adders are needed

## Slide 7: Sequential Adder
1-bit memory and two (2) 4-bit memory
Only one 1-bit full-adder needed!
4 clocks to get the output
The 1-bit memory defines the circuit state (0 or 1)

## Slide 8: Types of Sequential Circuits
Two types of sequential circuits:
  Synchronous: The behavior of the circuit depends on the input signal at discrete instances of time (also called clocked)
  Asynchronous: The behavior of the circuit depends on the input signals at any instance of time and the order of the inputs change
    A combinational circuit with feedback

## Slide 9: Synchronous Sequential Circuits
Synchronous circuits employ a synchronizing signal called clock (a periodic train of pulses; 0s and 1s)
A clock determines when computational activities occur
Other signals determine what changes will occur
Combinational
Circuits
inputs X
outputs Z
Flip-Flops
next state
present state
clock

## Slide 10: Synchronous Sequential Circuits
The storage elements (memory) used in clocked sequential circuits are called flip-flops
  Each flip-flop can store one bit of information (0 or 1)
  A circuit may use many flip-flops; together they define the circuit state
Flip-Flops (memory/state) update only with the clock
Combinational
Circuits
inputs X
outputs Z
Flip-Flops
next state
present state
clock

## Slide 11: Storage Elements (Memory)
A storage element can maintain a binary state (0,1) indefinitely, until directed by an input signal to switch state
Main difference between storage elements:
  Number of inputs they have
  How the inputs affect the binary state
Two main types:
  Latches (level-sensitive)
  Flip-Flops (edge-sensitive)
Latches are useful in asynchronous sequential circuits
Flip-Flips are built with latches

## Slide 12: Latches
A latch is binary storage element
Can store a 0 or 1
The most basic memory
Easy to build
  Built with gates (NORs, NANDs, NOT)

## Slide 13: SR Latch
What does this circuit do?

## Slide 14: SR Latch
Two states: Set (Q = 1) and Reset (Q = 0)
When S=R=0, Q remains the same, S=R=1 is not allowed!
Normally, S=R=0 unless the state need to be changed (memory?)
State of the circuit depends not only on the current inputs, but also on the recent history of the inputs

## Slide 15: S’ R’ Latch
How about this circuit?

## Slide 16: S’ R’ Latch
Similar to SR latch (complemented)
Two states: Set (Q = 0) and Reset (Q = 1)
When S=R=1, Q remains the same
S=R=0 is not allowed!

## Slide 17: SR Latch with Clock
An SR Latch can be modified to control when it changes
An additional input signal Clock (C)
When C=0, the S and R inputs have no effect on the latch
When C=1, the inputs affect the state of the latch and possibly the output

## Slide 18: SR Latch with Clock (cont.)
How can we eliminate the undefined state?

## Slide 19: D Latch
Ensure S and R are never equal to 1 at the same time
Add inverter
Only one input (D)
  D connects to S
  D’ connects to R
D stands for data
Output follows the input when C = 1
  Transparent
When C = 0, Q remains the same
R
S

## Slide 20: Graphic Symbols for Latches
A latch is designated by a rectangular block with inputs on the left and outputs on the right
One output designates the normal output, the other (with the bubble) designates the complement
For S’R’ (SR built with NANDs), bubbles added to the input
clk

## Slide 21: Problem with Latches
What happens if Clock=1? What will be the value of Q when Clock goes to 0?
Problem: A latch is transparent; state keeps changing as long as the clock remains active
Due to this uncertainty, latches can not be reliably used as storage elements.
Example
Combinational
Circuits
inputs X
outputs Z
Latches?
clock
C
D
Q
Q
Q
Clock

## Slide 22: Flip Flops
A flip-flop is a one bit memory similar to latches
Solves the issue of latch transparency
Latches are level sensitive memory element
  Active when the clock = 1 (whole duration)
Flip-Flops are edge-triggered or edge-sensitive memory elements
  Active only at transitions; i.e. either from 0  1 or 1  0
positive (rising) edge
negative (falling) edge
level

## Slide 23: Flip Flops
A flip flop can be built using two latches in a master-slave configuration
A master latch receives external inputs
A slave latch receives inputs from the master latch
Depending on the clock signal, only one latch is active at any given time
  If clk=1, the master latch is enabled and the inputs are latched
  If clk=0, the master is disabled and the slave is activated to generate the outputs
clk
clk

## Slide 24: Flip Flops
Important Timing Considerations:
Delay of logic gates inside the flip-flop
Setup Time (Ts): The minimum time during which D input must be maintained before the clock transition occurs.
Hold Time (Th): The minimum time during which D input must not be changed after the clock transition occurs.
clk
clk

## Slide 25: SR Flip Flop
Built using two latches (Master and Slave)
  C = 1, master is active
  C = 0, slave is active
Q is sampled at the falling edge
Data is entered on the rising edge of the clock pulse, but the output does not reflect the change until the falling edge of the clock pulse.

## Slide 26: Graphic Symbols for Flip Flops
A Flip Flop is designated by a rectangular block with inputs on the left and outputs on the right (similar to latches)
The clock is designated with an arrowhead
A bubble designates a negative-edge triggered flip flops

## Slide 27: Other Flip Flops
How does it work?
Hint: D = ?
JK Flip Flop

## Slide 28: Other Flip Flops
D = J Q’ + K’ Q
J sets the flip flop (1)
K reset the flip flop (0)
When J = K = 1, the output is complemented
JK Flip Flop

## Slide 29: Other Flip Flops
D = J Q’ + K’ Q
J sets the flip flop (1)
K reset the flip flop (0)
When J = K = 1, the output is complemented
JK Flip Flop
JK Flip Flop built with SR latches

## Slide 30: Other Flip Flops (cont.)
T (toggle) flip flop is a complementing flip flop
Built with a JK or D flip flop (as shown above)
T = 0, no change,
T = 1, complement (toggle)
For D-FF implementation, D = T  Q
T Flip Flop

## Slide 31: Characteristic Tables
A characteristic table defines the operation of a flip flop in a tabular form
Next state is defined in terms of the current state and the inputs
  Q(t) refers to current state (before the clock arrives)
  Q(t+1) refers to next state (after the clock arrives)
Similar to the truth table in combinational circuits

## Slide 32: Characteristic Equations
A characteristic equation defines the operation of a flip flop in an algebraic form
For D-FF
  Q(t+1) = D
For JK-FF
  Q(t+1) = J Q’ + K’ Q
For T-FF
  Q(t+1) = T  Q

## Slide 33: Direct Inputs
Some flip-flops have asynchronous inputs to set/reset their states independently of the clock.
Preset or direct set, sets the flip-flop to 1
Clear or direct reset, set the flip-flop to 0
When power is turned on, a flip-flop state is unknown; Direct inputs are useful to put in a known state
Figure shows a positive-edge D-FF with active-low asynchronous reset.
1
1
1

## Slide 34: Flip Flops Sheet (Mano’s Textbook)

## Slide 35: Summary
In a sequential circuit, outputs depend on current inputs and previous inputs
  Previous inputs are stored as binary information into memory
  The stored information at any time defines a state
  Similarly, next state depends on current inputs and present state
Two types of sequential circuits: Synchronous and Asynchronous
Two types of Memory elements: Latches and Flip-Flops.
Flip-flops are built with latches
A flip-flop is described using characteristic table/equation
Flips-flops can have direct asynchronous inputs