COE 202 / Term 071/ Sec. 02

Fundamentals of Computer Engineering

Quiz #03 Solution

F = ∑(0,2,10,13,15)

Prime Implicants: A'B'D' , CD' , ABD , ABC

Essential Prime Implicants: ABD , A'B'D' , CD'

F = ABD + A'B'D' + CD'