## Slide 1: Introduction
COE 301
Computer Organization
Dr. Muhamed Mudawar
Computer Engineering Department
King Fahd University of Petroleum and Minerals

## Slide 2: Presentation Outline
Welcome to COE 301
Assembly-, Machine-, and High-Level Languages
Classes of Computers
Programmer's View of a Computer System

## Slide 3: Welcome to COE 301
Instructor: Dr. Muhamed F. Mudawar
Office: Building 22, Room 410-2
Office Phone: 4642
Schedule and Office Hours:
  http://faculty.kfupm.edu.sa/coe/mudawar/schedule/
Course Web Page:
  http://faculty.kfupm.edu.sa/coe/mudawar/coe301/
Email:
  mudawar@kfupm.edu.sa

## Slide 4: Which Textbook will be Used?
Computer Organization & Design:
The Hardware/Software Interface
  Fifth Edition, 2013
  David Patterson and John Hennessy
  Morgan Kaufmann
Read the textbook in addition to slides

## Slide 5: Grading Policy
Quizzes 10%
MIPS Programming 10%
Lab Work 15%
CPU Design Project 15%
Midterm Exam 25%
Final Exam 25%
No makeup will be given for missing exam or quiz

## Slide 6: Software Tools
MIPS Simulators
  MARS: MIPS Assembly and Runtime Simulator
    Runs MIPS-32 assembly language programs
    Website: http://courses.missouristate.edu/KenVollmar/MARS/
  SPIM
    Also Runs MIPS-32 assembly language programs
    Website: http://www.cs.wisc.edu/~larus/spim.html
CPU Design and Simulation Tool
  Logisim
    Educational tool for designing and simulating CPUs
    Website: http://ozark.hendrix.edu/~burch/logisim/

## Slide 7: Course Learning Outcomes
Towards the end of this course, you should be able to …
  Describe the instruction set architecture of a processor
  Analyze, write, and test assembly language programs
  Describe organization/operation of integer & floating-point units
  Design the datapath and control of a single-cycle CPU
  Design the datapath/control of a pipelined CPU & handle hazards
  Describe the organization/operation of memory and caches
  Analyze the performance of processors and caches
Required Background
  Ability to program confidently in Java or C
  Ability to design a combinational and sequential circuit

## Slide 8: Next . . .
Welcome to COE 301
Assembly-, Machine-, and High-Level Languages
Classes of Computers
Programmer's View of a Computer System

## Slide 9: Some Important Questions to Ask
What is Assembly Language?
What is Machine Language?
How is Assembly related to a high-level language?
Why Learn Assembly Language?
What is an Assembler, Linker, and Debugger?

## Slide 10: A Hierarchy of Languages
Application Programs
High-Level Languages
Assembly Language
Machine Language
Hardware
High-Level Language
Low-Level Language
Machine independent
Machine specific

## Slide 11: Assembly and Machine Language
Machine language
  Native to a processor: executed directly by hardware
  Instructions consist of binary code: 1s and 0s
Assembly language
  Slightly higher-level language
  Readability of instructions is better than machine language
  One-to-one correspondence with machine language instructions
Assemblers translate assembly to machine code
Compilers translate high-level programs to machine code
  Either directly, or
  Indirectly via an assembler

## Slide 12: Compiler and Assembler

## Slide 13: Translating Languages
MIPS Assembly Language:
sll $2,$5, 2
add $2,$4,$2
lw $15,0($2)
lw $16,4($2)
sw $16,0($2)
sw $15,4($2)
jr $31
Compiler
Program (C Language):
swap(int v[], int k) {
int temp;
temp = v[k];
v[k] = v[k+1];
v[k+1] = temp;
}
A statement in a high-level language is translated typically into several machine-level instructions
MIPS Machine Language:
00051080
00821020
8C620000
8CF20004
ACF20000
AC620004
03E00008
Assembler

## Slide 14: Advantages of High-Level Languages
Program development is faster
  High-level statements: fewer instructions to code
Program maintenance is easier
  For the same above reasons
Programs are portable
  Contain few machine-dependent details
    Can be used with little or no modifications on different machines
  Compiler translates to the target machine language
  However, Assembly language programs are not portable

## Slide 15: Why Learn Assembly Language?
Many reasons:
  Accessibility to system hardware
  Space and time efficiency
  Writing a compiler for a high-level language
Accessibility to system hardware
  Assembly Language is useful for implementing system software
  Also useful for small embedded system applications
Programming in Assembly Language is harder
  Requires deep understanding of the processor architecture
  However, it is very rewarding to system software designers
  Adds a new perspective on how programs run on real processors

## Slide 16: Assembly Language Programming Tools
Editor
  Allows you to create and edit assembly language source files
Assembler
  Converts assembly language programs into object files
  Object files contain the machine instructions
Linker
  Combines object files created by the assembler with link libraries
  Produces a single executable program
Debugger
  Allows you to trace the execution of a program
  Allows you to view machine instructions, memory, and registers

## Slide 17: Assemble and Link Process
Source
File
Source
File
Source
File
Assembler
Object
File
Assembler
Object
File
Assembler
Object
File
Linker
Executable
File
Link
Libraries
A program may consist of multiple source files
Assembler translates each source file into an object file
Linker links all object files together and with link libraries
The result executable file can run directly on the processor

## Slide 18: MARS Assembler and Simulator Tool

## Slide 19: MARS Assembler and Simulator Tool
Simulates the execution of a MIPS program
  No direct execution on the underlying Intel processor
Editor with color-coded assembly syntax
  Allows you to create and edit assembly language source files
Assembler
  Converts MIPS assembly language programs into object files
Console and file input/output using system calls
Debugger
  Allows you to trace the execution of a program and set breakpoints
  Allows you to view machine instructions, edit registers and memory
Easy to use and learn assembly language programming

## Slide 20: Next . . .
Welcome to COE 301
Assembly-, Machine-, and High-Level Languages
Classes of Computers
Programmer's View of a Computer System

## Slide 21: Classes of Computers
Personal computers
  General purpose, variety of software, subject to cost/performance
Server computers
  Network based, high capacity, performance, and reliability
  Range from small servers to building sized
Supercomputers
  High-end scientific and engineering calculations
  Highest capability but only a small fraction of the computer market
Embedded computers
  Hidden as components of systems
  Stringent power/performance/cost constraints

## Slide 22: Classes of Computers (cont'd)
Personal Mobile Device (PMD)
  Battery operated
  Connects to the Internet
  Low price: hundreds of dollars
  Smart phones, tablets, electronic glasses
Cloud Computing
  Warehouse Scale Computers (WSC)
  Software, Platform, and Infrastructure as a Service
  However, security concerns of storing "sensitive data" in "the cloud"
  Examples: Amazon and Google

## Slide 23: Components of a Computer System
Processor
  Datapath and Control
Memory & Storage
  Main Memory
  Disk Storage
Input / Output devices
  User-interface devices
  Network adapters
    For communicating with other computers
Bus: Interconnects processor to memory and I/O
Essentially the same components for all kinds of computers
Computer
Memory
I/O Devices
Input
Output
BUS
Control
Datapath
Processor
Disk
Network

## Slide 24: Fetch - Execute Cycle
Fetch instruction
Compute address of next instruction
Generate control signals for instruction
Read operands from registers
Compute result value
Writeback result in a register
Instruction Decode
Instruction Fetch
Execute
Writeback Result
Infinite Cycle implemented in Hardware
Memory Access
Read or write memory

## Slide 25: Clock
Operation of digital hardware is governed by a clock
Clock period: duration of a clock cycle
  e.g., 250 ps = 0.25 ns = 0.25 ×10–9 sec
Clock frequency (rate) = 1 / clock period
  e.g., 1/ 0.25 ×10–9 sec = 4.0×109 Hz = 4.0 GHz
Clock (cycles)
Data transfer and computation
Update state
Clock period

## Slide 26: Memory and Storage Devices
Volatile Memory Devices
  RAM = Random Access Memory
  DRAM = Dynamic RAM
    Dense but must be refreshed (typical choice for main memory)
  SRAM: Static RAM
    Faster but less dense than DRAM (typical choice for cache memory)
Non-Volatile Storage Devices
  Magnetic Disk
  Flash Memory (Solid State Disk)
  Optical Disk (CDROM, DVD)

## Slide 27: Units for Storage and Memory
Size of disk storage
Value = 10n (base 10)
Size of memory
Value = 2n (base 2)
The binary terms are used to avoid the confusion with the commonly used decimal terms. The size of memory is 2n because the memory address is an n-bit binary number.

## Slide 28: Next . . .
Welcome to COE 301
Assembly-, Machine-, and High-Level Languages
Classes of Computers
Programmer's View of a Computer System

## Slide 29: Programmer’s View of a Computer System
Application Programs
High-Level Language
Assembly Language
Operating System
Instruction Set
Architecture
Microarchitecture
Physical Design
Level 0
Level 1
Level 2
Level 3
Level 4
Level 5
Increased level of abstraction
Each level hides the details of the level below it
Software
Hardware
Interface SW & HW

## Slide 30: Programmer's View (cont'd)
Application Programs (Level 5)
  Written in high-level programming languages
  Such as Java, C++, Pascal, Visual Basic . . .
  Programs compile into assembly language level (Level 4)
Assembly Language (Level 4)
  Instruction mnemonics (symbols) are used
  Have one-to-one correspondence to machine language
  Calls functions written at the operating system level (Level 3)
  Programs are translated into machine language (Level 2)
Operating System (Level 3)
  Provides services to level 4 and 5 programs
  Translated to run at the machine instruction level (Level 2)

## Slide 31: Programmer's View (cont'd)
Instruction Set Architecture (Level 2)
  Interface between software and hardware
  Specifies how a processor functions
  Machine instructions, registers, and memory are exposed
  Machine language is executed by Level 1 (microarchitecture)
Microarchitecture (Level 1)
  Controls the execution of machine instructions (Level 2)
  Implemented by digital logic
Physical Design (Level 0)
  Implements the microarchitecture at the transistor-level
  Physical layout of circuits on a chip