## Slide 1: Serial versus Pipelined Execution
COE 301 / ICS 233
Computer Organization
Dr. Muhamed Mudawar
College of Computer Sciences and Engineering
King Fahd University of Petroleum and Minerals

## Slide 2: Drawback of Single Cycle Processor
Drawback is the Long cycle time
  All instructions take as much time as the slowest instruction
longest delay
Instruction
Fetch
ALU
Decode
Reg Read
ALU
Reg
Write
Load
Instruction
Fetch
Decode
Reg Read
Compute
Address
Reg
Write
Memory Read
Store
Instruction
Fetch
Decode
Reg Read
Compute
Address
Memory Write
Jump
Instruction
Fetch
Decode &
Update PC
Branch
Instruction
Fetch
Reg Read
Br Target
Compare &
Update PC

## Slide 3: Alternative: Multicycle Implementation
Break instruction execution into five steps
  Instruction fetch
  Instruction decode, register read, target address for jump/branch
  Execution, memory address calculation, or branch outcome
  Memory access or ALU instruction completion
  Load instruction completion
One clock cycle per step (clock cycle is reduced)
  First 2 steps are the same for all instructions
Instruction | # cycles | Instruction | # cycles
ALU & Store | 4 | Branch | 3
Load | 5 | Jump | 2

## Slide 4: Performance Example
Assume the following operation times for components:
  Access time for Instruction and data memories: 200 ps
  Delay in ALU and adders: 180 ps
  Delay in Decode and Register file access (read or write): 150 ps
  Ignore the other delays in PC, mux, extender, and wires
Which of the following would be faster and by how much?
  Single-cycle implementation for all instructions
  Multicycle implementation optimized for every class of instructions
Assume the following instruction mix:
  40% ALU, 20% Loads, 10% stores, 20% branches, & 10% jumps

## Slide 5: Solution
Instruction Class | Instruction Memory | Register Read | ALU Operation | Data Memory | Register Write | Total
ALU | 200 | 150 | 180 |  | 150 | 680 ps
Load | 200 | 150 | 180 | 200 | 150 | 880 ps
Store | 200 | 150 | 180 | 200 |  | 730 ps
Branch | 200 | 150 | 180 |  |  | 530 ps
Jump | 200 | 150 |  |  |  | 350 ps
For fixed single-cycle implementation:
  Clock cycle =
For multi-cycle implementation:
  Clock cycle =
  Average CPI =
Speedup =
0.4×4 + 0.2×5 + 0.1×4+ 0.2×3 + 0.1×2 = 3.8
max (200, 150, 180) = 200 ps (maximum delay at any step)
880 ps determined by longest delay (load instruction)
880 ps / (3.8 × 200 ps) = 880 / 760 = 1.16
Compare and update PC
Decode and update PC

## Slide 6: Pipelining Example
Laundry Example: Three Stages
Wash dirty load of clothes
Dry wet clothes
Fold and put clothes into drawers
Each stage takes 30 minutes to complete
Four loads of clothes to wash, dry, and fold
A
B
C
D

## Slide 7: Sequential Laundry
Sequential laundry takes 6 hours for 4 loads
Intuitively, we can use pipelining to speed up laundry
Time
6 PM
A
30
30
30
7
8
9
10
11
12 AM
30
30
30
B
30
30
30
C
30
30
30
D

## Slide 8: Pipelined Laundry: Start Load ASAP
Pipelined laundry takes 3 hours for 4 loads
Speedup factor is 2 for 4 loads
Time to wash, dry, and fold one load is still the same (90 minutes)
Time
6 PM
A
30
7
8
9 PM
B
30
30
C
30
30
30
D
30
30
30
30
30
30

## Slide 9: Serial Execution versus Pipelining
Consider a task that can be divided into k subtasks
  The k subtasks are executed on k different stages
  Each subtask requires one time unit
  The total execution time of the task is k time units
Pipelining is to overlap the execution
  The k stages work in parallel on k different tasks
  Tasks enter/leave pipeline at the rate of one task per time unit
1
2
k
…
1
2
k
…
1
2
k
…
1
2
k
…
1
2
k
…
1
2
k
…
Without Pipelining
One completion every k time units
With Pipelining
One completion every 1 time unit

## Slide 10: Synchronous Pipeline
Uses clocked registers between stages
Upon arrival of a clock edge …
  All registers hold the results of previous stages simultaneously
The pipeline stages are combinational logic circuits
It is desirable to have balanced stages
  Approximately equal delay in all stages
Clock period is determined by the maximum stage delay
S1
S2
Sk
Register
Register
Register
Register
Input
Clock
Output

## Slide 11: Pipeline Performance
Let ti = time delay in stage Si
Clock cycle t = max(ti) is the maximum stage delay
Clock frequency f = 1/t = 1/max(ti)
A pipeline can process n tasks in k + n – 1 cycles
  k cycles are needed to complete the first task
  n – 1 cycles are needed to complete the remaining n – 1 tasks
Ideal speedup of a k-stage pipeline over serial execution
k + n – 1
Pipelined execution in cycles
Serial execution in cycles
=
=
Sk → k for large n
nk
Sk

## Slide 12: MIPS Processor Pipeline
Five stages, one cycle per stage
IF: Instruction Fetch from instruction memory
ID: Instruction Decode, register read, and J/Br address
EX: Execute operation or calculate load/store address
MEM: Memory access for load and store
WB: Write Back result to register

## Slide 13: Single-Cycle vs Pipelined Performance
Consider a 5-stage instruction execution in which …
  Instruction fetch = ALU operation = Data memory access = 200 ps
  Register read = register write = 150 ps
What is the clock cycle of the single-cycle processor?
What is the clock cycle of the pipelined processor?
What is the speedup factor of pipelined execution?
Solution
Single-Cycle Clock =
200+150+200+200+150 = 900 ps
Reg
ALU
MEM
IF
900 ps
Reg
Reg
ALU
MEM
IF
900 ps
Reg

## Slide 14: Single-Cycle versus Pipelined – cont’d
Pipelined clock cycle =
CPI for pipelined execution =
  One instruction completes each cycle (ignoring pipeline fill)
Speedup of pipelined execution =
  Instruction count and CPI are equal in both cases
Speedup factor is less than 5 (number of pipeline stage)
  Because the pipeline stages are not balanced
900 ps / 200 ps = 4.5
1
max(200, 150) = 200 ps
200
IF
Reg
MEM
ALU
Reg
IF
Reg
MEM
Reg
ALU
IF
Reg
MEM
ALU
Reg
200
200
200
200
200
200

## Slide 15: Pipeline Performance Summary
Pipelining doesn’t improve latency of a single instruction
However, it improves throughput of entire workload
  Instructions are initiated and completed at a higher rate
In a k-stage pipeline, k instructions operate in parallel
  Overlapped execution using multiple hardware resources
  Potential speedup = number of pipeline stages k
Pipeline rate is limited by slowest pipeline stage
Unbalanced lengths of pipeline stages reduces speedup
Also, time to fill and drain pipeline reduces speedup