# University Diploma Program

# Electrical Engineering Technology

Lab Instructor: Ajmal Khan, Lecturer EE Dept.

##### EET 027, Experiment # 5

# Thermocouple Voltage Measurement

Objectives:

To examine the thermocouple voltage and find corresponding temperature under the following conditions:

- To measure voltage of thermocouple without considering the intermediate thermocouple effect of measurement setup.

- To measure voltage of thermocouple with ice-point reference junction and fine corresponding voltage using the thermocouple table.

- To measure voltage of thermocouple using ambient reference block and calculate the corrected voltage and then find the corresponding temperature.

Apparatus:

J type thermocouples

4-1/2 digit DVM.

Temperature Indicator.

Ice point water

Boiling water

Theory:

Theory as per attached sheets.

Procedure:

- Setup the experiment as Figure 4 in theory sheets and measure voltage V.

V = _____________________

T = _____________________

- Setup the experiment as Figure 6 and measure voltage V and calculate V1. Find temperature corresponding to V1 from table.

where,

V = ____________________

V1 = ___________________

T = ____________________

T1 = ___________________

- Setup the experiment according to figure 12.

  - Note reference temperature, which will be ambient temperature from temperature indicator.

  - Measure V and find V1.

  - Find the temperature from table corresponding to V.

TREF = __________________

V = ______________________

V1 = _____________________

T = ______________________

T1 = _____________________

- Compare voltage from setup 1, 2 and 3.

Conclusions:

Explain:

Which set up gives the correct temperature?

Which set up gives maximum error?