KING FAHD UNIVERSITY OF PETROLEUM AND MINERALS

University Diploma Programs

EET 022: Digital Electronics Circuits

Preparatory Classroom Building, Building # 7, Room # 116.

QUIZ  #  5

NAME: _________________________________		        ID: ___________________

=================================================================

Circle the most accurate answer for each of the following questions

Q.1.	The basic mechanism for storing a data bit in an E2CMOS cell is:

(a)   control gate,

(b)   floating drain,

(c)   floating gale,

(d)   cell current.

Q.2.	When the frequency of the input signal to a CMOS gate is increased, the average power dissipation:

(a)   decreases,

(b)   increases,

(c)   does not change,

(d)   decreases exponentially.

Q.3.	Which of the following is not a TTL circuit? :

(a)   74F00,

(b)   74AS00,

(c)   74HC00,

(d)   74ALS00.

Q.4.	An open TTL NOR gate input:

(a)   acts as a LOW,

(b)   acts as a HIGH,

(c)   should be grounded,

(d)   should be connected to Vcc through a resistor,

(e)   answers (b) and (c),

(f)    answers (a) and (c).

Q.5.	ECL cannot be used in:

(a)   high-noise environments,

(b)   damp environments,

(c)   high-frequency applications.

Sunday, 12 January 2003.