# University Diploma Programs

# Electronic Equipment Maintenance

EET-029: Introduction to Communications

## Quiz # 4

Name: ________________________________	ID #: ___________

- Indicate the false statement regarding the Armstrong modulation system:

  - The system is basically phase, not frequency, modulation

  - AFC is not needed, as a crystal oscillator is used

  - Frequency multiplication must be used

  - Equalization is unnecessary

- An FM signal with a modulation index mf passed through a frequency tripler. The wave in the output of the tripler will have a modulation index of:

  - mf / 3

  - mf

  - 3 mf

  - 9 mf

- Since noise phase-modulates the FM wave, as the noise sideband frequency approaches the carrier frequency, the noise amplitude:

  - Remains constant

  - Is decreased

  - Is increased

  - In equalized

- One of the following is an indirect way of generating FM. This is the:

  - Reactance FET modulator

  - Varactor diode modulator

  - Armstrong modulator

  - Reactance bipolar transistor modulator

- In an FM stereo multiplex transmission, the:

  - Sum signal modulates the 19 kHz subcarrier

  - Difference signal modulates the 19 kHz subcarrier

  - Difference signal modulates the 38 kHz subcarrier

  - Difference signal modulates the 67 kHz subcarrier

- Indicate which of the following statements about the advantage of the phase discriminator over the slope detector is false:

  - Much easier alignment

  - Better linearity

  - Greater limiting

  - Fewer tuned circuits

- Show which of the following statements about the amplitude limiter is untrue:

  - The circuit is always biased in class C, by virtue of the leak-type bias

  - When the input increases past the threshold of limiting, the gain decreases to keep the output constant

  - The output must be tuned

  - Leak-type bias must be used.

- A pre-emphasis circuit provides extra noise immunity by:

  - Boosting the bass frequencies

  - Amplifying the higher audio frequencies

  - Preamplifying the whole audio band

  - Converting the phase modulation to FM.