EE 420 HW#7

1. A multimode optical fiber has an optimum near parabolic graded index profile. The source used is an LED having a spectral width of . The material dispersion parameter is . The pulse spread due to waveguide dispersion in this fiber is much smaller than the pulse spread due to material dispersion. The optical fiber has a numerical aperture of and a core axis refractive index of .

a) Estimate the total pulse spread per kilometer within the fiber.

b) Estimate the bandwidth-length product of the fiber.

2. Repeat problem 1) for a multimode step index fiber.

3. Repeat problem 1) for a single mode step index optical fiber using a LD having a spectral width of .

4. An , multimode optical fiber link with an optimum near parabolic refractive index profile exhibits a modal pulse spread of . The relative refractive index difference of the fiber is , estimate the core – axis refractive index.

5. A multimode step index optical fiber has a numerical aperture of  and a core refractive index of . Estimate the bandwidth of  length of the fiber, assuming that the bandwidth is limited by modal distortion when:

a) The fiber has a characteristic length of .

b) The fiber is perfect.