King Fahd University of Petroleum & Minerals

Electrical Engineering Department

# EE-390

| Prob.1 | Prob.2 | Prob.3 | Total |
| --- | --- | --- | --- |

1.  Write a program that will store “4#6SUUDI,A” into memory locations

starting from DS:001AH  and then convert only the capital-letters into small-letters and re-store them in original memory location.

Note that ASCII code of: 0 is 30, a is 61, and A is 41.

TITLE "Question 1"

.MODEL Small

.STACK   32H

.DATA

_________________________________________________

.CODE

MOV AX, @DATA

MOV DS,  AX

_____________________________________________________________

_____________________________________________________________

_____________________________________________________________

_____________________________________________________________

_____________________________________________________________

_____________________________________________________________

_____________________________________________________________

____________________________________________________________

_____________________________________________________________

_____________________________________________________________

_____________________________________________________________

_____________________________________________________________

_____________________________________________________________

_____________________________________________________________

2. After the following instructions are executed what will be the values of CX, DX, DI, VAL1, VAL2. Show the steps beside the instructions and put the answers in HEX

.DATA

Org 0009H

VAL1 DW 046AH

VAL2 DW 3FD9H

.CODE

LEA DI, VAL1

MOV CX, [DI]

ADD DI, 2H

MOV DX, [DI]

XCHG DX, VAL1

AND DX, 0FF00H

AGAIN:DEC WORD PTR [DI]

DEC DX

CMP DX, 03FEH

LOOPZ AGAIN

DEC WORD PTR [0009H]

Answer:

CX = (			H)

DX = (			H)

DI = (			H)

VAL2 = (		H)

VAL1 = (                         H)

3.  If AX=100H, CX=202H, DX=0270H, DS=1000H, ES=5000H,  SS=8000H, SI=300H, DI=506H, SP=10H, BP=200H,  and the given memory locations store  the following contents, 11506H ( 81H , 10506 H (  07H , 51506 H ( 45H ,

81506 H (  13H , 81350 H (  37H , 81530 H (  43H , 80406 H ( 9AH ,

81406 H ( 6AH ,   compute the required values of the registers after executing each line of the program. (assume all other memory locations ( 00H)

XCHG  AX,BP  	;

SAR      AX,CL     	;	                     AX =__________

XOR     AL,[1506H]	;	                     AX =__________

MUL	 Byte PTR [BP][SI]+6H    ;	               AX =__________

PUSH  AX	;	              SP =__________

Addressing Mode used in line 4 = ____________________

# Text boxes

One

Program

MOV AX, 4C00H

INT 21H

END