King Fahd University of Petroleum & Minerals

Electrical Engineering Department

# EE-390

| Prob.1 | Prob.2 | Prob.3 | Total |
| --- | --- | --- | --- |

Answer all four questions. All questions carry equal marks.

Name : Section : I.D.

1(a). For the given values shown in the table {assume the memory contents of the

addresses in-between the given addresses (in the table) contains zero values} ;

| Register contents | Memory addresses (PA) | Memory contents (Hex) |
| --- | --- | --- |
| AX=000AH, | 102AC : 01 |
| DX=E2F3H, | 102AD : 04 |
| BP=0206 H | 111AD : 05 |
| DS=1001H, | 112AC : 03 |
| SS=1101H, | 112AD : 02 |

MOV  BX, Word ptr[BP+96H]

IMUL BH

STC

RCR   DX,01

AX =___________H;             DX =___________H;           CF =_____ (‘1’or ’0’);

Addressing mode used in the 1st line of the program : ____________________

1(b) If SI= 2312H , AX= FF7AH , DS:[SI]= 1078H  and  ES:[SI]= A5C8H  Then execute the follwing program and find the values of the required registers,

LEA CX, Word Ptr [ES:SI]

MOV CH, Byte Ptr [DS:SI+1]

SAHF

CBW

SBB AX, CX

AX =___________H;            CX =___________H;           PF =_____ (‘1’or ’0’);

2. For the given PPI (8255) circuit, write a program using ‘JC’instruction to;

(a) Input a bit-data from the  LSB  of  Port A of 14th   PPI

(b) Also input another bit data from the  MSB  of  Port C of 2nd   PPI.

(b) Compare the inputted bits, and when they are same (or have same logic level),

(c) Output the inputted logic level through all the pins of Port C Lower of 2nd  PPI

Use Isolated input-output interface, Mode 0 operation, 0’s for don’t care address pins and un-used ports programmed as output ports

- In executing the instruction

MOV [A805H], CL

The 8088 processor performs a bus operation. Draw the timing diagram showing: CLK, Logic levels at pins 13-16,25,28,29,32,33,35,36,37 and 38. (Assume minimum-mode, DS=0000H, IF=0, and CX=031AH).

T1	       T2		    T3		  T4

CLK

Pin 13

Pin 14

Pin 15

Pin 16

Pin 25

Pin 28

Pin 29

Pin 32

Pin 33

Pin 35

Pin 36

Pin 37

# Text boxes

_____________________

______________________

______________________

______________________

______________________

______________________

______________________

______________________

______________________

______________________

Line 1:

_____________________

______________________

______________________

______________________

______________________

______________________

______________________

______________________

______________________

______________________

_____________________

______________________

______________________

______________________

______________________

______________________

______________________

______________________

______________________

______________________

Line 11:

Line 21:

Write the Program segment below: ( Don’t include … Title, Mode, Stack ……… end …)