Aquifer: is a geologic formation or group of formations or a part of a formation that exhibits porosity and hydraulic conductivity sufficient to store and transmit  water in significant quantities.

Aquiclude: a geologic formation that stores but does not transmit significant quantities of water under ordinary field conditions (eg clay).

Aquifuge: neither stores nor transmits water (eg granite).

Aquitard: is a geologic formation permeable enough to transmit quantities that are significant in the study of regional groundwater flow, but their permeability is not sufficient to allow the completion of production wells.

# Classification of aquifers

- unconfined aquifer (water-table aquifer, phreatic aquifer): an aquifer in which water table forms the upper boundary of the aquifer.

- Perched aquifer: water accumulating on top of a low-permeability lens

- Confined aquifer (artesian aquifer): contains water at pressures greater than atmospheric pressure, and is sandwiched between two impervious or semi-pervious formations.

Piezometric surface: an imaginary surface passing through all points to which water will rise in wells penetrating a confined aquifer.

- Leaky aquifer : an aquifer that can lose or gain water through either or both formations bounding it from above or below.

Hydrostratigraphic unit: (has been employed recently): a formation, part of a formation, or a group of formations in which there are similar hydrologic characteristics that allow for a grouping into aquifers and associated confining layers