5.1

- Fill in the blanks in the ANOVA table.  You can use bounds on the P-values.

| Two-way ANOVA: y versus A, B |
| --- |
| Source | DF | SS | MS | F | P |
| A | 1 | 0.0002 | 0.0002 | 0.00001 | 0.998 |
| B | 3 | 180.378 | 60.1260 | 3.02907 | 0.093 |
| Interaction | 3 | 8.479 | 2.8263 | 0.14239 | 0.932 |
| Error | 8 | 158.797 | 19.8496 |  |  |
| Total | 15 | 347.653 |  |  |  |

- How many levels were used for factor B?

4 levels.

- How many replicates of the experiment were performed?

2 replicates.

- What conclusions would you draw about this experiment?

Factor B is moderately significant with a P-value of 0.93.  Factor A and the two-factor interaction are not significant.

5.4

Design Expert Output

Response	1	Force

ANOVA for selected factorial model
  Analysis of variance table [Classical sum of squares - Type II]
		Sum of		Mean	F	p-value
	Source	Squares	df	Square	Value	Prob > F

Model		0.28	7	0.040	13.61	0.0007	significant

A-Drill Speed	0.14	1	0.14	49.37	0.0001
	    B-Feed Rate	0.092	3	0.031	10.54	0.0037
	    AB		0.042	3	0.014	4.75	0.0346
	Pure Error	0.023	8	2.925E-003
	Cor Total	0.30	15

The Model F-value of 13.61 implies the model is significant.  There is only
a 0.07% chance that a "Model F-Value" this large could occur due to noise.

Values of "Prob > F" less than 0.0500 indicate model terms are significant.  
In this case A, B, AB are significant model terms.

The factors speed and feed rate, as well as the interaction is important.

The standard analysis of variance treats all design factors as if they were qualitative. In this case, both factors are quantitative, so some further analysis can be performed.  In Section 5.5, we show how response curves and surfaces can be fit to the data from a factorial experiment with at least one quantative factor.  Since both factors in this problem are quantitative, we can fit polynomial effects of both speed and feed rate, exactly as in Example 5.5 in the text.  The Design-Expert output with only the significant terms retained, including the response surface plots, now follows.

# Design Expert Output

Response	1	Force

ANOVA for Response Surface Reduced Quadratic Model
Analysis of variance table [Partial sum of squares - Type III]
	Sum of		Mean	F	p-value
Source	Squares	df	Square	Value	Prob > F

Model		0.22	3	0.073	10.64	0.0011	significant

A-Drill Speed	0.14	1	0.14	21.00	0.0006
	  B-Feed Rate	0.020	1	0.020	2.89	0.1151
	  B2		0.055	1	0.055	8.03	0.0151
	Residual	0.083	12	6.875E-003
	Lack of Fit	0.059	4	0.015	5.05	0.0250	significant
	Pure Error	0.023	8	2.925E-003
	Cor Total	0.30	15

The Model F-value of 10.64 implies the model is significant.  There is only
	a 0.11% chance that a "Model F-Value" this large could occur due to noise.

	Values of "Prob > F" less than 0.0500 indicate model terms are significant.  
	In this case A, B2 are significant model terms.

Std. Dev.	0.083		R-Squared	0.7268
	Mean	2.77		Adj R-Squared	0.6585
	C.V. %	3.00		Pred R-Squared	0.5292

PRESS	0.14		Adeq Precision	8.937

5.6

Response:	Surface Finish

ANOVA for Selected Factorial Model

Analysis of variance table [Partial sum of squares]

Sum of		Mean	F

Source	Squares	DF	Square	Value	Prob > F

Model	1.14	8	0.14	8.00	0.0026	significant

A	0.77	2	0.38	21.59	0.0004

B	0.30	2	0.15	8.47	0.0085

AB	0.069	4	0.017	0.97	0.4700

Residual	0.16	9	0.018

Lack of Fit	0.000	0

Pure Error	0.16	9	0.018

Cor Total	1.30	17

The Model F-value of 8.00 implies the model is significant.  There is only a 0.26% chance that a

"Model F-Value" this large could occur due to noise.

Values of "Prob > F" less than 0.0500 indicate model terms are significant.

In this case A, B are significant model terms.

Values greater than 0.1000 indicate the model terms are not significant.

If there are many insignificant model terms (not counting those required to support hierarchy),

model reduction may improve your model.

- Prepare appropriate residual plots and comment on the model’s adequacy.

The residual plots show no serious deviations from the assumptions.

- Under what conditions would you operate this process?

Set pressure at 215 and Temperature at the high level, 170 degrees C, as this gives the highest yield.

The standard analysis of variance treats all design factors as if they were qualitative. In this case, both factors are quantitative, so some further analysis can be performed.  In Section 5.5, we show how response curves and surfaces can be fit to the data from a factorial experiment with at least one quantative factor.  Since both factors in this problem are quantitative and have three levels, we can fit linear and quadratic effects of both temperature and pressure, exactly as in Example 5.5 in the text.  The Design-Expert output, including the response surface plots, now follows.

# Design Expert Output

Response:	Surface Finish

ANOVA for Selected Factorial Model

Analysis of variance table [Partial sum of squares]

Sum of		Mean	F

Source	Squares	DF	Square	Value	Prob > F

Model	1.13	5	0.23	16.18	< 0.0001	significant

A	0.10	1	0.10	7.22	0.0198

B	0.067	1	0.067	4.83	0.0483

A2	0.67	1	0.67	47.74	< 0.0001

B2	0.23	1	0.23	16.72	0.0015

AB	0.061	1	0.061	4.38	0.0582

Residual	0.17	12	0.014

Lack of Fit	7.639E-003	3	2.546E-003	0.14	0.9314	not significant

### Pure Error		0.16	9	0.018

Cor Total	1.30	17

The Model F-value of 16.18 implies the model is significant.  There is only

a 0.01% chance that a "Model F-Value" this large could occur due to noise.

Values of "Prob > F" less than 0.0500 indicate model terms are significant.

In this case A, B, A2, B2 are significant model terms.

Values greater than 0.1000 indicate the model terms are not significant.

If there are many insignificant model terms (not counting those required to support hierarchy),

model reduction may improve your model.

Std. Dev.	0.12	R-Squared	0.8708

Mean	90.41	Adj R-Squared	0.8170

C.V.	0.13	Pred R-Squared	0.6794

PRESS	0.42	Adeq Precision	11.968

5.18

Design Expert Output

Response	1	Score
	        ANOVA for selected factorial model
Analysis of variance table [Classical sum of squares - Type II]
	Sum of		Mean	F	p-value
Source	Squares	df	Square	Value	Prob > F

Model		1214.83	17	71.46	20.75	< 0.0001	significant

A-Cycle Time	426.33	2	213.17	61.89	< 0.0001
	    B-Operator	279.00	2	139.50	40.50	< 0.0001
	    C-Temperature	44.46	1	44.46	12.91	0.0010
	    AB		349.67	4	87.42	25.38	< 0.0001
	    AC		68.93	2	34.46	10.01	0.0004
	    BC		8.04	2	4.02	1.17	0.3229
	    ABC		38.41	4	9.60	2.79	0.0409
	Pure Error	124.00	36	3.44
	Cor Total	1338.83	53

	The Model F-value of 20.75 implies the model is significant.  There is only
	a 0.01% chance that a "Model F-Value" this large could occur due to noise.

	Values of "Prob > F" less than 0.0500 indicate model terms are significant.  
	In this case A, B, C, AB, AC, ABC are significant model terms.

5.24

(a)	Analyze the data from this experiment (use ( = 0.05).

Design Expert Output

Response:	Crack Growth

ANOVA for Selected Factorial Model

Analysis of variance table [Partial sum of squares]

Sum of		Mean	F

Source	Squares	DF	Square	Value	Prob > F

Model	376.11	8	47.01	234.02	< 0.0001	significant

A	209.89	2	104.95	522.40	< 0.0001

B	64.25	2	32.13	159.92	< 0.0001

AB	101.97	4	25.49	126.89	< 0.0001

Residual	5.42	27	0.20

Lack of Fit	0.000	0

Pure Error	5.42	27	0.20

Cor Total	381.53	35

The Model F-value of 234.02 implies the model is significant.  There is only

a 0.01% chance that a "Model F-Value" this large could occur due to noise.

Values of "Prob > F" less than 0.0500 indicate model terms are significant.

In this case A, B, AB are significant model terms.

Both frequency and environment, as well as their interaction are significant.

- Analyze the residuals.

The residual plots indicate that there may be some problem with inequality of variance.  This is particularly noticable on the plot of residuals versus predicted response and the plot of residuals versus frequency.

- Repeat the analyses from parts (a) and (b) using ln(y) as the response.  Comment on the results.

Design Expert Output

Response:  Crack Growth	Transform:  Natural log		Constant:  0.000

ANOVA for Selected Factorial Model

Analysis of variance table [Partial sum of squares]

Sum of		Mean	F

Source	Squares	DF	Square	Value	Prob > F

Model	13.46	8	1.68	179.57	< 0.0001	significant

A	7.57	2	3.79	404.09	< 0.0001

B	2.36	2	1.18	125.85	< 0.0001

AB	3.53	4	0.88	94.17	< 0.0001

Residual	0.25	27	9.367E-003

Lack of Fit	0.000	0

Pure Error	0.25	27	9.367E-003

Cor Total	13.71	35

The Model F-value of 179.57 implies the model is significant.  There is only

a 0.01% chance that a "Model F-Value" this large could occur due to noise.

Values of "Prob > F" less than 0.0500 indicate model terms are significant.

In this case A, B, AB are significant model terms.

Both frequency and environment, as well as their interaction are significant.  The residual plots based on the transformed data look better.