Machine Design (ME – 308) Term 022

Project # 1: Design of A Hydraulic Press

Given Data:

F Max  	= 	70 Metric Tons

P Fluid 	=	15 ~ 25 Mpa

Increase in the Force due to friction = 15 ~ 25 % of the Total Force

Plunger Material: Grey Cast Iron (or) Low Carbon Cold Drawn Steel

# Step # 1:  Design of the Plunger

Where

D0 = Outside Dia. of the Plunger

Di = Inside Dia. of the Plunger

Tw = Thickness of the walls

Tp = Thickness of the lower

## Plate of the plunger

- Select a Material for the plunger. Preferably, Grey Cast Iron.

- Select the shape of the Plunger, Solid or Hollow.

- Assume a percentage increase in the force due to friction (Say 20 %). So, the total force now will be:

F = F Max * 1.2

- Calculate the Outside Diameter as follows

P Fluid =    where A =

- Calculate the Thickness of the Lower Plate of the Plunger.

For Flat plates the stresses are given as follows: (Ref. Machine Design Hand Book Pg. 5-47)

Where k = 1.24 (Constant), P is the Pressure of the fluid,

And n is the safety Factor (Assume > 3 for Cast iron)

Check for the Deflections in the plate as follows:

- Calculate the Inner Radius of the Plunger

Considering the Plunger to be Thick Walled Cylinder, we can use Equations 3-53 in Machine Design Textbook, Page 132, for calculating the Tangential and Radial Stress at the inner wall since the stresses are Maximum there. In these equations,

Solve the equation for r i.

- Calculate the Thickness of the Walls

Step # 2 Design of The Glands

Thickness of the Gland t G is given by an Empirical Equation, which is:

mm

Thus

O – Rings:

Go to the Machine Design Handbook and see Table 17.1 on Page 17.2

In our case The Inside Diameter (ID) of the O-Ring is D0

So, depending on it select a standard size for the O-ring.

#### Step # 3 Design of Studs

### The Total Load on the Studs   = F

Assume the Number of Studs Ns

Load on each stud (Fs)  = F\Ns

Select a Standard Stud from the Table 8-11 in the Machine Design Textbook and find out the corresponding Proof Strength (Sp) and assume a Factor of Safety (2 ~ 3)

Calculate the Diameter of the stud as follows:

After you calculate the Ds Select a Standard Metric Stud from the table.

##### Step # 4 Design of the Flange

Assume a Pitch Circle Diameter (P.C.D) = D0 + Some Value

Assume a Diameter of the Flange D f   = P.C.D. + Some Value

- Select a Material for the flange, preferably Cast Iron and note down the S ut

- Considering the top of the flange to be a cantilever beam subjected to bending due to the force acting on the studs:

Where

,        And