Summary of Field calculations equations for various symmetric charge distributions

| Charge Distribution | Point in Electric Field | Electric Field Magnitude |
| --- | --- | --- |
| Single Point Charge | Distance r from q | E= 1/(4((0) q/ r2 |
| Charge q on surface of conducting sphere with radius R | Outside sphere (r>R) | E=1/(4((0) q/ r2 |
|  | Inside sphere (r<R) | E=0 |
| Solid insulating sphere with radius R, charge Q distributed uniformly throughout volume | Outside sphere (r>R) | E= 1/(4((0) Q/ r2 |
|  | Inside sphere (r<R) | E= 1/(4((0) Qr/ R3 |
| Infinite wire, charge per unit length ( | Distance r from wire | E= 1/(2((0) (/r |
| Infinite conducting cylinder with radius R and charge per unit length ( | Outside cylinder (r>R) | E= 1/(2((0) (/r |
|  | Inside cylinder (r<R) | E=0 |
| Infinite insulating cylinder with radius R and charge per unit length ( | Outside cylinder (r>R) | E= 1/(2((0) (/r |
|  | Inside cylinder (r<R) | E= 1/(2((0) (r/R2 |
| Infinite sheet of charge with uniform charge per unit area ( | Any point | E= (/2(0 |
| Charged conducting plate with uniform charge per unit area ( | Outside plate | E= (/(0 |
|  | inside plate | E=0 |
| Two oppositely charged plates with surface charge densities (+ and (- | Any point between the plates | E= (/(0, (=2(+=2(- |

Some useful relations:         (= Q/(4(R3/3);  (=Q/L

(=(R2(

(2= (1 (R22/R21)