King Fahd University of Petroleum and Minerals

Department of Physics

Phys 102-Lab Sec.# 76, 80 (042)

Homework # 3 (Due On May 11)

Name:                                               I.D.#                                            Sec.#

Read the handout given in class about error analysis, then work the following problem:

Table 1 shows the dependence of current I passing through a (linear) resistor R on the voltage V across that resistor. When using the voltmeter to take the voltage readings, fluctuations were noticed and the error in each reading was 0.02 V maximum. Uncertainty in current measurements had a maximum value of 1 mA.

| V (volts) | I (mA) |
| --- | --- |
| 20.15 | 13 |
| 25.20 | 18 |
| 30.00 | 22 |
| 35.15 | 25 |
| 40.30 | 29 |
| 45.30 | 32 |
| 50.50 | 38 |
| 55.00 | 39 |
| 60.20 | 41 |
| 70.00 | 51 |
| 75.55 | 61 |

- Is the number of significant figures in the data above consistent with the given uncertainties in the voltage and current? Explain. (5 pts)

- Fill in table 2 below. Round to the correct number of significant figures. (11 pts)

Notice: Leave the units as they are given.

| V (volts) | I (mA) | R(kΩ) |  |
| --- | --- | --- | --- |
| 20.15 | 13 |  |  |
| 25.20 | 18 |  |  |
| 30.00 | 22 |  |  |
| 35.15 | 25 |  |  |
| 40.30 | 29 |  |  |
| 45.30 | 32 |  |  |
| 50.50 | 38 |  |  |
| 55.00 | 39 |  |  |
| 60.20 | 41 |  |  |
| 70.00 | 51 |  |  |
| 75.55 | 61 |  |  |

- The average value of R is given by (5 pts):

- The standard deviation in R is given by (5 pts):

- Estimate the maximum possible error (MPE) from the range of R values (5 pts):

- What do you conclude aboutand MPE? Explain. (5 pts)

# Text boxes

Table 1

Table 2

Round to one significant figure