## Slide 1
Chap. 3.4 Transit-Time Broadening
Prepared by Dist. Prof. Dr. M.A. Gondal for Phys 608 Laser Spectroscopy course in KFUPM (Term 251)

## Slide 2
Prepared by Dist. Prof. Dr. M.A. Gondal for Phys 608 Laser Spectroscopy course in KFUPM (Term 251)

## Slide 3: Slide 1: Transit-Time Broadening — Why It Matters
Prepared by Dist. Prof. Dr. M.A. Gondal for Phys 608 Laser Spectroscopy course in KFUPM (Term 251)
Spectroscopic linewidth determines the achievable resolution and the minimum measurable frequency shift.
When a particle crosses a laser beam quickly, the interaction time 𝑇
can be far shorter than its spontaneous-emission lifetime 𝜏sp.
In this short-interaction regime, the uncertainty principle associates the finite time window 𝑇 with an intrinsic frequency uncertainty: shorter 𝑇 → broader line.

## Slide 4
Transit-time broadening therefore replaces natural (lifetime-limited) broadening as the dominant mechanism whenever
|𝑣|
𝑇 = ≪
Prepared by Dist. Prof. Dr. M.A. Gondal for Phys 608 Laser Spectroscopy course in KFUPM (Term 251)
𝑑
𝜏sp,
where 𝑑 = effective beam diameter [m], |𝑣| = speed of the particle perpendicular to the beam [m s−1].

## Slide 5
Prepared by Dist. Prof. Dr. M.A. Gondal for Phys 608 Laser Spectroscopy course in KFUPM (Term 251)
Understanding, predicting, and mitigating this effect is essential for high-precision laser spectroscopy, frequency standards, and Doppler-free techniques.
---

## Slide 6
Slide 2: Computing The Transit Time 𝑻 — Step-by-Step
Assume a cylindrically symmetric laser beam of diameter 𝑑.
A particle with speed magnitude
|𝑣|
travels approximately
perpendicularly across the beam.
𝑇 =
𝑑
|𝑣|
Units consistency check:
Prepared by Dist. Prof. Dr. M.A. Gondal for Phys 608 Laser Spectroscopy course in KFUPM (Term 251)

## Slide 7
m
m s−1
= s → 𝑇 has units of seconds.
Prepared by Dist. Prof. Dr. M.A. Gondal for Phys 608 Laser Spectroscopy course in KFUPM (Term 251)
Practical importance: for thermally populated molecular beams, |𝑣| is typically hundreds of m s−1; for ion beams, |𝑣| can reach 106–108 m s−1.
Therefore,
even millimetre-scale beams can impose sub-
microsecond interaction times, orders of magnitude below most spontaneous lifetimes (µs – ms).
---

## Slide 8: Slide 3: Numerical Illustration — Example 1 (Molecular
Prepared by Dist. Prof. Dr. M.A. Gondal for Phys 608 Laser Spectroscopy course in KFUPM (Term 251)
Beam)
Given thermal speed
|𝑣|
= 5.0 × 104 cm s−1 = 5.0 × 102 m s−1,
and beam diameter
𝑑
Transit time:
= 0.10 cm
= 1.0 × 10−3 m.

## Slide 9
𝑇 =
1.0 × 10−3 m
5.0 × 102 m s−1
= 2.0 × 10−6 s
Prepared by Dist. Prof. Dr. M.A. Gondal for Phys 608 Laser Spectroscopy course in KFUPM (Term 251)
= 2 𝜇s.
Typical spontaneous lifetime for rovibrational levels:
𝜏sp
∼ 1 ms
= 10−3 s.
Ratio 𝜏sp/𝑇 ≈ 500 → transit-time broadening dominates by two orders of magnitude.

## Slide 10
[IMAGE REQUIRED: Provide a schematic showing a molecular beam crossing a circular laser beam; include labels: diameter 𝑑, velocity vector 𝑣⃗, path length, and shaded interaction region.]
Prepared by Dist. Prof. Dr. M.A. Gondal for Phys 608 Laser Spectroscopy course in KFUPM (Term 251)

## Slide 11: Slide 4: Numerical Illustration — Example 2 (Fast Ion
Beam)
Ion speed
𝑣 = 3.0 × 108 cm s−1 = 3.0 × 106 m s−1.
Beam diameter
𝑑 = 0.10 cm
= 1.0 × 10−3 m.
Transit time:

## Slide 12
𝑇 =
1.0 × 10−3
3.0 × 106
= 3.3 × 10−10 s
= 0.33 ns.
Many atomic excited states possess 𝜏sp ≈ 10−8–10−7 s; here 𝑇 is still shorter, so even atomic lines are transit-time limited in fast-ion experiments.

## Slide 13
[IMAGE REQUIRED: Depict fast ion beam traversing small laser-probe region; include ultra-short interaction timeline vs spontaneous lifetime bar.]
Prepared by Dist. Prof. Dr. M.A. Gondal for Phys 608 Laser Spectroscopy course in KFUPM (Term 251)

## Slide 14: Slide 5: Finite-Duration Oscillator Model — Physical
Analogy
Model an atom or molecule as a classical electric dipole (oscillator) with natural frequency 𝜔0.
The dipole is excited and oscillates during a finite interval 0 ≤ 𝑡 ≤
𝑇.
Mathematically, position coordinate

## Slide 15
𝑥(𝑡)
=
{𝑥0 cos(𝜔0𝑡)
0 ≤ 𝑡 ≤ 𝑇,
𝑡 > 𝑇.
0
The sudden shut-off at 𝑡 = 𝑇 emulates the particle leaving the laser field.
Goal: compute the emitted spectrum via the Fourier transform of
𝑥(𝑡).
---

## Slide 16: Slide 6: Fourier Transform — Step-by-Step Integration
𝐴(𝜔)
√2𝜋
Define spectral amplitude
𝑇
1
= ∫ 𝑥0 cos(𝜔0𝑡) 𝑒−𝑖𝜔𝑡 𝑑𝑡.
0
Express cosine via exponentials:
cos(𝜔0𝑡)
= 1⁄2 (𝑒𝑖𝜔0𝑡 + 𝑒−𝑖𝜔0𝑡).
Insert and integrate term-by-term:

## Slide 17
𝐴(𝜔)
=
𝑥0
2√2𝜋
𝑇
∫
0
[𝑒𝑖(𝜔0−𝜔)𝑡 + 𝑒−𝑖(𝜔0+𝜔)𝑡]𝑑𝑡.
Evaluate integrals of the form
𝑇
∫ 𝑒𝑖𝛥𝜔 𝑡 𝑑𝑡
0
=
𝑒
𝑖𝛥𝜔𝑇
− 1
, 𝛥𝜔 = 𝜔0 − 𝜔 or − (𝜔0 + 𝜔).
𝑖𝛥𝜔
Keep only the first term 𝛥𝜔 = 𝜔0 − 𝜔 for |𝜔 − 𝜔0| ≪ 𝜔0 (rotating- wave approximation) and drop the second rapidly oscillating term.
---

## Slide 18
Slide 7: Resulting Intensity Profile — Sinc𝟐 Function
After simplification,
𝐴(𝜔)
2√2𝜋
𝑖(𝜔0 − 𝜔)
≈ .
𝑥0
𝑒𝑖(𝜔0−𝜔)𝑇 − 1
Spectral intensity 𝐼(𝜔) = |𝐴(𝜔)|2:
𝐼(𝜔)
= 𝐶
sin2[(𝜔 − 𝜔0) 𝑇/2]
(𝜔 − 𝜔 )2
0
,
where 𝐶 = 𝑥0 /(8𝜋).
2

## Slide 19
Key features of 𝐼(𝜔):
Central maximum at 𝜔 = 𝜔0.
 Zeros whenever (𝜔 − 𝜔0) 𝑇/2 = 𝑛𝜋, 𝑛 ∈ ℤ\{0}.
Side lobes characteristic of a finite rectangular time window (Fourier transform of a box).
Full halfwidth at half maximum (HWHM):
5.6
𝛿𝜔𝑇 = 𝑇 .

## Slide 20
[IMAGE REQUIRED: Plot of sinc2 function with annotated HWHM, side lobes, and zero crossings.]
Prepared by Dist. Prof. Dr. M.A. Gondal for Phys 608 Laser Spectroscopy course in KFUPM (Term 251)

## Slide 21: Slide 8: Connecting Model to a Rectangular Laser Beam
Rectangular spatial intensity profile ⇒ particle experiences constant field amplitude while inside the beam.
Interaction time 𝑇 = 𝑑/|𝑣| effectively replaces the mathematical window length in the oscillator model.
Therefore
𝛿𝜔rect
≃
5.6 |𝑣|
𝑑
.

## Slide 22
Each symbol:
𝛿𝜔rect = full width at half maximum (rad s−1).
|𝑣| = particle speed (m s−1).
𝑑 = beam diameter where intensity is uniform (m).
Implication: doubling the beam diameter halves the width; reducing the speed has the same effect.
---

## Slide 23: Slide 9: Realistic Laser Beams — Gaussian Spatial Profile
Fundamental TEM00 coordinate 𝑟.
Electric field amplitude:
𝐸(𝑟, 𝑡)
where
mode intensity varies as Gaussian in radial
2 2
= 𝐸0 𝑒−𝑟 /𝑤0 cos(𝜔𝑡),
𝑤0 = beam waist radius (m) at which |𝐸| = 𝐸0/𝑒.

## Slide 24
Forced dipole amplitude proportional to field: 𝑥 = 𝛼𝐸 with 𝛼 = polarizability [C m2 V−1].
Gaussian spatial envelope maps onto Gaussian frequency envelope after transit-time Fourier transform.
Derived Gaussian line shape:
𝐼(𝜔)
= 𝐼0 exp [−
(𝜔 − 𝜔0)2 𝑤2
2 |𝑣|2
].

## Slide 25
[IMAGE REQUIRED: Cross-section of Gaussian beam showing 2 𝑤0
width, plus overlaid temporal Gaussian in frequency domain.]
Prepared by Dist. Prof. Dr. M.A. Gondal for Phys 608 Laser Spectroscopy course in KFUPM (Term 251)

## Slide 26: Slide 10: Transit-Time Limited Width for Gaussian Beam
Full width at half maximum (FWHM) in angular frequency:
𝛿𝜔𝑡
|𝑣|
= 2 √2ln2 ≈ 2.4 .
𝑤 𝑤
|𝑣|
Convert to ordinary frequency (Hz):
𝛿𝜈𝑡 =
𝛿𝜔𝑡
2𝜋
|𝑣|
≈ 0.4 𝑤
Symbol definitions:

## Slide 27
𝑤 = beam waist radius (m).
|𝑣| = particle speed (m s−1).
Beam waist relates to wavelength 𝜆 and Rayleigh range 𝑅 (to be defined later):
𝑤 =
√
𝜆𝑅
2𝜋
.

## Slide 28
Key
proportionalities:
reduce
width
by either
enlarging 𝑤 or
lowering |𝑣|.
---

## Slide 29: Slide 11: How To Reduce Transit-Time Broadening
Strategy 1 — Increase beam diameter 2 𝑤:
Optical lenses can expand the waist.
Trade-off: lower intensity at fixed power.
Strategy 2 — Reduce particle velocity |𝑣|:
Cool translational motion (cryogenic beams, buffer-gas cooling).
Laser cooling provides dramatic velocity reduction.

## Slide 30
Strategy 3 — Combine both: optical cavities support large spot sizes at high intensity.
Experimental verification: discussed in detail in Volume 2, Sections
2.3 & 9.2; record-narrow molecular lines achieved using both methods.

## Slide 31
[IMAGE REQUIRED: Flowchart comparing manipulation of beam diameter and molecular velocity, with example experimental setups.]
Prepared by Dist. Prof. Dr. M.A. Gondal for Phys 608 Laser Spectroscopy course in KFUPM (Term 251)

## Slide 32: Slide 12: Transit-Time Broadening vs Natural Width —
Example 3.6(a)
Species: nitrogen dioxide (NO2).
Mean thermal velocity:
𝑣 = 600 m s−1.
Focused laser beam waist:
𝑤 = 0.10 mm
= 1.0 × 10−4 m.

## Slide 33
Transit-time width (Hz):
𝛿𝜈𝑡
600
≈ 0.4 1.0 × 10−4
= 2.4 × 106 Hz = 2.4 MHz.
Natural linewidth 𝛿𝜈𝑛 ≈ 10 kHz ⇒ transit-time broadening exceeds natural width by factor ∼ 240.
---

## Slide 34: Slide 13: Transit-Time Broadening vs Natural Width —
Example 3.6(b)
Frequency standard transition: methane (CH4) at
𝜆 = 3.39 𝜇m.
Mean molecular speed:
𝑣 = 7.0 × 104 cm s−1 = 700 m s−1.
Desired limit: 𝛿𝜈𝑡 ≤ 10 kHz.

## Slide 35
Required beam waist: solving 0.4
𝑣 = 10 kHz →
𝑤
𝑤 = 0.4 = 0.4 ≈ 3.0 cm,
𝑣
2𝜋 𝛿𝜈𝑡
700
2𝜋 × 104
so diameter 2 𝑤 ≈ 6 cm.
Practical implication: frequency-standard cells employ large-mode cavities to satisfy this requirement.

## Slide 36
[IMAGE REQUIRED: Side-by-side bars: natural linewidth vs transit-time linewidth at varying beam diameters for CH4.]
Prepared by Dist. Prof. Dr. M.A. Gondal for Phys 608 Laser Spectroscopy course in KFUPM (Term 251)

## Slide 37: Slide 14: Beyond Plane Waves — Curved Phase Fronts in
Focused Beams
Real Gaussian beams possess spherical phase fronts with radius of curvature 𝑅(𝑧).
Atom moving radially (along 𝑟) experiences spatial phase variation.
Maximum longitudinal phase shift between center 𝑟 = 0 and edge
𝑟 = 𝑟1:

## Slide 38
𝛥𝜙 =
2𝜋 𝑥
𝜆
,
where 𝑥 = optical path difference.
Geometry of circle:
𝑟2 = 𝑅2 − (𝑅 − 𝑥)2 ⇒ 𝑥 ≈ 𝑟
2
2 𝑅
for 𝑥 ≪ 𝑅.
Therefore

## Slide 39
𝛥𝜙 =
𝑘 𝑟2
2 𝑅 2 𝑐 𝑅
=
𝜔 𝑟2
.

## Slide 40
[IMAGE REQUIRED: Diagram of spherical wavefront with center of curvature, showing 𝑅, 𝑟, 𝑥, and phase shift region.]
Prepared by Dist. Prof. Dr. M.A. Gondal for Phys 608 Laser Spectroscopy course in KFUPM (Term 251)

## Slide 41: Slide 15: Linewidth Including Wave-Front Curvature
Combined effect of transit time and phase curvature derived in Ref. [105]:
𝛿𝜔 = √2ln2 [1 + (
2 |𝑣|
𝑤
𝜋 𝑤2
𝑅 𝜆
2
) ]1/2.
Define purely transit-time component
𝛿𝜔𝑡𝑙 =
2 |𝑣|
𝑤
√2ln2.

## Slide 42
Introduce dimensionless phase-front parameter
𝑅 𝜆
𝛥𝜙 = .
𝜋 𝑤2
Compact form:
𝛿𝜔 = 𝛿𝜔𝑡𝑙 (1 + 𝛥𝜙2)1/2 .
Curvature adds in quadrature; significant only when 𝛥𝜙 ≳ 1.
---

## Slide 43: Slide 16: Condition For Negligible Curvature Broadening
Require phase variation over 𝑟 = 𝑤 to be much less than 𝜋:
𝛥𝜙 = ≪ 𝜋.
𝜋 𝑤2
𝑅 𝜆
Simplifies to
𝑅 ≫
𝑤2
𝜆
.
Interpretation:

## Slide 44
Larger 𝑅 (flatter wavefronts) → smaller phase spread.
For
fixed 𝑅, widening the beam (𝑤 ↑) increases curvature
broadening — trade-off with earlier strategy.
Experimental design: choose focusing optics that place interaction region near beam waist but with sufficiently large 𝑅.

## Slide 45
[IMAGE REQUIRED: Plot showing 𝛿𝜔/𝛿𝜔𝑡𝑙 versus 𝛥𝜙 with threshold region.]
Prepared by Dist. Prof. Dr. M.A. Gondal for Phys 608 Laser Spectroscopy course in KFUPM (Term 251)

## Slide 46: Slide 17: Numerical Example 3.7 — Quantifying Curvature
Effects
Wavelength
𝜆 = 1.0 𝜇m.
Beam waist radius
𝑤 = 1.0 cm.
 Desired 𝛥𝜙 ≪ 2𝜋.

## Slide 47
Compute required radius of curvature:
𝑅 ≫ =
𝑤2
𝜆
(1.0 × 10−2)2
1.0 × 10−6
= 1.0 × 102 m = 1.0 × 104 cm.
If 𝑅 = 5.0 × 103 cm (focusing too strong), then
𝛥𝜙 = = = 2𝜋,
𝜋𝑤2 𝜋(1.0 × 10−2)2
𝑅𝜆
5.0 × 103 × 1.0 × 10−6
leading to (1 + 𝛥𝜙2)1/2 ≈ 6.5 times additional linewidth!

## Slide 48
Conclusion: for precision work, ensure 𝑅 well above 104 cm or expand the beam to reduce 𝑤.

## Slide 49
[IMAGE REQUIRED: Table comparing 𝑅, 𝛥𝜙, and resulting linewidth enhancement factors.]
Prepared by Dist. Prof. Dr. M.A. Gondal for Phys 608 Laser Spectroscopy course in KFUPM (Term 251)

## Slide 50: Slide 18: Key Takeaways & Experimental Guidelines
Transit-time broadening scales linearly with |𝑣| and inversely with beam size: mitigate by cooling and/or beam expansion.
Gaussian beams give Gaussian line shapes; rectangular beams give sinc2 profiles — choose geometry deliberately.
Wave-front curvature can substantially enlarge linewidth unless
𝑅 ≫ 𝑤2/𝜆.

## Slide 51
Precision frequency standards (e.g., CH4 at 3.39 µm) demand cm- scale waists or ultra-cold molecules to stay within natural linewidths.
Future frontier: laser cooling and optical trapping enable interaction times ≫ 𝜏sp, effectively eliminating transit-time limits altogether.
---