## Slide 1
Chap. 5.3 Spectral Characteristics of Laser Emission

## Slide 2: Slide 1: Spectral Characteristics of Laser Emission —
Setting the Stage
Goal
of this block of slides: build a rigorous, step-by-step
understanding of how an active medium and an optical resonator together determine the exact set of frequencies emitted by a laser.
Key
ingredients that must be analysed separately and then
combined:
The spectral gain profile of the amplifying transition in the medium.

## Slide 3
The discrete resonance spectrum (axial and transverse modes) of the passive optical cavity.
The non-linear, intensity-dependent phenomena that arise once oscillation starts (gain saturation, mode competition, spatial hole burning, mode pulling, …).
Strategy for the forthcoming slides:
Introduce mathematical description of the passive cavity.
Insert an active medium, derive modified eigenfrequencies.

## Slide 4
Develop the laser threshold condition from first principles.
Examine line-narrowing effects, saturation physics, multimode behaviour, and the frequency shifts produced by dispersion in the gain medium.
  Conventions adopted throughout:
  𝑐: speed of light in vacuum [m s−1].
  𝑑: physical mirror separation [m].

## Slide 5
𝑛(𝜈): frequency-dependent refractive index of the active medium (dimensionless).
𝐿: length of the gain medium inside the cavity [m].
Axial mode index 𝑞 ∈ ℤ.
All symbols will be re-defined on the

## Slide 6
Slide where they first appear.
CGS and SI units will be stated explicitly when needed.
---

## Slide 7: Slide 2: Passive Fabry–Perot Resonator — Eigenfrequency
Review
Consider two perfectly parallel mirrors separated by distance 𝑑. For vacuum between the mirrors, the round-trip optical path length is 2 𝑑.
Standing-wave condition (electric field node at each mirror):
2 𝑑 = 𝑞
𝑐
𝜈𝑞,vac

## Slide 8
where
𝜈𝑞,vac: eigenfrequency of the 𝑞-th axial mode in vacuum [Hz].
𝑞: integer mode number ( 0,1,2, … ).
Solve for the eigenfrequencies:
𝜈𝑞,vac = 2 𝑑
𝑞 𝑐
Important derived quantity – Free Spectral Range (FSR):

## Slide 9
𝛿𝜈 =
𝜈𝑞+1,vac − 𝜈𝑞,vac
=
𝑐
2 𝑑
FSR is the constant spacing between adjacent axial modes of the passive cavity.
Passive cavity half-width (power) of each resonance, caused by mirror transmission 𝑇 and additional losses 𝛾, will be derived later when 𝐺(𝜈) is introduced.
---

## Slide 10: Slide 3: Inserting an Active Medium — Effective Optical
Length
Whenever a dielectric slab of physical length 𝐿 and frequency- dependent index 𝑛(𝜈) is placed between the mirrors, the effective round-trip optical path length changes.
Replace the earlier geometric length 𝑑 by an effective length 𝑑∗(𝜈). Detailed derivation:
1. Segment outside the gain medium:

## Slide 11
(𝑑 − 𝐿) in vacuum ⇒ optical length (𝑑 − 𝐿)
Segment inside the gain medium:
𝐿 gives optical length 𝑛(𝜈) 𝐿
Total optical length:
𝑑∗(𝜈) = (𝑑 − 𝐿) + 𝑛(𝜈) 𝐿
Rearranged form:
𝑑∗(𝜈) = 𝑑 + [𝑛(𝜈) − 1]𝐿
  The new eigenfrequency condition becomes:

## Slide 12
2 𝑑∗(𝜈) = 𝑞
𝑐
𝜈𝑞,act
where 𝜈𝑞,act denotes the active-cavity eigenfrequency.

## Slide 13
[IMAGE REQUIRED: Show side-by-side sketches of (a) empty cavity 𝑑; (b) cavity with active medium of length 𝐿; optical paths indicated; arrows marking 𝑑 − 𝐿 and 𝑛𝐿.]
---
Prepared by Dist. Prof. Dr. M.A. Gondal for Phys 608 Laser Spectroscopy course in KFUPM (Term 251)

## Slide 14: Slide 4: Anomalous Dispersion and Its Spectroscopic
Importance
Within the gain bandwidth of an inverted transition, the real part of the refractive index exhibits anomalous dispersion:
𝑛(𝜈) decreases below unity on the low-frequency side ( 𝜈 < 𝜈0 ).
𝑛(𝜈) increases above unity on the high-frequency side ( 𝜈 > 𝜈0 ).
Physical reason:

## Slide 15
Kramers–Kronig
relations link negative absorption (stimulated
emission) to a dispersive phase shift.
The sign change in 𝛼(𝜈) (gain instead of loss) forces a corresponding sign change in d𝑛/d𝜈.
Resulting pulling of the cavity modes:
Frequency of each mode is shifted towards 𝜈0 compared with the passive value 𝜈𝑞,vac.

## Slide 16
Quantitative formula).
expression
derived
in later
slides
(mode
pulling

## Slide 17
[IMAGE REQUIRED: Plot 𝛼(𝜈) (negative peak) and corresponding 𝑛(𝜈)
crossing unity; annotate “anomalous dispersion” region.]
Prepared by Dist. Prof. Dr. M.A. Gondal for Phys 608 Laser Spectroscopy course in KFUPM (Term 251)

## Slide 18: Slide 5: Net Round-Trip Gain — Precise Definition
Define 𝐺(𝜈, 2 𝑑): amplitude (not intensity) gain factor for one round-trip of length 2 𝑑 inside the resonator.
𝐺(𝜈, 2 𝑑) = exp[−2𝛼(𝜈)𝐿 − 𝛾(𝜈)]
where
𝛼(𝜈) : small-signal absorption coefficient (negative if net gain) [m−1].
𝐿 : length of the amplifying region [m].

## Slide 19
𝛾(𝜈) : total passive loss factor per round-trip (dimensionless, 𝛾 > 0). Includes mirror transmission, scattering, diffraction, intracavity element losses.
The first term −2𝛼𝐿 appears twice because the light crosses the gain medium on the forward and backward paths.
Threshold condition:
𝐺(𝜈thr, 2 𝑑) = 1
means “round-trip amplification equals all losses.”

## Slide 20
Observe carefully:
𝐺 is frequency dependent through both 𝛼(𝜈) and 𝛾(𝜈).
The exponent is additive — changes in 𝛼 or 𝛾 shift the logarithm of 𝐺
linearly.
---

## Slide 21: Slide 6: How a Probe Beam Reveals the Resonator
Transmission Spectrum
Thought experiment: send weak, broadband light with spectral intensity 𝐼0(𝜈) into the cavity through mirror 𝑀1.
Multiple internal reflections lead to constructive or destructive interference.

## Slide 22
If amplification per pass is 𝐺(𝜈), mirror intensity transmission is 𝑇, reflectivity is 𝑅 ( 𝑅 + 𝑇 + scattering = 1 ), then total transmitted intensity follows an Airy-type formula extended by gain:
𝐼T(𝜈) = 𝐼0(𝜈)
𝑇 2 𝐺(𝜈)
[1 − 𝐺(𝜈)]2 + 4 𝐺(𝜈) sin2 (2)
𝜙
with
Phase advance per round-trip:

## Slide 23
𝜙(𝜈) =
4𝜋 𝑑∗(𝜈) 𝜈
𝑐
Transmission maxima condition:
𝜙(𝜈) = 2𝜋𝑞
Exactly the active-cavity eigenfrequency condition derived earlier.
Important limit:

## Slide 24
 As 𝐺(𝜈) → 1−
and 𝜙 satisfies the resonance condition, the
denominator tends to zero ⇒ 𝐼T/𝐼0 diverges ⇒ laser oscillation set- up.

## Slide 25
[IMAGE REQUIRED: Plot of 𝐼T(𝜈) vs 𝜈 for three cases: (a) 𝐺 < 1, (b) 𝐺 = 0.99, (c) 𝐺 = 1.0; show narrowing and height growth of peaks.]
Prepared by Dist. Prof. Dr. M.A. Gondal for Phys 608 Laser Spectroscopy course in KFUPM (Term 251)

## Slide 26: Slide 7: Graphical Visualization of the Threshold
Condition
Procedure often used in laboratory alignment:
Plot the unsaturated gain curve −2𝛼(𝜈)𝐿 (negative ordinate implies amplification) vs frequency.
On the same axis plot the frequency-dependent total losses 𝛾(𝜈).
Subtract point-wise to obtain the net gain

## Slide 27
𝛥𝛼(𝜈) = −2𝛼(𝜈)𝐿 − 𝛾(𝜈)
Those frequencies where 𝛥𝛼(𝜈) > 0 satisfy 𝐺 > 1 and can lase.
  The contact points 𝛥𝛼(𝜈) = 0 mark the threshold.

## Slide 28
[IMAGE REQUIRED: Schematic similar to Fig. 5.24 – three curves (gain, loss, net gain); shades indicating regions where lasing is allowed.]
---
Prepared by Dist. Prof. Dr. M.A. Gondal for Phys 608 Laser Spectroscopy course in KFUPM (Term 251)

## Slide 29: Slide 8: Case Study — Gas Laser With Doppler-Broadened
Gain (Example 5.9a, Part 1)
Given parameters (He-Ne-like):
Line-centre small-signal absorption coefficient
𝛼(𝜔0) = −0.01 cm−1
Gain cell length
𝐿 = 10 cm

## Slide 30
Doppler FWHM (angular frequency)
−2𝛼(𝜔)𝐿 = −2 𝛼(𝜔0) 𝐿 exp [− (
𝜔 − 𝜔0
0.68 𝛿𝜔D
𝛿𝜔D = 1.3 × 109 Hz × 2𝜋 = 8.17 × 109 rad s−1
Passive loss exponent per round-trip
𝛾 = 0.03
Doppler-broadened Gaussian profile for amplification coefficient:
2
) ]
Condition for positive net gain:

## Slide 31
−2𝛼(𝜔)𝐿 > 𝛾
Insert numbers ⇒ determine the angular frequency interval satisfying the inequality.
---

## Slide 32: Slide 9: Case Study — Gas Laser With Doppler-Broadened
0.02 exp [− (
0.68 𝛿𝜔D
Gain (Example 5.9a, Part 2)
Solve inequality numerically:
2
𝜔 − 𝜔0
) ] > 0.03
1. Rearrange:
exp [− (
𝜔 − 𝜔0
0.68 𝛿𝜔D
2
) ] > 1.5

## Slide 33
2. Exponential on left cannot exceed 1 ⇒ the inequality has no solution
unless the prefactor −2𝛼(𝜔0)𝐿 is > 0.03. But the given magnitude
  < 0.03 contradicts that.
    Interpretation:
    Pump power must be increased further until −2𝛼(𝜔0)𝐿 = 0.03.
    After threshold, the valid frequency range broadens as the pump increases because unsaturated 𝛼(𝜔) becomes more negative.

## Slide 34
Once −2𝛼(𝜔)𝐿 > 0.03 at line centre, approximate stimulated- emission bandwidth:
𝛿𝜔 ≈ 2𝜋 × 3 GHz
as quoted in the text.

## Slide 35
[IMAGE REQUIRED: Gaussian profile with shaded central region where gain exceeds losses; adjustable vertical offset representing pump power.]
---

## Slide 36: Slide 10: Example 5.9a — Mode Counting in a 50 cm
Resonator
Mirror separation (physical length) 𝑑 = 50 cm = 0.5 m.
Passive cavity FSR:
𝛿𝜈 = =
𝑐 3.00 × 108 m s−1
2 𝑑 1.0 m
= 3.00 × 108 Hz = 300 MHz
Amplification bandwidth supporting oscillation ≈ 3 GHz.
Number 𝑁axial of axial modes inside the gain band:

## Slide 37
3 GHz
𝑁axial = 300 MHz ≈ 10
These ten modes are potentially able to reach threshold; final number depends on saturation and competition effects elaborated in later slides.
---

## Slide 38: Slide 11: Case Study — Solid-State / Dye Laser Broad Gain
(Example 5.9b)
Typical dye laser gain FWHM:
𝛥𝜈gain ≈ 1 × 1013 Hz
Using same cavity length 𝑑 = 50 cm:
1 × 1013 Hz
𝑁axial = 3.0 × 108 Hz ≈ 3 × 10
4
Crucial observation:

## Slide 39
In broad-band media, the passive cavity mode spacing is extremely fine compared with the gain window.
Additional
intra-cavity wavelength-selective elements (gratings,
prisms, etalons) become essential for spectroscopy-grade single- mode operation.

## Slide 40
[IMAGE REQUIRED: Histogram illustrating density of resonator modes under a broad dye gain curve; 30 000 discrete lines packed under a smooth envelope.]

## Slide 41: Slide 12: Passive vs Active Cavity Linewidth and the
Quality Factor
Define passive resonator finesse 𝐹𝑝 and linewidth 𝛥𝜈𝑝 (half-power width). For mirrors of amplitude reflectivity 𝑟 (𝑇 = 1 − 𝑟2 − losses):
𝜋√𝑟
𝐹𝑝 = 1 − 𝑟
𝛥𝜈𝑝 =
𝛿𝜈
𝐹
𝑝
When gain medium compensates losses and approaches threshold
𝐺 → 1−, effective finesse rises:

## Slide 42
𝐹𝑎
∗
2𝜋√𝐺(𝜈)
=
1 − 𝐺(𝜈)
Corresponding active-cavity linewidth:
𝛥𝜈 =
𝑎
𝛿𝜈
𝐹
𝑎
∗
= 𝛿𝜈
1 − 𝐺(𝜈)
2𝜋√𝐺(𝜈)
Limit behaviour:
 As 𝐺(𝜈) → 1, 𝐹𝑎 → ∞ and 𝛥𝜈𝑎 → 0.
∗

## Slide 43
In practice quantum noise sets a lower bound on the achievable laser linewidth (see Sect. 5.6 — Schawlow-Townes limit).
---

## Slide 44: Slide 13: Off-Resonance Regions — Why Threshold Is Not
Met
Between successive resonances, phase 𝜙 deviates from 2𝜋𝑞 by ≈ 𝜋.
For a Lorentzian resonance of half-width 𝛥𝜈𝑟 , loss factor 𝛽(𝜈)
increases approximately ten-fold at |𝜈 − 𝜈0| ≃ 3 𝛥𝜈𝑟 .
Since the gain curve decays away from 𝜈0, net gain quickly turns negative outside the immediate vicinity of each mode.

## Slide 45
Conclusion: lasing occurs only in narrow frequency slots centred at cavity resonances; broad “valleys” remain non-lasing despite active medium present.
---

## Slide 46: Slide 14: Introduction to Gain Saturation — The Basic
Concept
Population inversion 𝛥𝑁 ≡ 𝑁2 − 𝑁1 created by pumping.
Stimulated emission rate for one frequency component 𝜈:
𝑅stim(𝜈) = 𝐵21 𝜌(𝜈) 𝑔(𝜈 − 𝜈0) 𝑁2
where
𝐵21: Einstein 𝐵-coefficient.

## Slide 47
𝜌(𝜈): spectral energy density [J m−3 Hz−1].
𝑔(𝜈 − 𝜈0): normalized line-shape function.
As intra-cavity intensity 𝐼 grows, 𝜌(𝜈) ∝ 𝐼
depletes 𝑁2.
grows, hence 𝑅stim
Under steady-state operation:
pump rate = stimulated emission rate
⇒ inversion is “pinned” to a smaller value 𝛥𝑁thr.

## Slide 48
This process is termed gain saturation. It introduces nonlinearity necessary for amplitude stability.
---

## Slide 49: Slide 15: Homogeneous Broadening — Uniform
Saturation Across Frequency
For a homogeneously broadened line:
All atoms/molecules “see” every frequency component equally well.
Saturation of one laser mode reduces gain for the entire line profile.
Standard
saturation formula (derivation recalled from rate
equations):

## Slide 50
𝛼
𝑠,hom
( )
𝜈 =
𝛼0(𝜈)
1 + 𝑆 1 + 𝐼/𝐼
=
𝛼0(𝜈)
𝑠
where
𝛼0(𝜈): small-signal gain coefficient (before saturation).
𝐼𝑠: saturation intensity, the intensity for which 𝑆 = 1.
𝑆 ≡ 𝐼/𝐼𝑠: dimensionless saturation parameter.
Consequence:

## Slide 51
Once one mode reaches high intensity, the gain for neighbouring modes drops as well ⇒ mode competition, often resulting in single- frequency output for perfectly homogeneous media.
---

## Slide 52: Slide 16: Inhomogeneous Broadening — Selective
Saturation and Hole Burning
In inhomogeneous ensembles (Doppler, Stark, inhomogeneous crystal fields):
Individual molecules respond only to frequencies within their narrow homogeneous sub-profile 𝛥𝜈hom.
A strong monochromatic field at 𝜈𝐿
population distribution 𝛥𝑁(𝜈).
“burns a hole” in the overall

## Slide 53
Calculated saturated gain coefficient:
𝛼𝑠,inh(𝜈) = 𝛼0(𝜈)
√1 + 𝑆
1 + 𝑆
=
√1 + 𝐼/𝐼
𝛼0(𝜈)
𝑠
Two competing trends with rising 𝐼:
Population depletion ⇒ gain ∝ 1/(1 + 𝑆).
Spectral hole broadening ⇒ effective molecules ∝ √1 + 𝑆. Net result given above.
number
of contributing

## Slide 54
[IMAGE REQUIRED: Illustrate (a) unsaturated inhomogeneous Gaussian;
(b) narrow hole at low 𝐼; (c) wider h
---
o
le at high 𝐼. Axes labelled 𝜈 vs 𝛥𝑁.]

## Slide 55
Prepared by Dist. Prof. Dr. M.A. Gondal for Phys 608 Laser Spectroscopy course in KFUPM (Term 251)

## Slide 56: Slide 17: Spatial Hole Burning — Standing-Wave
Saturation Pattern
In a linear resonator the field is a standing wave:
𝐸(𝑧) = 𝐸0 cos(2𝜋𝑧/𝜆)
nodes at mirrors, antinodes inside.
 Local intensity 𝐼(𝑧) ∝ |𝐸(𝑧)|2 = 𝐸2 cos2(2𝜋𝑧/𝜆).
0
Saturation therefore occurs only at the antinodes.

## Slide 57
Nodes remain unsaturated ⇒ residual inversion.
Another mode shifted by 𝜆/4 can exploit these unsaturated regions
⇒ multiple modes may co-exist even in homogeneous media.

## Slide 58
[IMAGE REQUIRED: (a) Two standing-wave patterns offset by 𝜆/4; (b) corresponding inversion profile with periodic troughs (holes).]
---
Prepared by Dist. Prof. Dr. M.A. Gondal for Phys 608 Laser Spectroscopy course in KFUPM (Term 251)

## Slide 60: Slide 18: Quantitative Treatment of Spatial Hole-Burning
Mode Spacing
Suppose gain medium length 𝐿 is short and is located a distance 𝑎
from mirror 𝑀1.
Condition for two standing waves of wavelengths 𝜆1, 𝜆2
maxima separated by 𝜆/𝑝:
to have
1
𝑚 𝜆1 = 𝑎 = (𝑚 + 𝑝) 𝜆2

## Slide 61
where 𝑚 is an integer.
Convert to frequency ( 𝜈 = 𝑐/𝜆 ):
𝜈1 =
𝑚 𝑐
𝑎 𝑎
,
𝜈2 =
(𝑚 + 1/𝑝)𝑐
Spacing between spatial-hole-burning modes:
𝛿𝜈sp = 𝜈2 − 𝜈1 = 𝑎 𝑝
𝑐
Expressed relative to axial FSR 𝛿𝜈 = 𝑐/(2 𝑑):

## Slide 62
𝛿𝜈sp = 𝑎 𝑝 𝛿𝜈
2 𝑑
3
If the homogeneous gain width < 2 (𝑑/𝑎)𝛿𝜈, only one spatial-hole-
burning mode can survive.
---

## Slide 63: Slide 19: Example 5.10 — Numerical Illustration of Spatial
Hole Burning
Given:
Cavity length 𝑑 = 100 cm.
Gain medium length 𝐿 = 0.1 cm.
Distance from mirror 𝑎 = 5 cm.
Desired separation index 𝑝 = 3.

## Slide 64
Calculated quantities:
𝛿𝜈 =
𝑐 3.00 × 108
2 𝑑 2
=
Hz = 150 MHz
2 𝑑 200 cm
𝛿𝜈sp = 𝑎 𝑝 𝛿𝜈 = 5 cm × 3 150 MHz ≈ 2.0 GHz
Interpretation:

## Slide 65
If the homogeneous width of the gain profile < 2.0 GHz, spatial hole burning will not allow more than one mode ⇒ single-mode operation feasible.
---

## Slide 66: Slide 20: Eliminating Spatial Hole Burning — Ring Lasers
In a unidirectional ring cavity the field is purely travelling wave.
Intensity 𝐼 is uniform along the propagation axis ⇒ no nodes and antinodes.
Result:
Entire gain medium experiences the same saturation ⇒ no spatial holes.
Higher overall extraction efficiency; favoured in high-power lasers.

## Slide 67
Practical ring implementations:
Four-mirror folded ring (bow-tie).
Fibre ring lasers.
Unidirection enforced with optical isolators or Faraday rotators.
---

## Slide 68: Slide 21: Homogeneous vs Inhomogeneous —
Consequences for Multimode Operation
Homogeneous gain:
Strong mode competition through shared population.
Tends towards single-mode output if* spatial hole burning and technical noise can be suppressed.
Inhomogeneous gain:

## Slide 69
Minimal competition; each mode taps a distinct sub-ensemble.
Many axial and transverse modes can oscillate simultaneously.
Real media are mixed; the ratio 𝛿𝜈/𝛥𝜈hom
strength.
Transverse modes (TEM𝑚,𝑛) complicate the spectrum because they have different longitudinal frequencies in non-confocal resonators.
---
dictates competition

## Slide 70: Slide 22: Designing Cavities to Suppress Higher-Order
Transverse Modes
Key tools:
Choose mirror radii such that the resonator is stable only for TEM00.
Insert intracavity apertures matched to the Gaussian beam waist.
Employ unstable or confocal resonator geometries when high power is needed but single transverse mode is tolerated.

## Slide 71
Benefit: a Gaussian beam with minimal divergence, higher spatial coherence.
Spectral implication: still potentially multimode in frequency unless axial mode selection is also enforced.
---

## Slide 72: Slide 23: Example 5.11 — HeNe Laser Detailed Mode
Count
Parameters recap:
 𝜆 = 632.8 nm.
Doppler width 1.5 GHz (FWHM).
Cavity length 𝑑 = 1.0 m.
Axial mode spacing 𝛿𝜈 = 150 MHz.

## Slide 73
Gain above threshold ≈ 1.2 GHz wide.
Potential axial modes 𝑁 ≈ 8.
Homogeneous linewidth contributions:
Natural width 20 MHz.
Pressure width ≈ 20 MHz.
Power broadening (example 𝐼/𝐼𝑠 = 10): increases to ≈ 100 MHz.

## Slide 74
Since homogeneous width < 𝛿𝜈, modes do not overlap strongly ⇒ simultaneous oscillation of several independent modes yields stable multi-line spectrum (Fig. 5.27a).
---

## Slide 75: Slide 24: Example 5.12 — Argon-Ion Laser Multimode
Dynamics
Key numerical data:
Doppler width 8–10 GHz.
Resonator length 𝑑 = 1.2 m ⇒ 𝛿𝜈 = 125 MHz.
Homogeneous width ≫ 𝛿𝜈 due to:
Electron–ion pressure broadening.

## Slide 76
High intracavity power (10–100 W) ⇒ strong power broadening.
Resulting behaviour:
𝛥𝜈hom ≫ 𝛿𝜈 ⇒ intense mode competition.
However, technical perturbations (cavity length jitter, discharge noise) constantly redistribute gain ⇒ observed spectrum fluctuates randomly (Fig. 5.27b).
---

## Slide 77: Slide 25: Example 5.13 — Dye Laser Spectral Features
Liquid dye medium: gain FWHM of order 2 × 1013 Hz (≈ 20 nm at 600
nm).
With 𝑑 = 0.75 m, axial modes 𝑁 ∼ 105.
Homogeneous profile dominates, yet refractive index fluctuations in the liquid cause mode coupling ⇒ time-dependent multimode emission.
Pulsed dye lasers:

## Slide 78
Gain builds up in 𝜇s-scale; spectrum integrates over hopping—final
bandwidth ≈ 1 nm.
To obtain tunable single-mode operation:
Introduce diffraction grating, prism, or birefringent filter inside cavity (Sect. 5.4).

## Slide 79
[IMAGE REQUIRED: Photographic spectrum of a pulsed dye laser showing clusters and gaps; annotate causes.]
---
Prepared by Dist. Prof. Dr. M.A. Gondal for Phys 608 Laser Spectroscopy course in KFUPM (Term 251)

## Slide 80: Slide 26: Non-Uniform Intensity Distribution Within a
Multimode Band
Laser spectral density 𝐼𝐿 (𝜈, 𝑡) is not smooth — contains peaks and holes:
𝐼𝐿 (𝜔, 𝑡) = ∑ 𝐴𝑘 (𝑡) cos2[𝜔𝑘𝑡 + 𝜙𝑘(𝑡)]
𝑘
Time-averaged output:

## Slide 81
⟨𝐼(𝜔)⟩ =
1
𝑇
𝑇
∫ ∑ 𝐴𝑘 (𝑡) cos2[𝜔𝑘𝑡 + 𝜙𝑘(𝑡)] d𝑡
0 𝑘
For spectroscopic scanning, holes cause artificial features if the scanning time < 𝑇.
Experimental remedy:
 Wobble the cavity length 𝑑(𝑡) = 𝑑0 + 𝛿𝑑 sin(2𝜋𝑓𝑡) with 𝑓 > 1/𝑇.
Rapidly modulates all 𝜔𝑘 ⇒ smoother averaged spectrum.
---

## Slide 82: Slide 27: Mode Pulling — Concept Introduction
Even after mode selection, the exact frequency of a laser mode
differs from the passive cavity
resonance 𝜈𝑟
because of the
frequency-dependent index 𝑛(𝜈).
This shift is called mode pulling.
Two intuitive viewpoints:
1. Cavity view: refractive index changes effective length 𝑑∗.

## Slide 83
Gain medium view: phase of standing wave adjusted so that round- trip phase remains an integer multiple of 𝜋 in presence of dispersion.
  Quantitative derivation on next slide.
---

## Slide 84: Slide 28: Mode Pulling — Mathematical Derivation Step-
by-Step
Passive cavity phase per round-trip:
𝜙𝑝 = 2𝜋𝜈𝑝
Active cavity phase:
2 𝑑
𝑐
= 𝑚𝜋, 𝑚 ∈ ℤ
𝜙𝑎 = 2𝜋𝜈𝑎
2 𝑑 𝑛(𝜈𝑎)
𝑐
= 𝑚𝜋

## Slide 85
Expand 𝜙(𝜈) in Taylor series around 𝜈𝑝:
𝜙𝑎 ≈ 𝜙𝑝 + ∂𝜈 |
∂𝜙
𝜈𝑝
(𝜈𝑎 − 𝜈𝑝) + [𝜙𝑎(𝜈𝑎) − 𝜙𝑝(𝜈𝑎)] = 𝑚𝜋
Setting 𝜙𝑝 = 𝑚𝜋 and rearranging yields:
∂𝜙
∂𝜈
(𝜈𝑎 − 𝜈𝑝) + [𝜙𝑎(𝜈𝑎) − 𝜙𝑝(𝜈𝑎)] = 0
identical to Eq. (5.72).
Need dispersion relation linking 𝑛(𝜈) to gain coefficient 𝛼(𝜈):

## Slide 86
𝑛(𝜈) = 1 +
𝛥𝜈𝑚
𝜈0 − 𝜈 𝑐
2𝜋𝜈
𝛼(𝜈)
where
𝜈0: centre frequency of gain line.
𝛥𝜈𝑚 = 𝛾/(2𝜋): homogeneous half-width.
After algebra (see next slide) obtain the mode-pulled frequency.
---

## Slide 87: Slide 29: Mode Pulling — Final Formula and Limiting
Cases
Derived expression:
𝜈𝑟 𝛥𝜈𝑚 + 𝜈0 𝛥𝜈𝑟
𝜈 =
𝛥𝜈𝑚 + 𝛥𝜈𝑟
𝑎
where

## Slide 88
𝛥𝜈𝑟 = 4𝜋𝑑: passive cavity resonance half-width (determined by total losses 𝛾).
Interpretation:
Weighted average of cavity resonance 𝜈𝑟 and gain centre 𝜈0.
Weighting factors are respective half-widths.
Gas lasers typical numbers:
 𝛥𝜈𝑟 ∼ 1 MHz.
𝑐 𝛾

## Slide 89
 𝛥𝜈𝑚 ∼ 100 MHz.
Simplified form for 𝛥𝜈𝑟 ≪ 𝛥𝜈𝑚:
𝜈 ≈ 𝜈
𝑎
𝑟
𝛥𝜈𝑟
+ (𝜈
𝛥𝜈𝑚
0
− 𝜈 )
𝑟
Mode pulled only slightly towards 𝜈0.
Pulling magnitude proportional to detuning (𝜈0 − 𝜈𝑟 ).
---

## Slide 90: Slide 30: Practical Consequences of Mode Pulling
In line-centre operation (𝜈𝑟 ≈ 𝜈0) pulling is negligible.
Near slope of gain curve:
Small cavity length drifts ⇒ large frequency drifts partially cancelled
by pulling.
Stabilization schemes exploit or compensate for this.
For precision spectroscopy:

## Slide 91
Mode pulling introduces systematic error if laser is locked to cavity rather than atomic reference.
Correction requires knowledge of 𝛥𝜈𝑚, 𝛥𝜈𝑟 , and detuning.
[IMAGE REQUIRED: Plot showing cavity resonance (vertical lines) and gain curve; arrows indicating mode shift towards centre as gain slope steepens.]
---

## Slide 92: Slide 31: Summary of Key Quantitative Relationships
Passive cavity FSR:
𝛿𝜈 =
𝑐
2 𝑑
Round-trip gain factor:
𝐺(𝜈) = exp[−2𝛼(𝜈)𝐿 − 𝛾(𝜈)]
Active cavity linewidth:

## Slide 93
𝛥𝜈𝑎 = 𝛿𝜈
1 − 𝐺
2𝜋√𝐺
Saturated gain coefficients:
Homogeneous:
𝛼 =
𝑠
𝛼0
1 + 𝐼/𝐼
𝑠
Inhomogeneous:

## Slide 94
𝛼𝑠 =
𝛼0
√1 + 𝐼/𝐼𝑠
Mode pulling:
𝜈𝑎 =
𝜈𝑟 𝛥𝜈𝑚 + 𝜈0 𝛥𝜈𝑟
𝛥𝜈𝑚 + 𝛥𝜈𝑟
Each equation requires understanding of the definitions and units provided earlier; together they form the quantitative backbone for predicting and controlling laser spectra.

## Slide 95: Slide 32: Concluding Remarks and Next Steps
The frequency composition of laser emission is not a simple direct mirror of the gain profile; it emerges from a rich interplay of:
Cavity resonance conditions.
Gain saturation (homogeneous vs inhomogeneous).
Spatial hole burning and transverse-mode structure.
Dispersive frequency shifts (mode pulling).

## Slide 96
Experimental control levers:
Adjust cavity length 𝑑 and geometry.
Shape gain profile via temperature, pressure, and pumping.
Insert selective elements (etalons, gratings, birefringent filters).
  Subsequent chapters/slides will extend these concepts to:
  Linewidth narrowing mechanisms (Schawlow-Townes limit).
  Active frequency stabilization techniques.

## Slide 97
Tunable and mode-locked laser systems.
Mastery of today’s material equips you to design, diagnose, and optimize laser sources for high-resolution spectroscopy and other precision applications.
---