K F U P M (Physics)OSB

Review: - Chapter 17 – Waves I

Q1.	A rope of mass 0.45 kg is stretched between two supports 30 m apart.  If the tension in the rope is 2400 N, how long does it take a pulse to travel from one support to the other?  (ANS: 0.075 s)

Q2.	The speed of a transverse wave propagating along a thin cylindrical copper wire is 200 m/s.  Find the speed of such a wave along a second copper wire of half the diameter, assuming the tension is the same in both cases.           					(ANS: 400 m/s)

Q3.	At t=0, a transverse wave pulse in a wire is described by the function

y (x,0) = 8/(x2 +111)

where x and y are in cm.  Calculate y at x = 3 cm and t =1 s if the wave is traveling in the negative x direction with a speed of 4 m/s?  		       			(ANS: 0. 05 m )

Q4.	A transverse wave in a string is described by

y = 5.0 sin ( 2 * x – 3 * t )

where x and y are in cm and t is in s.  What is the magnitude of the transverse acceleration for the point located at x = 2 cm?						(ANS: 0.487 m/s**2)

Q5.	Consider a transverse wave in a long string described by

y = 0.200 * sin ( 15 * x – 2 * PI * t +3 ),

where x and y are in cm and t is in s.  What is the displacement of a point on the string at x = 2. 50 cm and t = 3.51 s? 							(ANS: - 0. 0785 cm )

Q6.	A travelling wave train on a string is harmonic, and its transverse displacement is given by y = 3.0 cos ( PI * x – 4 * PI * t ), where x and y are in cm and t is in s.  Calculate the power required to generate these waves if the string has a length of 20 m and a mass of 50 g .  Assume all the power produced by the source is delivered by the string.	(ANS: 7.1 * 10 **(-6) W )

Q7.	Harmonic waves 15 cm in amplitude are to be transmitted along a string that has a linear density of 4 * 10 ** ( - 2 ) kg/m.  If the maximum power delivered by the source is 500 W and the string is under a tension of 200 N, what is the highest vibrational frequency at which the source can operate?							(ANS: 20 Hz)

Q8.	Two strings with linear densities mu1 and mu2 are joined together and under the same tension.  If a wave has a wavelength of 2.0 cm in string 1, what is the wavelength in string 2?								(ANS: 2 * sqr ( mu1/ mu2) cm )

Q9.	Consider the following sinusoidal wave y = 10 cos ( 0.2 x – 100 t ), where x and y are in cm and t is in s.  At a given instant, let point A be at the origin ( x = 0 ) and point B be the first point along x that is 90 degrees out of phase with point A.  What is the coordinate of point B?										(ANS: 7. 85 cm )

Q10.	The wave function for a standing wave in a string is given by  y = 0.12 sin ( PI * x ) cos ( 4 * PI * t ), where x and y are in m and t is in s.  Find the three smallest values of x corresponding to maximum displacement of the motion (anti-nodes).	(ANS: 50 cm, 150 cm 250 cm )

Q11.	Two sinusoidal waves, having equal frequency and amplitude and traveling in the same direction, are combined.  Determine the amplitude of the resulting motion if the amplitude of each wave is 5 . 00 cm and the two differ in phase by ( PI/3 ) radians? 	(ANS: 8.7 cm )

Q12.	One end of a 120-cm string is held fixed.  The other end is attached to a weightless ring that can slide along a frictionless rod.  What are the three longest possible wavelengths for standing waves in this string? 				(ANS: 480 cm, 160 cm, 96 cm )