## Slide 1: Arithmetic Circuits 2
COE 202
Digital Logic Design
Dr. Muhamed Mudawar
King Fahd University of Petroleum and Minerals

## Slide 2: Zero versus Sign Extension
Unsigned Integers are Zero-Extended
Signed Integers are Sign-Extended
Given that X is a 4-bit unsigned integer  Range = 0 to 15
Given that Y is a 4-bit signed integer  Range = -8 to +7
If unsigned X = 4’b1101 (binary), then X = 13 (decimal)
If signed Y = 4’b1101 (binary), then Y = -3 (decimal)
If X is zero-extended from 4 to 6 bits then X = 6’b001101 = 13
If Y is sign-extended from 4 to 6 bits then Y = 6’b111101 = -3

## Slide 3: Unsigned Addition S = X + Y
Design a circuit that computes: S = X + Y (unsigned X and Y)
X[3:0] and Y[3:0] are 4-bit unsigned integers  Range = 0 to 15
Solution:
Maximum S = 15 + 15 = 30  unsigned S must be 5 bits
FA
X0
Y0
S0
0
FA
X1
Y1
S1
FA
X2
Y2
S2
FA
X3
S3
S4
Y3
c1
c2
c3
c4
c0
Most-significant sum bit S4 is the carry bit c4

## Slide 4: Signed Addition S = X + Y
Design a circuit that computes: S = X + Y (signed X and Y)
X[3:0] and Y[3:0] are 4-bit signed integers  Range = -8 to +7
Solution:
Minimum S = (-8) + (-8) = -16, Maximum S = (+7) + (+7) = + 14
Therefore, signed range of S = -16 to +14  S must be 5 bits
X and Y are sign-extended
X3 and Y3 are replicated to produce S4
FA
X0
Y0
S0
0
FA
X1
Y1
S1
FA
X2
Y2
S2
FA
X3
S3
Y3
c1
c2
c3
c0
FA
S4
c4

## Slide 5: Unsigned Subtraction S = X - Y
Design a circuit that computes S = X – Y (unsigned X and Y)
X[3:0] and Y[3:0] are 4-bit unsigned integers  Range = 0 to 15
Solution: S = X – Y = 2’s complement of Y = X + Y’ + 1
Minimum S = 0 – 15 = -15, Maximum S = 15 – 0 = +15
S is signed, even though X are Y are unsigned  S is 5 bits
X–Y = X+Y’+1
X and Y are
zero-extended.
FA
X0
Y0
S0
1
FA
X1
Y1
S1
FA
X2
Y2
S2
FA
X3
S3
FA
S4
Y3
0
1
c1
c2
c3
c4
c0

## Slide 6: Unsigned Subtraction S = X - Y
Most-significant bit: S4 = 0 + 0’ + c4 = 1 + c4 = c4’
Full Adder for S4 can be replaced by an inverter
FA
X0
Y0
S0
1
FA
X1
Y1
S1
FA
X2
Y2
S2
FA
X3
S3
S4
Y3
c1
c2
c3
c4
c0
FA
S4
0
1
c4

## Slide 7: Signed Subtraction S = X - Y
Design a circuit that computes S = X – Y (signed X and Y)
X[3:0] and Y[3:0] are 4-bit signed integers  Range = -8 to +7
Solution: S = X – Y = X + Y’ + 1
Minimum S = -8 – (+7) = -15, Maximum S = +7 – (-8) = +15
Signed range for S is -15 to +15  S is 5 bits
X–Y = X+Y’+1
X and Y are
sign-extended.
FA
X0
Y0
S0
1
FA
X1
Y1
S1
FA
X2
Y2
S2
FA
X3
S3
FA
S4
Y3
c1
c2
c3
c4
c0

## Slide 8: S = 2*X + Y (Unsigned X and Y)
Design a circuit that computes S = 2*X + Y (unsigned X and Y)
X[3:0] and Y[3:0] are 4-bit unsigned integers  range = 0 to 15
Solution:
2*X + Y = X << 1 + Y (Shift-Left X by 1 bit)
Maximum value of S = 2*15 + 15 = 45  S is 6 bits = S[5:0]
FA
X0
Y1
S1
c1
c2
c3
c4
c5
S0
Y0
0
FA
X1
Y2
S2
FA
X2
Y3
S3
FA
X3
0
S4
S5

## Slide 9: S = 2*X + Y (Signed X and Y)
Design a circuit that computes S = 2*X + Y using Full Adders
X[3:0] and Y[3:0] are 4-bit signed integers  range = -8 to +7
Solution:
Range of X and Y is -8 to +7  Minimum S = 2*(-8) + (-8) = -24
Maximum S = 2*(+7) + 7 = +21  S is 6 bits = S[5:0]
FA
X0
Y1
S1
S0
Y0
0
FA
X1
Y2
S2
FA
X2
Y3
S3
FA
X3
S4
FA
S5
c1
c2
c3
c4
c5
X and Y are
sign-extended.
Sign bits X3 and Y3 are replicated.

## Slide 10: Unsigned Less Than: LT = X < Y
Design a circuit that computes unsigned LT (unsigned X and Y)
Solution:
If (X < Y) then (X – Y) < 0, If (X == Y) then (X – Y == 0)
Do unsigned subtraction, LT = S4 = sign-bit of the result
FA
X0
Y0
S0
1
FA
X1
Y1
S1
FA
X2
Y2
S2
FA
X3
S3
LT = S4
Y3
c1
c2
c3
c4
c0
GE = c4
EQ
Equality
(X – Y == 0)

## Slide 11: Signed Less Than: LT = X < Y
Design a circuit that computes signed LT (Signed X and Y)
Solution:
If (X < Y) then (X – Y) < 0, If (X == Y) then (X – Y == 0)
Do signed subtraction, LT = S4 = sign-bit of the result
S0
S1
S2
S3
LT = S4
EQ
Equality
(X – Y == 0)
FA
X0
Y0
1
FA
X1
Y1
FA
X2
Y2
FA
X3
FA
Y3
c1
c2
c3
c4
c0
Sign Extension

## Slide 12: Design a Circuit for Unsigned S = X + Y + Z
X, Y, and Z are 4-bit unsigned integers  Range = 0 to 15
Solution: Maximum S = 15 + 15 + 15 = 45  S must be 6 bits
X[3:0]
4
Y[3:0]
4
0
4-bit Adder
cin
cout
0
5-bit Adder
cin
cout
0, Z[3:0]
5
4
5
S[5], S[4:0]
S = 6-bit Unsigned Sum
T[4]
T[3:0]
One 4-bit Adder
One 5-bit Adder
Z is zero-extended

## Slide 13: Design a Circuit for Signed S = W + X – Y – Z
W, X, Y, and Z are 4-bit signed integers  Range = -8 to +7
Solution: S = W + X – Y – Z = (W+X) – (Y+Z)  6 bits are used
W[3], W[3:0]
5
X[3], X[3:0]
5
0
5-bit Adder
cin
cout
5
1
6-bit Adder
cin
cout
6
S[5:0]
S = 6-bit Signed Sum
Sign-Bit
Extension
U[4]
U[4:0]
Two 5-bit Adders
One 6-bit Adder
Y[3], Y[3:0]
5
Z[3], Z[3:0]
5
0
5-bit Adder
cin
cout
V[4:0]
V’[4]
5
V’[4:0]
Sign bit is replicated

## Slide 14: Absolute Difference |X – Y| of Signed X, Y
Design a circuit that computes A = |X – Y| (absolute difference)
Solution: Maximum A = |X – Y| = |-8 – +7| = 15  4 bits are used
4-bit Absolute Difference
4-bit Incrementor
is implemented using Half Adders
Sign-bit extension
4
A[3:0]
X[3], X[3:0]
5
Y[3], Y[3:0]
4
S[3:0]
S[4]
4
S[4] = sign-bit of (X – Y)
4-bit Inc
cin
cout
1
5-bit Adder
cin
cout

## Slide 15: Incrementor Circuit
Incrementor
4
4
X[3:0]
Y[3:0]
cin
cout
cin
HA
X0
Y0
HA
X1
Y1
HA
X2
Y2
HA
X3
Y3
cout
c1
c2
c3
X3
X2
X1
X0
cin
c1
c2
c3
Y3
Y2
Y1
Y0
cout