COE 202, Term 151

Digital Logic Design

Assignment# 1

Due date: Tuesday, Sep. 29, 2015

# It is required to design a combinational circuit that has three inputs A, B, and C and a single output Y such that the output is set to 1 if the three inputs are equal to each other.

## Derive the equation of the circuit as a sum-of-products equation.

## Write a Verilog model to model the gate level design of the circuit using the primitive gates: AND, OR, and NOT gates. Model the delay of each gate as a function of its input i.e., the delay of a NOT gate is 1ps, the delay of a 2-input gate is 2ps, and the delay of a 3-input gate is 3ps.

## Determine the longest delay of your circuit.

## Write a test bench to test the correctness of your Verilog model by applying all the possible input patterns. Apply consecutive inputs patterns after a delay of 10ps. Verify the correctness of your computed longest delay in (iii).

## Write a second Verilog model to model the circuit using the assign statement to model the equation of the circuit. Use your computed delay in (iii) as the delay of your circuit.

## Use the test bench in (iv) to test the correctness of your second Verilog model.

This assignment can be solved based on a group of two students. The solution should be well organized. Submit a soft copy of your solution in a zip file including your Verilog models. Your solution should be submitted in a word file that contains the following items:

#### Your name and ID

#### Assignment number

#### Problem statement

#### Your solution

#### Include snapshots of simulation output to illustrate the correctness of your models.