COE 202, Term 142

Digital Logic Design

Assignment# 2

Due date: Tuesday, March 31

# It is required to design a combinational circuit that computes the equation Y=3*X, where X is a 4-bit unsigned number.

## Determine the number of outputs needed for your circuit.

## Derive the truth table of your circuit.

## Derive minimized equations for your circuit using K-Map method.

## Write a Verilog model for modeling your design by using an assign statement for each output.

## Write a Verilog test bench to test the correctness of your design for the following input values: X=1, X=3, X=5, X=10 and X=15.

## This assignment can be solved based on a group of two students. The solution should be well organized. Submit a soft copy of your solution in a zip file including your Verilog models. Your solution should be submitted in a word file that contains the following items:

## i.      Your name and ID

## ii.     Assignment number

## iii.    Problem statement

## iv.    Your solution

## v. Include snapshots of simulation output to illustrate the correctness of your models.