COE 202, Term 132

Digital Logic Design

Assignment# 2

Due date: Thursday April 17

# Q.1. It is required to design a circuit that receives a 4-bit unsigned number A=A3A2A1A0 and produces 5-bit output C= C5C4C3C2C1C0. The circuit implements the following functions based on the values of the three selection inputs: S1, S1 and S0.

| S2 S1 S0 | Function |
| --- | --- |
| 0 0 0 | C = A + B |
| 0 0 1 | C = A - B |
| 0 1 0 | C = 2*A |
| 0 1 1 | C = A + 1 |
| 1 0 0 | C = A -1 |
| 1 0 1 | C = 1 if A == B |
| 1 1 0 | C = 1 if A > B |
| 1 1 1 | C = 1 if A < B |

# Show the block diagram design of your circuit using MSI components like Adder, Multiplexor, as needed.

# Model your design in logic works.

# Test your design and verify its correctness by simulation. Show snapshots of your simulation to demonstrate its correctness. For each function, test at least 2 input combinations of your choice to demonstrate correct functionality.

Include snapshots of simulation output to illustrate the correctness of your circuit.  Submit your solution as a word document along with the circuits in one zipped file.