COE 202, Term 151

Digital Logic Design

Assignment# 2 Solution

Due date: Sunday, Oct. 31

# It is required to design an iterative combinational circuit that computes the equation Z=3*X-Y, where X and Y are n-bit unsigned numbers.

## Determine the number of inputs and outputs needed for your 1-bit cell.

The meaning of the values of C1i-1 and C0i-1 is given in the table below:

| C1i-1 | C0i-1 | Meaning |
| --- | --- | --- |
| 0 | 0 | There is no carry or borrow |
| 0 | 1 | There is a carry of 1 |
| 1 | 0 | There is a carry of 2 |
| 1 | 1 | There is a borrow of 1 |

## Derive the truth table of your 1-bit cell.

| C1i-1 | C0i-1 | Xi | Yi | C1i | C0i | Zi |
| --- | --- | --- | --- | --- | --- | --- |
| 0 | 0 | 0 | 0 | 0 | 0 | 0 |
| 0 | 0 | 0 | 1 | 1 | 1 | 1 |
| 0 | 0 | 1 | 0 | 0 | 1 | 1 |
| 0 | 0 | 1 | 1 | 0 | 1 | 0 |
| 0 | 1 | 0 | 0 | 0 | 0 | 1 |
| 0 | 1 | 0 | 1 | 0 | 0 | 0 |
| 0 | 1 | 1 | 0 | 1 | 0 | 0 |
| 0 | 1 | 1 | 1 | 0 | 1 | 1 |
| 1 | 0 | 0 | 0 | 0 | 1 | 0 |
| 1 | 0 | 0 | 1 | 0 | 0 | 1 |
| 1 | 0 | 1 | 0 | 1 | 0 | 1 |
| 1 | 0 | 1 | 1 | 1 | 0 | 0 |
| 1 | 1 | 0 | 0 | 1 | 1 | 1 |
| 1 | 1 | 0 | 1 | 1 | 1 | 0 |
| 1 | 1 | 1 | 0 | 0 | 1 | 0 |
| 1 | 1 | 1 | 1 | 0 | 0 | 1 |

## Derive minimized equations for your 1-bit using K-Map method.

Zi = C0i-1 Xi'Yi' + C0i-1 Xi Yi + C0i-1' Xi'Yi + C0i-1' Xi Yi'

= C0i-1( Xi'Yi' + Xi Yi )+ C0i-1' (Xi' Yi + Xi Yi')

= C0i-1( Xi ( Yi )' + C0i-1' (Xi ( Yi)

= C0i-1 ( Xi ( Yi

C0i = C1i-1' C0i-1' Xi + C1i-1' C0i-1' Yi + C1i-1 C0i-1 Xi' + C1i-1 C0i-1 Yi' + C1i-1 Xi' Yi' + C1i-1' Xi Yi

=  C1i-1' C0i-1' (Xi + Yi ) + C1i-1 C0i-1 ( Xi' +Yi' )+ C1i-1 Xi' Yi' + C1i-1' Xi Yi

C1i = C1i-1 C0i-1 Xi' + C1i-1 C0i-1' Xi + C1i-1' C0i-1' Xi' Yi + C1i-1' C0i-1 Xi Yi'

= C1i-1 (C0i-1 ( Xi) + C1i-1' (C0i-1' Xi' Yi + C0i-1 Xi Yi')

## Write a Verilog model for modeling your 1-bit cell by using an assign statement for each output.

module OneBit3X_Y (input C1i_1, C0i_1, Xi, Yi, output C1i, C0i, Zi);

assign Zi =  C0i_1 ^ Xi  ^ Yi ;

assign C0i  =  ~C1i_1 & ~C0i_1 & (Xi | Yi ) | C1i_1 & C0i_1 & (~ Xi | ~Yi ) | C1i_1 & ~Xi &  ~Yi | ~C1i_1 &  Xi & Yi;

assign C1i =    C1i_1 & (C0i_1 ^ Xi) | ~C1i_1 & (~C0i_1 &  ~Xi & Yi | C0i_1 & Xi & ~Yi);

endmodule

## Write a Verilog model for modeling a 4-bit circuit based on the 1-bit model you have.

module FourBit3X_Y (input [3:0] X, Y, output [3:0] Z, output C1_out, C0_out);

wire [3:0] C1, C0;

assign C1_out = C1[3];

assign C0_out = C0[3];

OneBit3X_Y M0 (1'b0, 1'b0, X[0], Y[0], C1[0], C0[0], Z[0]);

OneBit3X_Y M1 (C1[0], C0[0], X[1], Y[1], C1[1], C0[1], Z[1]);

OneBit3X_Y M2 (C1[1], C0[1], X[2], Y[2], C1[2], C0[2], Z[2]);

OneBit3X_Y M3 (C1[2], C0[2], X[3], Y[3], C1[3], C0[3], Z[3]);

endmodule

## Write a Verilog test bench to test the correctness of your design for the following input values: {X=1,Y=1},  {X=3, Y=5}, {X=5, Y=1}, {X=4, Y=15}, and {X=15, Y=0}.

module FourBit3X_Ytest();

reg [3:0] X, Y;

wire [3:0] Z;

wire C1_out, C0_out;

FourBit3X_Y M1 (X, Y, Z, C1_out, C0_out);

initial begin

X=4'd1; Y=4'd1;

#10	X=4'd3; Y=4'd5;

#10	X=4'd5; Y=4'd1;

#10	X=4'd4; Y=4'd15;

#10	X=4'd15; Y=4'd0;

end

endmodule