COE 202, Term 162

Digital Logic Design

Assignment# 3

Due date: Thursday, April 27

# It is required to design a circuit that receives two 4-bit signed numbers in 2's complement representation A=A3A2A1A0, B=B3B2B1B0 and produces a 6-bit output C= C5C4C3C2C1C0. The circuit implements the following functions based on the values of the two selection inputs: S1 and S0.

| S1 S0 | Function |
| --- | --- |
| 0 0 | C = A + B |
| 0 1 | C = A - B |
| 1 0 | C = 2A + 1 |
| 1 1 | C = 2A - 1 |

# Show the block diagram design of your circuit using MSI components like Adder, Multiplexor, as needed. Use only one adder in your solution.

# Model your design in Verilog by modeling each component separately i.e. adder, MUX, etc. and then instantiating these components to model your circuit.

# Write a Verilog test bench to test your design and verify its correctness by simulation. Show snapshots of your simulation to demonstrate its correctness. For each function, test at least 2 input combinations of your choice to demonstrate correct functionality.

This assignment can be solved based on a group of two students. Include snapshots of simulation output to illustrate the correctness of your circuit. Submit your solution as a word document along with the circuit in one zipped file.