King Fahd University of Petroleum and Minerals

College of Computer Science and Engineering

Computer Engineering Department

COE 202: Digital Logic Design (3-0-3)

Term 121 (Fall 2012)

Major Exam II

Thursday Nov. 22, 2012

Time: 150 minutes, Total Pages: 9

Name:_KEY___________________________ ID:______________ Section: _______

Notes:

- Do not open the exam book until instructed

- Calculators are not allowed (basic, advanced, cell phones, etc.)

- Answer all questions

- All steps must be shown

- Any assumptions made must be clearly stated

| Question | Maximum Points | Your Points |
| --- | --- | --- |
| 1 | 15 |  |
| 2 | 14 |  |
| 3 | 9 |  |
| 4 | 15 |  |
| 5 | 11 |  |
| 6 | 13 |  |
| 7 | 8 |  |
| Total | 85 |  |

Question 2.											      (14 Points)

We would like to design a combinational circuit that multiples two unsigned integers X and Y and produces the product as output Z, i.e. Z = XY. Each of the two integers X and Y is 2 bits. The binary representations of the input and output numbers are X1 X0 for X (X0 is the LSB), Y1 Y0 for Y (Y0 is the LSB), Zn … Z2Z1Z0 for Z (Z0 is the LSB).

Question 3.											(9  Points)

- (5 points) Draw the multi-level NAND logic diagram for the following Boolean expression, don’t simplify:

- (4 points) Using the minimum number of logic gates, draw the 2-level NOR logic diagram for the following Boolean expression:

F(A,B,C) = Σm(0, 3, 5, 6)

Question 4:	(15 points)

- (6 points) Determine the decimal value of the 7-bit binary number (1001100) when interpreted as:

| Unsigned number | Signed-magnitude number | Signed-1’s complement number | Signed-2’s complement number |
| --- | --- | --- | --- |
| 76 | -12 | -51 | -52 |

- (3 points) Find the smallest 7-bit signed-2’s complement number that can be added to the 7-bit signed-2’s complement number (1001100) without causing an overflow. Note that negative numbers are considered to be smaller than positive numbers.

From part (a), 1001100 = -52

Smallest decimal number represented using signed-2’s complement with 7 bits = -26 = -64

(	Smallest number that can be added to -52 without causing an overflow = -64 – (-52) = -12

(	Smallest 7-bit signed-2’s complement number that can be added to (1001100) without causing an overflow = 1110100

Alternative Solution:

Smallest signed-2’s complement number using 7 bits = 1000000

(	Smallest 7-bit signed-2’s complement number that can be added to (1001100) without causing an overflow = 100000 – 1001100 = 1000000 + 0110100 = 1110100

- (6 points) Perform the following signed-2’s complement arithmetic operations in binary using 5 bits. All numbers given are represented in the signed-2’s complement notation.  Indicate clearly the carry values out of the last two stages. For each of the two operations, check and indicate whether an overflow occurred or not.

| Operation | Carry value out of the 4th bit | Carry value out of the 5th bit | Overflow occurred? (Yes/No) |
| --- | --- | --- | --- |
| 01011 ( (+11) +11110 (+(- 2) 01001 ( (+ 9) | 1 | 1 | No |
| 01001 ( 01001 ( (+ 9) -10010 ( +01110 (+(+14) ( 10111 ( (- 9) | 1 | 0 | Yes |

Question 5.											(11 Points)

- (6 points) You are given one 3-to-8 decoder, one NOR gate and one OR gate to implement the two functions given below.

F1 (A,B,C) = ( M (0, 1, 4, 5, 6)

F2 (A,B,C) = ∑ m (0, 4, 6)  + ∑d( 1, 3)

Draw the circuit and properly label all input and output lines.

Solution:

Complement of F1 =  ∑ m (0, 1,  4, 5,  6)  ; Connect the outputs D0, D1, D4, D5, D6 to the input of NOR gate.

For F2, use a three input OR gate, and connect D0, D4, and D6 to its input. Treat the don’t cares are zeros (ignore them).

- (5 points) Given the truth table below for a function with four inputs (A, B, C and D) and one output F, implement F using a 4-to-1 MUX (with 2 select lines) and additional logic. Show how you obtained your solution, and properly label all input and output lines. Apply A and B to the select inputs.

| A | B | C | D | F |
| --- | --- | --- | --- | --- |
| 0 | 0 | 0 | 0 | 0 |
| 0 | 0 | 0 | 1 | 1 |
| 0 | 0 | 1 | 0 | 0 |
| 0 | 0 | 1 | 1 | 1 |
| 0 | 1 | 0 | 0 | 1 |
| 0 | 1 | 0 | 1 | 1 |
| 0 | 1 | 1 | 0 | 1 |
| 0 | 1 | 1 | 1 | 1 |
| 1 | 0 | 0 | 0 | 1 |
| 1 | 0 | 0 | 1 | 1 |
| 1 | 0 | 1 | 0 | 0 |
| 1 | 0 | 1 | 1 | 0 |
| 1 | 1 | 0 | 0 | 0 |
| 1 | 1 | 0 | 1 | 0 |
| 1 | 1 | 1 | 0 | 0 |
| 1 | 1 | 1 | 1 | 0 |

Solution:  Since AB inputs are given to select lines, we can group the truth table into 4 parts, when AB=00, AB=01, AB=10, and AB=11.

When AB=00, note that F=D;

When AB=01, note that F=1;

When AB=10, note that F=C’

When AB=11, note that F=0.

Connect, D, 1, C’ and 0 to the four inputs of the MUX.

Question 6.											     (13  points)

Assume that the delay of a 2-input XOR gate is 3ns while the delay of other gates is equal to the gate’s number of inputs, i.e. the delay of an inverter is 1ns, the delay of a 2-input AND gate is 2ns, the delay of a 2-input OR is 2ns, the delay of a 3-input AND gate is 3ns, the delay of a 3-input OR gate is 3ns, etc.

- (6 points) A 4-bit Ripple Carry Adder (RCA) is given below:

Determine and compute the longest delay in the 4-bit Ripple Carry Adder (RCA).

The longest delay is 19 ns which is along the path from {A0 B0} across the propagate XOR gate until the Cout signal.

- (4 points) Show the design of a 2-bit Carry Look-Ahead Adder (CLA) by drawing its logic diagram.

- (3 points) Using the delay assumptions given in the beginning of the question, determine and compute the longest delay in the 2-bit Carry Look-Ahead Adder (CLA).

The longest delay is 10 ns which is along the path from {A0 B0} across the propagate XOR gate until the S1

signal.

Question 7.											       (8  points)

Using a minimal number of MSI components such as: decoders, encoders, multiplexers, adders, magnitude comparators and other necessary logic gates, design a circuit that takes two 4-bit binary numbers A=A3A2A1A0 and B= B3B2B1B0 and a 2-bit user selection input S=S1S0. The circuit should produce a 5-bit output O= O4O3O2O1O0 according to the following table:

| S1S0 | O is equal to |
| --- | --- |
| 00 | A+B |
| 01 | A-B |
| 10 | A+1 |
| 11 | 2*A |