## Slide 1: Sequential Circuit Analysis & Design
Dr. Aiman H. El-Maleh
Computer Engineering Department
King Fahd University of Petroleum & Minerals

## Slide 2: Outline
Sequential Circuit Model
Timing of Sequential Circuits
Latches and Flip flops
Sequential Circuit Timing Constraints
Sequential Circuit Analysis
Sequential Circuit Design Procedure
Sequential Circuit Design Examples

## Slide 3: Sequential Circuit Model
A Sequential circuit consists of:
  Data Storage elements: (Latches / Flip-Flops)
  Combinatorial Logic:
    Implements a multiple-output function
    Inputs are signals from the outside
    Outputs are signals to the outside
    State inputs (Internal): Present State from storage elements
    State outputs, Next State are inputs to storage elements

## Slide 4: Sequential Circuit Model
Combinatorial Logic
  Next state function: Next State = f(Inputs, State)
  2 output function types : Mealy & Moore
  Output function: Mealy Circuits Outputs = g(Inputs, State)
  Output function: Moore Circuits Outputs = h(State)
Output function type depends on specification and affects the design significantly

## Slide 5: Sequential Circuit Model
Mealy Circuit
Moore Circuit

## Slide 6: Timing of Sequential Circuits Two Approaches
Behavior depends on the times at which storage elements ‘see’ their inputs and change their outputs (next state  present state)
Asynchronous
  Behavior defined from knowledge of inputs at any instant of time and the order in continuous time in which inputs change
Synchronous
  Behavior defined from knowledge of signals at discrete instances of time
  Storage elements see their inputs and change state only in relation to a timing signal (clock pulses from a clock)
  The synchronous abstraction allows handling complex designs!

## Slide 7: Data Storage Logic Structures
Feedback across Two inverting buffers Connected in series
Problem: No separate input to change data stored
Set-Reset Latch (SR-Latch)

## Slide 8: Basic NOR-NOR Set–Reset (SR) Latch
S = 1, R = 1 is a forbidden
input pattern

## Slide 9: Basic NOR-NOR Set–Reset (SR) Latch

## Slide 10: Basic NAND-NAND Set–Reset (SR) Latch
S = 1 (S’=0), R = 1 (R’=0) is a forbidden input pattern

## Slide 11: Clocked SR Latch

## Slide 12: D Latch
Now S R can not become 1 1
So we got rid of the remaining unwanted condition (SR =11 with C = 1)
This latch is transparent: with C = 1, Input D is ‘connected’ to output Q
D Latch

## Slide 13: The Transparent Latch as a Storage Element

## Slide 14: Master Slave D Flip Flop (Rising-Edge Trigerred)
When CLK=0, the master is activated and the value on D is copied to Qm. The slave is unactivated and keeps its previous value.
When CLK=1, the master is unactivated and its hold the last value stored at Qm while the slave is activated and copies the value of Qm.

## Slide 15: Another Rising Edge-Triggered D-type Flip-Flop

## Slide 16: D Flip-Flop Timing Parameters

## Slide 17: Sequential Circuit Timing Constraints
TD = worst case delay through combinational logic
TSU = FF set up time – Minimum time before the clock edge where the input data must be ready and stable
TclkQ = Clock to Q delay – Time between clock edge and data appearing at the output of the FF
THold = FF hold time – Minimum time after the clock edge where data has to remain stable (held stable)
Based on the FF & combinational logic timing parameters, the following timing constraints are obtained for correct operation of the circuit: Tclk ≥ Tclkq1 + TD + Tsu

## Slide 18: State Initialization
When a sequential circuit is turned on, the state of the flip flops is unknown (Q could be 1 or 0)
Before meaningful operation, we usually bring the circuit to an initial known state, e.g. by resetting all flip flops to 0’s
This is often done asynchronously through dedicated direct S/R inputs to the FFs
It can also be done synchronously by going through the clocked FF inputs

## Slide 19: Sequential Circuit Analysis

## Slide 20: Sequential Circuit Analysis
Given a sequential Circuit
Objective: Derive outputs & state behavior (outputs and next state) from (present states and inputs)
Two equivalent approaches to represent the results:
  State table: A truth table-like approach
  State diagram: A graphical, more intuitive way of representing the state table and expressing the sequential circuit operation

## Slide 21: State Table Characteristics
State table – a multiple variable table with the following four sections:
   CL Inputs:
  Present State – the values of the state variables for each allowed state (FF outputs)
  External Inputs
   CL Outputs:
  Next-state – the value of the state (FF outputs) at time (t+1) based on the present state and the inputs. Determined by FF inputs
  Outputs – the value of the outputs as a function of the present state and (sometimes- Mealy) the inputs.

## Slide 22: Sequential Circuit Analysis Example

## Slide 23: Sequential Circuit Analysis Example

## Slide 24: Sequential Circuit Analysis Example

## Slide 25: Sequential Circuit Analysis Example

## Slide 26: Moore and Mealy Models

## Slide 27: Moore Sequential Circuit Analysis Example

## Slide 28: Sequential Circuit Design Procedure
1. Specification – e.g. Verbal description
2. Formulation – Interpret the specification to obtain a state diagram and a state table
3. State Assignment - Assign binary codes to symbolic states
4. Flip-Flop Input Equation Determination - Select flip-flop types and derive flip-flop input equations from next state entries in the state table
5. Output Equation Determination - Derive output equations from output entries in the state table
6. Verification - Verify correctness of final design

## Slide 29: Example: Bit Sequence Recognizer 1101
1. Specifications: Detect the occurrence of bit sequence 1101 whenever it occurs on input X and indicate this detection by raising an output Z high
2. Formulation: State Diagram

## Slide 30: Example: Bit Sequence Recognizer 1101
From the State Diagram, we can fill in the 2-D State Table
There are 4 states, one input, and one output.
Two dimensional table with four rows, one for each current state.
State Diagram
State Table

## Slide 31: Example: Bit Sequence Recognizer 1101
3. State Assignment: From abstract symbols to binary bit representation of states
Each of the m symbolic states must be assigned a unique binary code
Minimum number of state bits (state variables) (FFs) required is nb, such that 2nb ≥ ns
If 2nb > ns, this leaves (2nb – ns) unused states
Utilize them as don’t care conditions to simplify CL design
But may need caution: e.g. what if the circuit enters an unused state by mistake
nb= log2 ns.

## Slide 32: Example: Bit Sequence Recognizer 1101
Also which code is given to which state?  different CL implementations  may influence optimization, e.g. (with 2 FFs) State A is assigned 00 or 01 or 10 or 11?
There are possible encodings = 16
Let A = 00 (to suit being a Reset state), B = 01, C = 11, D = 10

## Slide 33: Example: Bit Sequence Recognizer 1101
For optimization of FF input equations we express A(t+1), B(t+1), Z(t) in terms of A(t), B(t) and X(t) (using one dimensional state table)

## Slide 34: Example: Bit Sequence Recognizer 1101

## Slide 35: State Diagram (Moore Model)

## Slide 36: Sequential Circuit Design: Serial Comparator
It is required to design a sequential circuit that compares two n-bit numbers A=An-1A2A1A0 and B=Bn-1B2B1B0, applied to the sequential circuit serially from the least significant bits to the most significant bits.
The circuit produces two outputs GT and LT.
  If A>B, then output signal GT is set to 1 and LT is set to 0.
  If A<B, then output signal LT is set to 1, and GT is set to 0.
  Otherwise, both signals will be set to 0, which indicates that the two numbers are equal (i.e. A=B).

## Slide 37: Sequential Circuit Design: Serial Comparator

## Slide 38: Sequential Circuit Design: Serial Comparator

## Slide 39: Sequential Circuit Design: Y = 3*x + 1
It is required to design a sequential circuit that has a single input X and a single output Y.
The circuit receives an unsigned number serially through the input X from the least significant bit (LSB) to the most significant bit (MSB), and computes the equation Y=3*X+1 and generates the output serially from the least significant bit to the most significant bit.

## Slide 40: Sequential Circuit Design: Y = 3*x + 1
State Diagram

## Slide 41: Sequential Circuit Design: Y = 3*x + 1

## Slide 42: BCD to Excess-3 Serial Code Converter
Assume that once the machine is reset, a continues stream of BCD digits will be transmitted serially and converted to Excess-3 digits.

## Slide 43: BCD to Excess-3 Serial Code Converter
State Diagram
State Table

## Slide 44: BCD to Excess-3 Serial Code Converter

## Slide 45: BCD to Excess-3 Serial Code Converter
Karnaugh maps for the encoded state bits and output bit (Bout)

## Slide 46: BCD to Excess-3 Serial Code Converter