May 30, 2006

COMPUTER ENGINEERING DEPARTMENT

COE 202

FUNDAMENTALS OF COMPUTER ENGINEERING

Final Exam

Second Semester  (052)

Time: 7:30-10:30 AM

Student Name : ______________________________________________

Student ID.     : ______________________________________________

| Question | Max Points | Score |
| --- | --- | --- |
| Q1 | 20 |  |
| Q2 | 20 |  |
| Q3 | 15 |  |
| Q4 | 10 |  |
| Q5 | 10 |  |
| Q6 | 10 |  |
| Q7 | 15 |  |
| Total | 100 |  |

Dr. Aiman El-Maleh

[20 Points]

# (Q1) Consider the circuit shown below that has two inputs A, B, and two outputs X , Y:

## (i) Draw the timing diagram for the outputs X and Y given the waveforms for the inputs A and B shown below. Assume that Y is initially having the value 0.

## (ii) Does this circuit implement a latch or a flip-flop, and what type? Justify your answer. Indicate what A, B, X, and Y represent.

## (iii) Show the design of a positive-edge-triggered T flip-flop using SR latches.

## (iv) Show the design of a positive-edge-triggered JK flip-flop using a positive-edge-triggered T flip-flop.

# [20 Points]

# (Q2) It is required to design a sequential circuit that receives a serial input X, and produces a serial output Z, equivalent to 3*X, i.e., Z=3*X. The state diagram for this circuit is shown below:

## Implement the sequential circuit using JK-FFs and the smallest number of gates possible assuming the state assignment: S0=00, S1=01, and S2=10.  Show the state table and minimize your equations using K-map method.

# [15 Points]

(Q3)  A sequential circuit has two D flip-flops A and B, two inputs X and Y, and one output Z. The flip-flop input equations and output function are as follows:

DA = B X  + A Y`

DB = A` X + B` Y

Z   = X A B

## (i)  Show the implementation of this circuit using a ROM and D-FFs. Determine the size of the ROM that will be used and show the ROM table.

## (ii)  Obtain the state diagram for this circuit.

[10 Points]

# (Q4) Implement the following two functions with a PLA:

F1(A, B, C, D)=m(1, 2, 3, 5, 6, 7, 10, 11, 14, 15)

F2(A, B, C, D)=m(0, 1, 4, 5, 9, 10, 13, 14)

# Minimize the number of product terms used in the PLA. Show the internal logic of the PLA that will be used to implement these two functions.

[10 Points]

## (Q5) A single-input, single-output sequential circuit is to be designed that recognizes the input sequence 01101 applied to its input any time it occurs in the input stream starting from a reset state. If the sequence is detected the output will be 1, otherwise it will be 0. Show the state diagram for this circuit assuming detection of overlapping sequences assuming a Mealy model. As an example, the input stream 01101101101 will produce the output stream 00001001001.

[10 Points]

# (Q6) It is required to design a sequential circuit that has one serial input stream X and produces a serial output stream computing the 2’s complement of X. Obtain the state diagram for this circuit assuming a Moore  model.

[15 Points]

## (Q7) It is required to design a synchronous 3-bit up-down counter using positive-edge-triggered D-FFs. The counter has two inputs E and M. If E=0, the counter remains in the same state, regardless of the value of M. When E=1 and M=1, the counter counts up, and when E=1 and M=0, the counter counts down. Show the logic required to make the counter have Synchronous Reset, RESET. When RESET=1, the counter is reset to 0.

# Text boxes

Y

X

B

A

G3

G2

G1

A

Y

X

1/1

1/0

0/0

0/1

0/0

1/1

S2

S1

B

S0