## Slide 1
COE 202: Digital Logic Design
Courtesy of Dr. Radwan E Abdel-Aal
Registers and Counters

## Slide 2: Registers and Counters Useful MSI blocks made of Flip-Flops
Registers with Parallel Load
Shift Registers
Counters: Synchronous and Asynchronous
Modulo Counters

## Slide 3: Registers
Register – a collection of binary storage elements
In theory, a register is sequential logic, i.e. can be defined by a state table
But more often, we think of a register as an array of n flip flops (possibly with some extra gates) that store a vector of n binary bits
Used to perform simple data storage, movement, manipulation and processing operations (e.g. load, increment, shift, add, etc.)
The computer processes data by performing operations on registers, e.g. ADD A, B where A and B are say 32-bit registers

## Slide 4: Register/Counter Design Methods
Classical Direct Approach: From State Diagram
  Design individual cells using the state diagram/state table model and combine them into a register
Problem: for n large  large number of states  state diagram/state table model is often not feasible!- Pentium has 64-bit data registers (states = ?)
Alternative (Ad hoc?) Approach: (similar to iterative design method in combinational logic)
  Add predefined combinational circuits to a register to perform desired functions
    Example: To count up, connect the register flip-flop outputs to an incrementer

## Slide 5: Example: 4-bit Register, with Clear & Selective Parallel Load by clock gating
Reset (Cleared)
Asynchronously with
A 0 pulse on the normally
High Clear input
Loaded with
Data at inputs
at every clock edge
D  Q
What is the problem
with this?
You need a controlled
loading, only when input
data is valid and a Load
Signal arrives
(not on every clock pulse!)
Solution: Gate the clock to the
Register flip flops so that clock
Pulses arrive only when Load = 1
Clock input to FFs
D3-D0
Data to be loaded
Q
Notes: States: 22 = 4
Input Combinations: 22 = 4
Output Combinations: 22 = 4
Y = A
A(t+1) = IN
Moore
States = 2n
Input Combinations = 2n
Output Combinations = 2n

## Slide 6: Further Improvement Avoid clock gating. Apply Load control to D input
Avoid clock gating if you can!
It causes clock skew – clock arriving to various flip flops in the system at different times
So such flip flops change state at different times
No good- could lead to erroneous state transitions!
Load does not gate the clock,
But controls what goes into the D input
Load = 1  EN = 1, D = input data to be loaded
on next clock edge
Load = 0  EN = 0, D = present Q, so no change
on next clcok edge
EN = 1 for Load
EN = 0 for no Load
External Data
to be loaded
Clock pulses go
Always Unhindered
To all FFs
But we control what
Clock pulses do using
The EN control on D
D3-D0
Data to be loaded
Notes: States: 22 = 4
Input Combinations: 22 = 4
Output Combinations: 22 = 4
Y = A
A(t+1) = IN
Moore
States = 2n
Input Combinations = 2n
Output Combinations = 2n

## Slide 7: Shift Registers
Shift Registers move data laterally () within the n-bit register toward its MSB or LSB position
In the simplest case, the shift register is simply a set of D flip-flops connected in a row like this:
Data input, In, is called a serial input or the shift right input.
Data output, Out, is often called the serial output (=D).
The vector (A, B, C, D) is called the parallel output.
Serial
Serial
D
Shift Right
Shift Left

## Slide 8: Shift Registers
Behavior of the 4- stage serial shift
register
Initial register state just before the first clock pulse arrives
T1: State after the first pulse and before the second
Initially unknown states are denoted
by “?”
Complete the last three rows of the table
D
Q
D
Q
D
Q
D
Q
In
Clock CP
A
B
C
Out
CP
In
A
B
C
D, Out
0
?
?
?
?
T1
1
0
?
?
?
T2
1
1
0
?
?
T3
0
1
1
0
?
T4
1
T5
1
T6
1
0
1
1
0
2. Serial I/P
starts
appearing
Serially
at O/P
0
1
1
After 4
Clock
Pulses:
1. Serial I/P
Appears
in parallel
In register
Problem: Serial loading takes n clock cycles-
Possible Improvements: Load in parallel?
Notes: ROW T4: 10110
Row T5: 11011
Row T6: 11101

## Slide 9: Some Shift Register Applications
Delaying:
 input sequence appears at output after n-clock cycles
Parallel to serial (and Serial to parallel) conversion
Arithmetic:
 Shifting one bit to the right causes dividing by ?
 Shifting one bit to the left (inserting 0s) causes multiplying by ?
n–bit
Shift Register
Lateral Shift
Parallel Load
n
n–bit
Shift Register
Parallel Read
n
Serial Link
e.g. Ethernet
101100000010110
Notes: ROW T4: 10110
Row T5: 11011
Row T6: 11101

## Slide 10: Shift Register with Parallel Load
ddd
Parallel Input
Serial
Out
Qi  Qi
i = 0,1,..,3
Di  Qi
Serial Input  Q0
Q(i-1)  Qi; i=1,…,3
D input
Selection hardware-
Could use a MUX here!

## Slide 11: Bi-directional Shift Register with Parallel Load
Parallel Data I/P
4-to-1
MUX
Info Inputs
Select Inputs
Mode
Select

## Slide 12: Counters
A counter is a register that has its parallel outputs "count" through a specific state sequence
Sequences can be binary, BCD, etc.
Counting can be up, down
A modulo-n counter goes through values 0,1,2, …, (n-1)
e.g. modulo-10 up counter counts: 0,1,…9
Some Applications:
Frequency division
Event counting
Timers
000
001
010
011
100
101
000
001
Successive
Clock
Pulses
ABC (LSB)
This is a modulo-?
Up/Down? Counter

## Slide 13: Implementing Counters Two Basic Approaches
1. Asynchronous (Ripple) Counters
  The external clock is connected to the flip-flop clock input of the LSB bit flip-flop (first counter stage)
  For all subsequent stages, the clock input is derived from the output of the preceding stage,
  i.e. circuit is not truly synchronous- no common clock to all stages
  Advantage:
  - Simpler circuit, lower power consumption
  Disadvantages:
  - Output change delayed further for each stage toward the MSB
  - Max clock frequency limited by this ripple propagation delay

## Slide 14: Ripple Up and down Counter Modulo-16 binary counter (n = 4)
 How to get an Up/Down counter?
In-stage
Toggling link
Inter-stage
Clocking
link
Toggle at
+ ive edge
on Q0
Connect
Q to
next C
Toggle at
- ive edge
on Q0
Connect
Q to
next C
Worst-case
Ripple delay
of 4 tPHL
Up
Down
fc = Clock Frequency
fc/2
fc/4
fc/8
fc/16
Frequency Division
Every Stage Toggles

## Slide 15: Ripple Up Counter 2-bit counter (modulo 4: Counts: 00,01,10,11
How does it work?
  At the positive edge on the external clock input of A, A toggles
  The clock input for flip- flop B is the complemented output of flip-flop A
  When flip A changes from 1 to 0, there is a positive edge on the clock input of B causing B to complement it toggles
Reset
External
Clock, f Hz
D
D
CR
CR
B
A
CP
QB
QA
0
1
2
3
0
1
00
01
10
11
2 Toggling stages- each is modulo-2 i.e. divide by 2
Q (i-1)
to Clk (i)
0 1 0 1 0
0 0 1 1 0 0
Toggle
Every CP
Toggle
Every 2 CPs
f/2 Hz
f/4 Hz
+ive
edges
On Q
LSB

## Slide 16: Ripple Counter (continued) Ripple delay: may limit max clock frequency
These are called ripple counters because in order to toggle, each stage waits for a change in the output of the previous stage edge
Such changes “ripple” through the chain of flip-flops, i. e., each transition occurs after a clock-to-output delay from the stage before
For long ripple counters, total ripple delay to last stage may limit max usable clock frequency (Clock width must be > delays)

## Slide 17: Implementing Counters
2
Synchronous Counters
  System clock is connected directly to the clock inputs of ALL flip-flops (truly synchronous)
  Combinational logic is used to implement the desired state sequencing as inputs to the D inputs of the flip-flops

## Slide 18: Synchronous Counters No fiddling with clock inputs- Go through the Ds
Avoid “clock ripple" limitations:
 A common clock to all flip-flops
+ A combinational circuit
to generate the next state
For an up-counter, use a combinational logic
incrementer that operates
on the present Q outputs
to calculate the next counter
state and feed it to the Ds)
An incrementer is a reduced (contracted) form of the full n-bit adder
D3
Q3
D2
Q2
D1
Q1
D0
Q0
Clock
(common to all stages)
Incrementer
(CL)
A3
A2
A1
A0
Y3
Y2
Y1
Y0
Present
Count
Next
Count
(When clock pulse comes)
+1
Go through the Ds
Not the clock

## Slide 19: Synchronous Counters with incrementer: Serial and Parallel Implementations
Incrementer is a contraction
of the 4-bit ripple adder,
with +0001 (count up)
or +0000 (do not count)
“000” led to the reduced
Adder logic shown
This is the EN input
Carry propagation module
 Speed limitation due to
carry ripple
For faster performance
Replace this module with
a carry lookahead module
Generates C’s fast from
available Qs, EN directly
C1
C2
C3
CO
0
No count, 0 at input of all XORs
 Di = Qi (No change on next CP)
Serial Counter
Parallel Counter
Sum

## Slide 20: Synchronous Counter with Parallel Load
Add path for input data
  Enabled for Load = 1
Add logic to:
  Disable count logic for Load = 1
  Disable feedback from outputs for Load = 1
  Enable count logic for Load = 0 and Count = 1
The resulting function table:
D
0
D
C
Q
0
D
1
D
C
Q
1
D
2
D
C
Q
2
D
3
D
C
Q
3
Load
Count
Clock
Carry
Output CO
Load | Count | Action
0 | 0 | Hold last count (No change)
0 | 1 | Increment current count
1 | X | Parallel Load D0-D3
0
1
0
1
0
0: Not Counting
(Enable feedback)
1: Counting
(Enable incrementer)
Error in Fig. 7-14

## Slide 21: Ideas for Up/Down Synchronous Binary Counting EN = 1 for counting, S: 0 = Up , 1 = Down
Use an incrementer/decrementer hardware reduced for adding/subtracting only 1. Output of the hardware feeds the D inputs of the counter flip-flops
Or: Derive next state from previous state from observations
- Verify that the following works:
EN
S
Up/Down
Counter
Count Enable
Count Direction
Q0
Q1
Q2
Q3
;Always toggles if counting, either directions (no S)
No change if counting disabled
(EN = 0)
EN = 1, Up (S=0): Q1 toggles if Q0=1, otherwise no change
Down (S=1): Q1 toggles if Q0=0, otherwise no change
S= 0 Up
S= 1 Down
Next state of a stage
is determined by present state of that stage and all preceding stages

## Slide 22: Modulo N (i.e. divide by N) Counters N counting states: 0, 1, 2, …, (N-1)
 The following techniques use an n-bit (2n >= N) binary counter with synchronous clear or parallel load:
  Detect terminal count (N – 1) and use to synchronously Clear the counter to 0 (first count) on next clock pulse
  Detect terminal count (N – 1) in to synchronously Load in the value 0 (first count) on next clock pulse
Caution: Note that in the cases above, asynchronous Clear or load is problematic, as the terminal count removes itself immediately (not at the next clock cycle) and therefore may not have a chance to exist!
 Alternatively, custom design a modulo N counter as a sequential circuit (FSM)

## Slide 23: Modulo 7 (0,1,…,6): Synchronously Load 0 on Terminal Count 6
Synchronous 4-bit binary counter with a synchronous load and an asynchronous clear is used to make a Modulo 7 counter
Detect the end count "6" and use to load in the start count "zero"
This gives the count sequence
0, 1, 2, 3, 4, 5, 6, 0, 1, 2, 3, 4, 5, 6, ...etc.
Note: states beyond 6 do not occur, and therefore Q1 Q2 = 11 uniquely define count 6 and it is enough to detect it for sync loading of 0 (no need to decode it as 110).
D3
Q3
D2
Q2
D1
Q1
D0
Q0
CLEAR
CP
LOAD (Synchronous)
Clock
0
0
0
0
Reset
0000 0
0001 1
0010 2
0011 3
0100 4
0101 5
0110 6
Q3 Q2 Q1 Q0
Q2 Q1 = 11
Only here!
First
Count
For //L
Load
End
Count
Detection

## Slide 24: Modulo 6: 9,10,11,12,13,14 (do not have to start from 0!) Detect count 14 to synchronously load 9
Use a synchronous, 4-bit binary counter
Note the counter must cover
the states needed (9-14)
So, although we use only
6 states, a 3-bit counter
is not enough (does not
cover counts 9-14)
Since the counter does not
use state 0, “Clear” is meaningless!
Preset is taken to mean as “go to first count” and therefore invokes a synchronous parallel load of 9

## Slide 25: Designing Synchronous Counters as Sequential Circuit (Finite State Machines (FSM))
The above methods of counter design were somewhat ad hoc
They suit simple counting schemes, e.g. binary up, down, etc.
But here we generalize….
We treat a counter as a FSM in its own right and use formal FSM design methods
Use sequential logic design methods (Unit 4-Chapter 6) to build a synchronous counter from a number of D flip-flops
and combinational logic (CL) as required
Counts can now assume any values- do not have to be even successive, since next count is considered as an arbitrary next state
Will give two examples, including a BCD (0-9) counter

## Slide 26: Example 1: Synchronous BCD Counter (0-9) Modulo ? Divide-by ?
For Divide-by N applications, we need an output that gives one pulse equal to the clock period every counting cycle (i.e. every N pulses)- Here N = 10
This is the additional (external) output Y
Q2 has a pulse that is 2 clock periods wide, Q4: 4 periods wide
Use K-Maps to optimize next state and Y equations and manipulate into forms containing XOR gates:
Note new naming for Qs
Optimize CL for D1, D2, D4, D8, and Y
using Five 4-variable K-maps for optimizing
Time duration of this “1” pulse?
These 2 O/Ps also have a single one pulse- but…
How many FFs?, Available States?
Unused state?

## Slide 27: BCD Counter, Contd.: State Diagram, Handling unused states
From the FF input equations determine the actual values of the six next states for the don’t care combinations from the equations
Find the overall state diagram to assess behavior for the don’t care states (states shown in decimal)
Present State | Next State
Q8 Q4 Q2 Q1 | Q8 Q4 Q2 Q1
1 0 1 0 | 1 0 1 1
1 0 1 1 | 0 1 1 0
1 1 0 0 | 1 1 0 1
1 1 0 1 | 0 1 0 0
1 1 1 0 | 1 1 1 1
1 1 1 1 | 0 0 1 0
0
1
8
7
6
5
4
3
2
9
10
11
14
15
12
13
If the circuit finds itself in an unused state you want to
make sure it returns safely to a used state, i.e. does not,
say, get stuck within unused states (self-correcting).
How many clock pulses
Are needed to ‘go home’ ?
Determined by how you utilized your don’t cares!
(whether you considered each X as 1 or 0)
If so, is it
Acceptable?
Normal states do not lead
to unused states

## Slide 28: Example 2: Counter with Arbitrary Count Sequence: i.e. not straight binary
For Unused states:
Determine transitions
From circuit
Three 3-variable K-maps
for CL Optimization
Modulo?
Count
Sequence?
Number
of states?
Number of FFs?
Unused states?
Missing?