Name:									Id#

COE 200, Term 041

Fundamentals of Computer Engineering

Quiz# 1

Date: Monday, Oct 4 (8:00-9:00AM)

# Q1. Represent the following numbers in binary and hexadecimal. Use as many bits as needed, and approximate the fraction to 4 binary digits:

## (120.3)10

## (32.3)5

# Q2. Assume that an 8-bit register contains the following number 11010100. Determine the content of the register assuming that it represents:

## an unsigned number.

## a 2’s complement signed number.

# Q3. Perform the following operations assuming that numbers are represented using 8-bits assuming r’s complement representation, and determine if there is an overflow or not:

## 11110000 + 11111101

## 6A -  F0

# Q4.  Determine, in binary and decimal, the smallest (negative) number and the largest (positive) number that can be stored using the 2`s complement notation, assuming 6-bit representation.