Name:									Id#

COE 200, Term 001

Fundamentals of Computer Engineering

Quiz# 1

Date: Saturday, September 23

# Q1. Represent the following numbers in binary and hexadecimal. Use as many bits as needed, and approximate the fraction to 4 binary digits:

## (2699.32)10

## (44.44)5

# Q2. Determine the radix R that satisfies the following: (365)R = (194)10.

# Q3. Consider the following two numbers A=-98 and B= 33:

## a. Express the two numbers in 1`s complement and 2`s complement notations, assuming 8-bit representation.

## Perform the operation A-B two times, once using 1`s complement notation and once using 2`s complement notation.

## Determine, in binary and decimal, the smallest (negative) number and the largest (positive) number that can be stored using the 2`s complement notation, assuming 12-bit representation.