Name:									Id#

COE 200, Term 993

Fundamentals of Computer Engineering

Quiz# 1

Date: Sunday, June 18

# Q1. Represent the following numbers in binary and hexadecimal. Use as many bits as needed, and approximate the fraction to 3 digits:

## (250.375)10

## (11.2)3

# Q2. Determine the value of a 3-digit number in base 2R, i.e. (d2d1d0)2R that is equivalent to the 3-  digit number (421)R in base R.

# Q3. Consider the following two numbers A=-100 and B=-125:

## a. Express the two numbers in 1`s complement and 2`s complement notations, assuming 8-bit representation.

Perform the operation A-B two times, once using 1`s complement notation and once using 2`s complement notation.

## Determine, in binary and decimal, the smallest (negative) number and the largest (positive) number that can be stored using the 2`s complement notation, assuming 6-bit representation.