Name:									Id#

COE 200, Term 001

Fundamentals of Computer Engineering

Quiz# 3

Date: Saturday, Nov. 4

# Q.1. Implement the following Boolean function F(A, B, C, D)=A` C` + B C` + A` D + B D using only:

## (i) Four 2x4 decoders and four 3-input OR gates.

## (ii) Three 2x1 multiplexers.

# Q.2. It is required to design a Combinational circuit that compares two n-bit numbers, A=An-1-A0 and B=Bn-1-B0, to check if A is less than B or not. Design a circuit that has three inputs and one output, that can be used for each of the n bits, such that the circuit is connected in cascade by carry-like signals. One of the inputs to each circuit is a carry input, and the single output is a carry output. If the final output from the last circuit is 1, then this indicates that A is less than B, otherwise A is greater than or equal to B. Using this circuit, show the design of a 4-bit less than comparator.