Name: 										Id#

COE 202, Term 102

Fundamentals of Computer Engineering

Quiz# 5 (Take Home)

Due date: Saturday, May 7, 2011

# Q.1. It is required to design a 4-bit arithmetic and logic unit that has two 4-bit inputs A=A3A2A1A0 and B=B3B2B1B0 and one 6-bit output C= C5C4C3C2C1C0. The circuit implements the following functions based on the values of the four selection inputs S3, S2, S1 and S0.

| S3 S2 S1 S0 | Function |
| --- | --- |
| 0 0 0 0 | C = A + B |
| 0 0 0 1 | C = A – B |
| 0 0 1 0 | C = A+1 |
| 0 0 1 1 | C = A-1 |
| 0 1 0 0 | C = A+ 2 |
| 0 1 0 1 | C = A – 2 |
| 0 1 1 0 | C = B |
| 0 1 1 1 | C = -B |
| 1 0 0 0 | C = 2B |
| 1 0 0 1 | C = 3B |
| 1 0 1 0 | C = 4B |
| 1 0 1 1 | C = A and B |
| 1 1 0 0 | C = A or B |
| 1 1 0 1 | C = A xor B |
| 1 1 1 0 | C = A xnor B |
| 1 1 1 1 | C = not B |

# Show the block diagram design of your circuit using MSI components like Adder, Multiplexor, as needed.

# Model your design in logic works.

# Test your design and verify its correctness by simulation. Show snapshots of your simulation to demonstrate its correctness. For each function, test at least 4 input combinations of your choice to demonstrate correct functionality.

Submit your solution as a word document along with the circuits in one zipped file.