Name: KEY										Id#

COE 202, Term 052

Fundamentals of Computer Engineering

Quiz# 5 (Take Home)

Due date: Monday, April 17, 2006

# Q.1. Assume the delay of a gate is equal to the number of its inputs, i.e. the delay of a 2-input gate is 2, and the delay of a 3-input gate is 3. Using Logic works do the following:

## Model a full-adder.

## Use the full adder model and construction from it an 8-bit Ripple Carry Adder.

In order to simplify the modeling process, we will create a symbol for the full adder cell and then connect 8 copies of it as shown below. We first connect input and output ports then create the symbol.

The simulation waveform that illustrates that the adder works properly is shown below:

## Determine the worst case delay in your 8-bit Ripple Carry Adder by simulation.

The worst case delay is when the A & B inputs have propoagation condition and the Cin signal is changing from 0 to 1 or from 1 to 0. The Cout signal will change accordingly after a delay equal 2+4*8=34 ns. This is exactly what is obtained by simulation as shown below.

As can be seen, the delay from the Cin signal to the Cout signal is 544-510= 34ns.

## Model a 4-bit Carry Look Ahead adder.

The 4-bit carry look ahead adder is modeled as shown below.

P0 = A0 ( B0 ;	G0= A0 AND B0

S0 = P0  ( C0

C0 = G0 + C0 P0

P1 = A1 ( B1 ;	G1= A1 AND B1

S1 = P1  ( C1

C1 = G1 + G0 P1 + C0 P0 P1

P2 = A2 ( B2 ;	G2= A2 AND B2

S2 = P2  ( C2

C1 = G2 + G1 P2 + G0 P1 P2 + C0 P0 P1 P2

P3 = A3 ( B3 ;	G3= A3 AND B3

S3 = P3  ( C3

C3 = G3 + G2 P3 + G1 P2 P3 + G0 P1 P2 P3 + C0 P0 P1 P2 P3

## Simulate the following values to verify that your adder works properly: 3+4, -1-7, 3+1, 2+5, 3+3.

## Determine the longest delay in the 4-bit Carry Look Ahead adder by simulation.

The longest delay will 2+5+5=12ns. This is as verified by simulation shown below from the time the propagation condition is met until the carry out appears = 33-21=12 ns..

## Construct an 8-bit adder by connecting two 4-bit Carry Look Ahead adders together.

The 8-bit adder based on two 4-bit CLA adders is shown below:

## Determine by simulation the longest delay in the 8-bit adder in (g).

The worst case delay is 12 (first block) + 10 (2nd block) = 22. This is exactly what is obtained by simulation as shown below = 113-91=22.

Q.2. It is required to design a BCD adder to perform addition in BCD representation.

## Model a single-digit BCD adder.

## Using the single digit BCD adder, build a 3-digit BCD adder.

## Verify the correct functionality of the 3-digit BCD adder by simulating the following operations: 999 + 1, 999+222, 100+999, 279+465

999 + 1 = 1000

999 + 222 = 1221

100+999 = 1099

279+465 = 744

Q.3. [1% Bonus]

## Model a 4-bit multiplier.

## Verify the correct functionality of the 4-digit multiplier by simulating the following operations: 15 * 1, 15*0, 5*5, 2*8, 8*7, 15*15.

15*1=15=0FH

15*0=0

5*5=25=19H

2*8=16=10H

8*7=56=38H

15*15=225=E1H