Name: 										Id#

COE 202, Term 052

Fundamentals of Computer Engineering

Quiz# 6

Date: Saturday, April 29, 2006

# Q.1. Implement the following Boolean function F(A,B,C)=A B C+A B’ C’+A’ B C’+A’ B’ C with the minimum possible gates using only:

## (i) 2x4 decoders (with or without enable), 2-input OR gates and inverters.

## (ii) 2x1 multiplexers and inverters.