Name: 										Id#

COE 202, Term 102

Fundamentals of Computer Engineering

Quiz# 6

Due date: Saturday, May 14, 2011

# Q.1. Show the design of a clocked D-latch using only Nand gates and inverters.

# Q.2. Show the design of a rising-edge triggered D-flip flop using master-slave D-latches.

# Q.3. Design a rising-edge triggered JK flip flop using a rising-edge triggered T flip flop.

# Q.4. Derive the state diagram of the following sequential circuit with input X and output Z. Determine whether the machine is Mealy or Moore.