Name: KEY										Id#

COE 202, Term 102

Fundamentals of Computer Engineering

Quiz# 6

Due date: Saturday, May 14, 2011

# Q.1. Show the design of a clocked D-latch using only Nand gates and inverters.

# Q.2. Show the design of a rising-edge triggered D-flip flop using master-slave D-latches.

# Q.3. Design a rising-edge triggered JK flip flop using a rising-edge triggered T flip flop.

| Q | J | K | Q+ | T |
| --- | --- | --- | --- | --- |
| 0 | 0 | 0 | 0 | 0 |
| 0 | 0 | 1 | 0 | 0 |
| 0 | 1 | 0 | 1 | 1 |
| 0 | 1 | 1 | 1 | 1 |
| 1 | 0 | 0 | 1 | 0 |
| 1 | 0 | 1 | 0 | 1 |
| 1 | 1 | 0 | 1 | 0 |
| 1 | 1 | 1 | 0 | 1 |

# T = Q’ J + Q K

# Q.4. Derive the state diagram of the following sequential circuit with input X and output Z. Determine whether the machine is Mealy or Moore.

# The machine is Moore machine as the output depends only on the current state and does not depend on the input. The next state and output equations are as follows:

DA = QA X’ + QB’ X

DB = QA X + QB X’

Z = QA ( QB

The state diagram is as follows: