## Slide 1: Binary Arithmetic
COE 233
Digital Logic and Computer Organization
Dr. Muhamed Mudawar
King Fahd University of Petroleum and Minerals

## Slide 2: Presentation Outline
Binary and Hexadecimal Addition and Subtraction
Binary Multiplication and Bit Shifting
Signed Integers
Range, Overflow, Converting Subtraction into Addition

## Slide 3: Adding Bits
1 + 1 = 2, but 2 should be represented as (10)2 in binary
Adding two bits: the sum bit is S and the carry bit is C
Adding three bits: the sum bit is S and the carry bit is C
X
+ Y
C S
0
+ 0
0 0
0
+ 1
0 1
1
+ 0
0 1
1
+ 1
1 0
1
0
+ 0
0 1
1
0
+ 1
1 0
1
1
+ 0
1 0
1
1
+ 1
1 1
0
0
+ 0
0 0
0
0
+ 1
0 1
0
1
+ 0
0 1
0
1
+ 1
1 0

## Slide 4: Binary Addition
Start with the least significant bit (rightmost bit)
Add each pair of bits
Include the carry in the addition, if present
0
0
0
1
1
1
0
1
0
0
1
1
0
1
1
0
+
(54)
(29)
(83)
1
carry
0
1
2
3
4
bit position:
5
6
7
1
1
1
0
1
0
1
0
0
1
1

## Slide 5: Subtracting Bits
Subtracting 2 bits (X – Y): we get the difference (D) and the borrow-out (B) shown as 0 or -1
Subtracting two bits (X – Y) with a borrow-in = -1: we get the difference (D) and the borrow-out (B)
X
– Y
B D
0
– 0
0 0
0
– 1
-1 1
1
– 0
0 1
1
– 1
0 0
-1
0
– 0
-1 1
-1
0
– 1
-1 0
-1
1
– 0
0 0
-1
1
– 1
-1 1
-1
X
– Y
B D
borrow-in

## Slide 6: Binary Subtraction
Start with the least significant bit (rightmost bit)
Subtract each pair of bits
Include the borrow in the subtraction, if present
0
0
0
1
1
1
0
1
0
0
1
1
0
1
1
0
–
(54)
(29)
(25)
0
1
2
3
4
bit position:
5
6
7
-1
-1
0
0
0
1
1
0
0
1
borrow
-1

## Slide 7: Hexadecimal Addition
Start with the least significant hexadecimal digits
Let Sum = summation of two hex digits
If Sum is greater than or equal to 16
  Sum = Sum – 16 and Carry = 1
Example:
A
F
C
D
B
0
1
1
1
9
C
3
7
2
8
6
5
1
3
9
5
E
8
4
B
+
5 + B = 5 + 11 = 16
Since Sum ≥ 16
Sum = 16 – 16 = 0
Carry = 1
0
1
carry

## Slide 8: Hexadecimal Subtraction
Start with the least significant hexadecimal digits
Let Difference = subtraction of two hex digits
If Difference is negative
  Difference = 16 + Difference and Borrow = -1
Example:
8
8
1
1
0
4
-1
9
C
3
7
2
8
6
5
1
3
9
5
E
8
4
B
-
Since 5 < B, Difference < 0
Difference = 16+5–11 = 10
Borrow = -1
A
-1
borrow
A
-1

## Slide 9: Next . . .
Binary and Hexadecimal Addition and Subtraction
Binary Multiplication and Bit Shifting
Signed Integers
Range, Overflow, Converting Subtraction into Addition

## Slide 10: Binary Multiplication
Binary Multiplication table is simple:
0×0=0, 0×1=0, 1×0=0, 1×1=1
Multiplicand 11002 = 12
Multiplier × 11012 = 13
1100
0000
1100
1100
Product 100111002 = 156
n-bit multiplicand × n-bit multiplier = 2n-bit product
Accomplished via shifting and addition
Binary multiplication is easy
0 × multiplicand = 0
1 × multiplicand = multiplicand

## Slide 11: Shifting the Bits to the Left
What happens if the bits are shifted to the left by 1 bit position?
What happens if the bits are shifted to the left by 2 bit positions?
0
0
0
0
1
0
1
0
0
0
0
0
0
1
0
1
= 5
Before
After
= 10
0
0
0
1
0
1
0
0
0
0
0
0
0
1
0
1
= 5
Before
After
= 20
Shifting the Bits to the Left by n bit positions is multiplication by 2n
As long as we have sufficient space to store the bits
Multiplication
By 2
Multiplication
By 4

## Slide 12: Shifting the Bits to the Right
What happens if the bits are shifted to the right by 1 bit position?
What happens if the bits are shifted to the right by 2 bit positions?
0
0
0
1
0
0
1
1
0
0
1
0
0
1
1
0
= 38
Before
After
= 19, r=0
Shifting the Bits to the Right by n bit positions is division by 2n
The remainder r is the value of the bits that are shifted out
Division
By 2
Division
By 4
0
0
0
0
1
0
0
1
0
0
1
0
0
1
1
0
= 38
Before
After
= 9, r=2

## Slide 13: Next . . .
Binary and Hexadecimal Addition and Subtraction
Binary Multiplication and Bit Shifting
Signed Integers
Range, Overflow, Converting Subtraction into Addition

## Slide 14: Signed Integers
Several ways to represent a signed integer
  Sign-Magnitude
  1's complement
  2's complement
Divide the range of values into two parts
  First part corresponds to the positive numbers (≥ 0)
  Second part correspond to the negative numbers (< 0)
The 2's complement representation is widely used
  Has many advantages over other representations

## Slide 15: Sign-Magnitude Representation
Independent representation of the sign and magnitude
Leftmost bit is the sign bit: 0 is positive and 1 is negative
Using n bits, largest represented magnitude = 2n-1 – 1
Sign
Bit
bit
n-2
bit
2
bit
1
bit
0
. . .
Magnitude = n – 1 bits
n-bit number
1
0
1
1
0
1
0
0
1
0
1
1
0
1
0
1
Sign-magnitude
8-bit representation of +45
Sign-magnitude
8-bit representation of -45

## Slide 16: Properties of Sign-Magnitude
Symmetric range of represented values:
For n-bit register, range is from -(2n-1 – 1) to +(2n-1 – 1)
For example, if n = 8 bits then range is -127 to +127
Two representations for zero: +0 and -0 NOT Good!
Two circuits are needed for addition & subtraction NOT Good!
  In addition to an adder, a second circuit is needed for subtraction
  Sign and magnitude parts should be processed independently
  Sign bit should be examined to determine addition or subtraction
  Addition of numbers of different signs is converted into subtraction
  Increases the cost of the add/subtract circuit

## Slide 17: Sign-Magnitude Addition / Subtraction
Eight cases for Sign-Magnitude Addition / Subtraction
Operation | ADD Magnitudes | Subtract Magnitudes | 
 |  | A >= B | A < B
(+A) + (+B) | +(A+B) |  | 
(+A) + (-B) |  | +(A–B) | -(B–A)
(-A) + (+B) |  | -(A–B) | +(B–A)
(-A) + (-B) | -(A+B) |  | 
(+A) – (+B) |  | +(A–B) | -(B–A)
(+A) – (-B) | +(A+B) |  | 
(-A) – (+B) | -(A+B) |  | 
(-A) – (-B) |  | -(A–B) | +(B–A)

## Slide 18: 1’s Complement Representation
Given a binary number A
The 1’s complement of A is obtained by inverting each bit in A
Example: 1’s complement of (01101001)2 = (10010110)2
If A consists of n bits then:
A + (1’s complement of A) = (2n – 1) = (1…111)2 (all bits are 1's)
Range of values is -(2n-1 – 1) to +(2n-1 – 1)
For example, if n = 8 bits, range is -127 to +127
Two representations for zero: +0 and -0 NOT Good!
1's complement of (0…000)2 = (1…111)2 = 2n – 1
-0 = (1…111)2 NOT Good!

## Slide 19: 2’s Complement Representation
Standard way to represent signed integers in computers
A simple definition for 2’s complement:
Given a binary number A
The 2’s complement of A = (1’s complement of A) + 1
Example: 2’s complement of (01101001)2 =
(10010110)2 + 1 = (10010111)2
If A consists of n bits then
A + (2’s complement of A) = 2n
2’s complement of A = 2n – A

## Slide 20: Computing the 2's Complement
Another way to obtain the 2's complement:
Start at the least significant 1
Leave all the 0s to its right unchanged
Complement all the bits to its left
starting value | 001001002 = +36
step1: Invert the bits (1's complement) | 110110112
step 2: Add 1 to the value from step 1 | + 12
sum = 2's complement representation | 110111002 = -36
Binary Value
= 00100 1 00
2's Complement
= 11011 1 00
least
significant 1
2’s complement of 110111002 (-36) = 001000112 + 1 = 001001002 = +36
The 2’s complement of the 2’s complement of A is equal to A

## Slide 21: Properties of the 2’s Complement
Range of represented values: -2n-1 to +(2n-1 – 1)
For example, if n = 8 bits then range is -128 to +127
There is only one zero = (0…000)2 (all bits are zeros)
The 2’s complement of A is the negative of A
The sum of A + (2’s complement of A) must be zero
The final carry is ignored
Consider the 8-bit number A = 001011002 = +44
2’s complement of A = 110101002 = -44
001011002 + 110101002 = 1 000000002 (8-bit sum is 0)
Ignore final carry = 28

## Slide 22: 2's Complement Signed Decimal Value
Positive numbers (sign-bit = 0)
  Signed value = Unsigned value
Negative numbers (sign-bit = 1)
  Signed value = Unsigned value – 2n
  n = number of bits
Negative weight for sign bit
  The 2's complement representation assigns a negative weight to the sign bit (most-significant bit)
  -128 + 32 + 16 + 4 = -76
1
0
1
1
0
1
0
0
-128
64
32
16
8
4
2
1
8-bit Binary | Unsigned Value | Signed Value
00000000 | 0 | 0
00000001 | 1 | +1
00000010 | 2 | +2
. . . | . . . | . . .
01111101 | 125 | +125
01111110 | 126 | +126
01111111 | 127 | +127
10000000 | 128 | -128
10000001 | 129 | -127
10000010 | 130 | -126
. . . | . . . | . . .
11111101 | 253 | -3
11111110 | 254 | -2
11111111 | 255 | -1

## Slide 23: Values of Different Representations
8-bit Binary Representation | Unsigned Value | Sign Magnitude Value | 1's Complement Value | 2's Complement Value
00000000 | 0 | +0 | +0 | 0
00000001 | 1 | +1 | +1 | +1
00000010 | 2 | +2 | +2 | +2
. . . | . . . | . . . | . . . | . . .
01111101 | 125 | +125 | +125 | +125
01111110 | 126 | +126 | +126 | +126
01111111 | 127 | +127 | +127 | +127
10000000 | 128 | -0 | -127 | -128
10000001 | 129 | -1 | -126 | -127
10000010 | 130 | -2 | -125 | -126
. . . | . . . | . . . | . . . | . . .
11111101 | 253 | -125 | -2 | -3
11111110 | 254 | -126 | -1 | -2
11111111 | 255 | -127 | -0 | -1

## Slide 24: Next . . .
Binary and Hexadecimal Addition and Subtraction
Binary Multiplication and Bit Shifting
Signed Integers
Range, Overflow, Converting Subtraction into Addition

## Slide 25: Range, Carry, Borrow, and Overflow
Unsigned Integers: n-bit representation
Signed Integers: 2's complement representation
max = 2n–1
min = 0
Carry = 1 for
Addition
Number > max
Borrow for
Subtraction
Number < 0
Positive
Overflow
Number > max
Negative
Overflow
Number < min
max = 2n-1–1
Finite Set of Signed Integers
0
min = -2n-1
Finite Set of Unsigned Integers

## Slide 26: Range of Unsigned Integers
For n-bit unsigned integers: Range is 0 to (2n – 1)
There are NO negative values
Practice: What is the range of values for unsigned 20-bit integers?
Storage Size | Unsigned Range | Powers of 2
Byte = 8 bits | 0 to 255 | 0 to (28 – 1)
Half Word = 16 bits | 0 to 65,535 | 0 to (216 – 1)
Word = 32 bits | 0 to 4,294,967,295 | 0 to (232 – 1)
Double Word = 64 bits | 0 to 18,446,744,073,709,551,615 | 0 to (264 – 1)

## Slide 27: Range of Signed Integers
For n-bit signed integers: Range is -2n–1 to (2n–1 – 1)
Positive range: 0 to 2n–1 – 1
Negative range: -2n–1 to -1
Practice: What is the range of values for signed 20-bit integers?
Storage Type | Signed Range | Powers of 2
Byte = 8 bits | –128 to +127 | –27 to (27 – 1)
Half Word = 16 bits | –32,768 to +32,767 | –215 to (215 – 1)
Word = 32 bits | –2,147,483,648 to +2,147,483,647 | –231 to (231 – 1)
Double Word = 64 bits | –9,223,372,036,854,775,808 to +9,223,372,036,854,775,807 | –263 to (263 – 1)

## Slide 28: Carry and Overflow Examples
0
1
0
0
0
0
0
0
0
1
0
0
1
1
1
1
+
1
0
0
0
1
1
1
1
79
64
143 (-113)
Carry = 0 Overflow = 1
1
1
0
0
1
1
1
0
1
1
1
0
1
1
0
1
0
+
0
1
1
1
0
1
1
1
218 (-38)
157 (-99)
119
Carry = 1 Overflow = 1
1
1
1
We can have carry without overflow and vice-versa
Four cases are possible (Examples on 8-bit numbers)
1
1
1
1
1
0
0
0
0
0
0
0
1
1
1
1
+
0
0
0
0
0
1
1
1
15
248 (-8)
7
Carry = 1 Overflow = 0
1
1
1
1
1
0
0
0
0
1
0
0
0
0
0
0
0
1
1
1
1
+
0
0
0
1
0
1
1
1
15
8
23
Carry = 0 Overflow = 0
1

## Slide 29: Carry versus Overflow
Carry is important when …
  Adding unsigned integers
  Indicates that the unsigned sum is out of range
  Sum > maximum unsigned n-bit value
Overflow is important when …
  Adding or subtracting signed integers
  Indicates that the signed sum is out of range
Overflow occurs when …
  Adding two positive numbers and the sum is negative
  Adding two negative numbers and the sum is positive
Simplest way to detect Overflow: V = Cn–1  Cn
  Cn-1 and Cn are the carry-in and carry-out of the most-significant bit

## Slide 30: Converting Subtraction into Addition
When computing A – B, convert B to its 2's complement
A – B = A + (2’s complement of B)
Same adder is used for both addition and subtraction
This is the biggest advantage of 2's complement
Final carry is ignored, because
A + (2's complement of B) = A + (2n – B) = (A – B) + 2n
Final carry = 2n, for n-bit numbers
0 1 0 0 1 1 0 1 0 1 0 0 1 1 0 1
– 0 0 1 1 1 0 1 0 + 1 1 0 0 0 1 1 0 (2's complement)
0 0 0 1 0 0 1 1 0 0 0 1 0 0 1 1 (same result)
borrow:
carry:
-1
-1
-1
1
1
1
1