## Slide 1: Boolean Algebra and Logic Gates
COE 233
Digital Logic and Computer Organization
Dr. Muhamed Mudawar
King Fahd University of Petroleum and Minerals

## Slide 2: Presentation Outline
Boolean Algebra, truth tables, and DeMorgan’s theorem
Algebraic manipulation and expression simplification
From truth table to logic expression: minterms and maxterms
Logic gates, logic diagrams, and standard forms
Additional gates: NAND, NOR, XOR, XNOR

## Slide 3: Boolean Algebra
Introduced by George Boole in 1854
A set of two values: B = {0, 1}
Three basic operations: AND, OR, and NOT
The AND operator is denoted by a dot (·)
  or is read: AND
The OR operator is denoted by a plus (+)
  is read: OR
The NOT operator is denoted by a quotation ' or an overbar ¯
  or is the complement of
Today, Boolean algebra is being used to design digital circuits

## Slide 4: Postulates of Boolean Algebra
1. Closure: the result of any Boolean operation is in B = {0, 1}
2. Identity element with respect to + is 0:
Identity element with respect to · is 1:
3. Commutative with respect to +:
Commutative with respect to ·:
4. · is distributive over +:
+ is distributive over ·:
5. For every in B, there exists in B (called complement of ) such that: and

## Slide 5: AND, OR, and NOT Operators
The following tables define , , and
is the AND operator
is the OR operator
is the NOT operator
x y | x·y
0 0 | 0
0 1 | 0
1 0 | 0
1 1 | 1
x y | x+y
0 0 | 0
0 1 | 1
1 0 | 1
1 1 | 1
x | x'
0 | 1
1 | 0

## Slide 6: Boolean Functions
Boolean functions are described by expressions that consist of:
  Boolean variables, such as: , , etc.
  Boolean constants: 0 and 1
  Boolean operators: AND (·), OR (+), NOT (')
  Parentheses, which can be nested
Example:
  The dot operator is implicit and need not be written
Operator precedence: to avoid ambiguity in expressions
  Expressions within parentheses should be evaluated first
  The NOT (') operator should be evaluated second
  The AND (·) operator should be evaluated third
  The OR (+) operator should be evaluated last

## Slide 7: Truth Table
A truth table can represent a Boolean function
List all possible combinations of 0's and 1's assigned to variables
If n variables then 2n rows
Example: Truth table for
x y z | y' | xy' | x' | x'z | f = xy'+ x'z
0 0 0 | 1 | 0 | 1 | 0 | 0
0 0 1 | 1 | 0 | 1 | 1 | 1
0 1 0 | 0 | 0 | 1 | 0 | 0
0 1 1 | 0 | 0 | 1 | 1 | 1
1 0 0 | 1 | 1 | 0 | 0 | 1
1 0 1 | 1 | 1 | 0 | 0 | 1
1 1 0 | 0 | 0 | 0 | 0 | 0
1 1 1 | 0 | 0 | 0 | 0 | 0

## Slide 8: DeMorgan's Theorem
x | y | x' | y' | x+y | (x+y)' | x'y' | x y | (x y)' | x'+ y'
0 | 0 | 1 | 1 | 0 | 1 | 1 | 0 | 1 | 1
0 | 1 | 1 | 0 | 1 | 0 | 0 | 0 | 1 | 1
1 | 0 | 0 | 1 | 1 | 0 | 0 | 0 | 1 | 1
1 | 1 | 0 | 0 | 1 | 0 | 0 | 1 | 0 | 0
Can be verified
Using a Truth Table
Identical
Identical
Generalized DeMorgan's Theorem:

## Slide 9: Complementing Boolean Functions
What is the complement of ?
Use DeMorgan's Theorem:
  Complement each variable and constant
  Interchange AND and OR operators
So, what is the complement of ?
Answer: )
Example 2: Complement
Answer:

## Slide 10: Algebraic Manipulation of Expressions
The objective is to acquire skills in manipulating Boolean expressions, to transform them into simpler form.
Example 1: prove (absorption theorem)
Proof:
Distributive · over +
Example 2: prove (simplification theorem)
Proof: Distributive + over ·

## Slide 11: Expression Simplification
Using Boolean algebra to simplify expressions
Expression should contain the smallest number of literals
A literal is a variable that may or may not be complemented
Example: simplify
Solution: (15 literals)
(15 literals)
(13 literals)
(7 literals)
(7 literals)
(6 literals)
(5 literals only)

## Slide 12: Summary of Boolean Algebra
 | Property | Dual Property
Identity |  | 
Complement |  | 
Null |  | 
Idempotence |  | 
Involution | ( | 
Commutative |  | 
Associative | ( | 
Distributive |  | 
Absorption |  | 
Simplification |  | 
De Morgan | ( | 
 | Property | Dual Property
Identity |  | 
Complement |  | 
Null |  | 
Idempotence |  | 
Involution |  | 
Commutative |  | 
Associative |  | 
Distributive |  | 
Absorption |  | 
Simplification |  | 
De Morgan |  | 

## Slide 13: Importance of Boolean Algebra
Our objective is to learn how to design digital circuits
These circuits use signals with two possible values
Logic 0 is a low voltage signal (0 volts)
Logic 1 is a high voltage signal (for example, 1.2 volts)
The physical value of a signal is the actual voltage it carries, while its logic value is either 0 (low) or 1 (high)
Having only two logic values (0 and 1) simplifies the implementation of the digital circuit

## Slide 14: Next . . .
Boolean Algebra, truth tables, and DeMorgan’s theorem
Algebraic manipulation and expression simplification
From truth table to logic expression: minterms and maxterms
Logic gates, logic diagrams, and standard forms
Additional gates: NAND, NOR, XOR, XNOR

## Slide 15: From a Truth Table to Logic Expression
Given the truth table of a Boolean function , how to obtain the logic expression ?
Truth Table
x y z | f
0 0 0 | 0
0 0 1 | 0
0 1 0 | 1
0 1 1 | 1
1 0 0 | 0
1 0 1 | 1
1 1 0 | 0
1 1 1 | 1
What is the logic expression of ?
To answer this question, we need
to define Minterms and Maxterms

## Slide 16: Minterms and Maxterms
Minterms are AND terms with every variable present in either true or complement form
Maxterms are OR terms with every variable present in either true or complement form
Minterms and Maxterms for 2 variables and
For n variables, there are 2n Minterms and Maxterms
x | y | index | Minterm | Maxterm
0 | 0 | 0 |  | 
0 | 1 | 1 |  | 
1 | 0 | 2 |  | 
1 | 1 | 3 |  | 
x | y | index | Minterm | Maxterm
0 | 0 | 0 |  | 
0 | 1 | 1 |  | 
1 | 0 | 2 |  | 
1 | 1 | 3 |  | 

## Slide 17: Minterms and Maxterms for 3 Variables
Maxterm is the complement of Minterm
and
x | y | z | index | Minterm | Maxterm
0 | 0 | 0 | 0 |  | 
0 | 0 | 1 | 1 |  | 
0 | 1 | 0 | 2 |  | 
0 | 1 | 1 | 3 |  | 
1 | 0 | 0 | 4 |  | 
1 | 0 | 1 | 5 |  | 
1 | 1 | 0 | 6 |  | 
1 | 1 | 1 | 7 |  | 
x | y | z | index | Minterm | Maxterm
0 | 0 | 0 | 0 |  | 
0 | 0 | 1 | 1 |  | 
0 | 1 | 0 | 2 |  | 
0 | 1 | 1 | 3 |  | 
1 | 0 | 0 | 4 |  | 
1 | 0 | 1 | 5 |  | 
1 | 1 | 0 | 6 |  | 
1 | 1 | 1 | 7 |  | 

## Slide 18: Sum-Of-Minterms (SOM) Canonical Form
Sum of Minterm entries that evaluate to ‘1’
Truth Table
x y z | f | Minterm
0 0 0 | 0 | 
0 0 1 | 0 | 
0 1 0 | 1 | 
0 1 1 | 1 | 
1 0 0 | 0 | 
1 0 1 | 1 | 
1 1 0 | 0 | 
1 1 1 | 1 | 
x y z | f | Minterm
0 0 0 | 0 | 
0 0 1 | 0 | 
0 1 0 | 1 | 
0 1 1 | 1 | 
1 0 0 | 0 | 
1 0 1 | 1 | 
1 1 0 | 0 | 
1 1 1 | 1 | 
Focus on the ‘1’ entries

## Slide 19: Product-Of-Maxterms (POM) Canonical Form
Truth Table
x y z | f | Maxterm
0 0 0 | 0 | 
0 0 1 | 0 | 
0 1 0 | 1 | 
0 1 1 | 1 | 
1 0 0 | 0 | 
1 0 1 | 1 | 
1 1 0 | 0 | 
1 1 1 | 1 | 
x y z | f | Maxterm
0 0 0 | 0 | 
0 0 1 | 0 | 
0 1 0 | 1 | 
0 1 1 | 1 | 
1 0 0 | 0 | 
1 0 1 | 1 | 
1 1 0 | 0 | 
1 1 1 | 1 | 
Product of Maxterm entries that evaluate to ‘0’
Focus on the ‘0’ entries

## Slide 20: Purpose of the Index
Minterms and Maxterms are designated with an index
The index for the Minterm or Maxterm, expressed as a binary number, is used to determine whether the variable is shown in the true or complemented form
For Minterms:
  ‘1’ means the variable is Not Complemented
  ‘0’ means the variable is Complemented
For Maxterms:
  ‘0’ means the variable is Not Complemented
  ‘1’ means the variable is Complemented

## Slide 21: Examples of Sum-Of-Minterms

## Slide 22: Examples of Product-Of-Maxterms

## Slide 23: Conversions between Canonical Forms
The same Boolean function can be expressed in two ways:
  Sum-of-Minterms
  Product-of-Maxterms
x y z | f | Minterms | Maxterms
0 0 0 | 1 |  | 
0 0 1 | 0 |  | 
0 1 0 | 1 |  | 
0 1 1 | 1 |  | 
1 0 0 | 0 |  | 
1 0 1 | 1 |  | 
1 1 0 | 0 |  | 
1 1 1 | 1 |  | 
x y z | f | Minterms | Maxterms
0 0 0 | 1 |  | 
0 0 1 | 0 |  | 
0 1 0 | 1 |  | 
0 1 1 | 1 |  | 
1 0 0 | 0 |  | 
1 0 1 | 1 |  | 
1 1 0 | 0 |  | 
1 1 1 | 1 |  | 
To convert from one canonical form to another, interchange the symbols  and  and list those numbers missing from the original form.
Truth Table

## Slide 24: Function Complement
Given a Boolean function
Then, the complement of function
x y z | f | f'
0 0 0 | 1 | 0
0 0 1 | 0 | 1
0 1 0 | 1 | 0
0 1 1 | 1 | 0
1 0 0 | 0 | 1
1 0 1 | 1 | 0
1 1 0 | 0 | 1
1 1 1 | 1 | 0
The complement of a function expressed by a Sum of Minterms is the Product of Maxterms with the same indices. Interchange the symbols  and , but keep the same list of indices.
Truth Table

## Slide 25: Summary of Minterms and Maxterms
There are 2n Minterms and Maxterms for Boolean functions with n variables, indexed from 0 to 2n – 1
Minterms correspond to the 1-entries of the function
Maxterms correspond to the 0-entries of the function
Any Boolean function can be expressed as a Sum-of-Minterms and as a Product-of-Maxterms
For a Boolean function, given the list of Minterm indices one can determine the list of Maxterms indices (and vice versa)
The complement of a Sum-of-Minterms is a Product-of-Maxterms with the same indices (and vice versa)

## Slide 26: Next . . .
Boolean Algebra, truth tables, and DeMorgan’s theorem
Algebraic manipulation and expression simplification
From truth table to logic expression: minterms and maxterms
Logic gates, logic diagrams, and standard forms
Additional gates: NAND, NOR, XOR, XNOR

## Slide 27: Logic Gates and Symbols
AND gate
OR gate
NOT gate (inverter)
In the earliest days of computers, relays were used as mechanical switches controlled by electricity (coils)
Today, tiny transistors are used as electronic switches that implement the logic gates (CMOS technology)
AND: Switches in series
logic 0 is open switch
OR: Switches in parallel
logic 0 is open switch
NOT: Switch is normally
closed when x is 0

## Slide 28: Truth Table and Logic Diagram
Given the following logic function:
Draw the corresponding truth table and logic diagram
Truth Table
x y z | y'+ z | f = x(y'+ z)
0 0 0 | 1 | 0
0 0 1 | 1 | 0
0 1 0 | 0 | 0
0 1 1 | 1 | 0
1 0 0 | 1 | 1
1 0 1 | 1 | 1
1 1 0 | 0 | 0
1 1 1 | 1 | 1
Truth Table and Logic Diagram describe the same function .
Truth table is unique, but logic expression and logic diagram are not. This gives flexibility in implementing logic functions.
Logic Diagram

## Slide 29: Standard Forms
Boolean functions are usually expressed in standard form
Two standard forms: Sum-of-Products and Product-of -Sums
Sum of Products (SOP)
  Boolean expression is the ORing (sum) of AND terms (products)
  Examples:
Products of Sums (POS)
  Boolean expression is the ANDing (product) of OR terms (sums)
  Examples:

## Slide 30: From Sum-of-Minterms to Sum-of-Products
Simplify into minimal sum-of-products
First, write f as sum-of-minterms canonical form
Then, simplify expression using properties of Boolean Algebra
(12 literals)
)
(4 literals)

## Slide 31: Two-Level Gate Implementation
3-input AND gate
AND-OR
implementations
3-input OR gate
OR-AND
implementations

## Slide 32: Two-Level vs. Three-Level Implementation
(6 literals) is a sum-of-products
may also be written as: (5 literals)
However, is a non-standard form
  is not a sum-of-products nor a product-of-sums
2-level implementation
3-level implementation
3-input OR gate

## Slide 33: Next . . .
Boolean Algebra, truth tables, and DeMorgan’s theorem
Algebraic manipulation and expression simplification
From truth table to logic expression: minterms and maxterms
Logic gates, logic diagrams, and standard forms
Additional gates: NAND, NOR, XOR, XNOR

## Slide 34: Additional Logic Gates and Symbols
Why?
  Low-cost implementation
  Useful in implementing Boolean functions
AND gate
OR gate
NOT gate (inverter)
NAND gate
NOR gate
XOR gate
XNOR gate

## Slide 35: NAND Gate
The NAND gate has the following symbol and truth table
NAND represents NOT AND
The small bubble circle represents the invert function
NAND gate is implemented efficiently in CMOS technology
  In terms of chip area and speed
x y | NAND
0 0 | 1
0 1 | 1
1 0 | 1
1 1 | 0
NAND gate
Another symbol for NAND

## Slide 36: NOR Gate
The NOR gate has the following symbol and truth table
NOR represents NOT OR
The small bubble circle represents the invert function
NOR gate is implemented efficiently in CMOS technology
  In terms of chip area and speed
x y | NOR
0 0 | 1
0 1 | 0
1 0 | 0
1 1 | 0
NOR gate
Another symbol for NOR

## Slide 37: Multiple-Input NAND / NOR Gates
NAND/NOR gates can have multiple inputs, similar to AND/OR gates
2-input NAND gate
3-input NAND gate
4-input NAND gate
2-input NOR gate
3-input NOR gate
4-input NOR gate
Note: a 3-input NAND is a single gate, NOT a combination of two 2-input gates. The same can be said about other multiple-input NAND/NOR gates.

## Slide 38: NAND – NAND Implementation
Consider the following sum-of-products expression:
A 2-level AND-OR circuit can be converted easily to a 2-level NAND-NAND implementation
2-Level AND-OR
Inserting Bubbles
Two successive bubbles on same line cancel each other
2-Level NAND-NAND
3-input
NAND gate
3-input
AND gate

## Slide 39: NOR – NOR Implementation
Consider the following product-of-sums expression:
A 2-level OR-AND circuit can be converted easily to a 2-level NOR-NOR implementation
Two successive bubbles on same line cancel each other
2-Level OR-AND
Inserting Bubbles
2-Level NOR-NOR
3-input
NOR gate
3-input
OR gate

## Slide 40: Exclusive OR / Exclusive NOR
Exclusive OR (XOR) is an important Boolean operation used extensively in logic circuits
Exclusive NOR (XNOR) is the complement of XOR
XOR gate
XNOR gate
x y | XOR
0 0 | 0
0 1 | 1
1 0 | 1
1 1 | 0
x y | XNOR
0 0 | 1
0 1 | 0
1 0 | 0
1 1 | 1
XNOR is also known as equivalence

## Slide 41: XOR / XNOR Functions
The XOR function is:
The XNOR function is:
XOR and XNOR gates are complex
  Can be implemented as a true gate, or by
  Interconnecting other gate types
XOR and XNOR gates do not exist for more than two inputs
  For 3 inputs, use two XOR gates
  The cost of a 3-input XOR gate is greater than the cost of two XOR gates
Uses for XOR and XNOR gates include:
  Adders, subtractors, multipliers, incrementers, and decrementers

## Slide 42: XOR and XNOR Properties
XOR is an associative operation

## Slide 43: Odd Function
Output is 1 if the number of 1's is odd in the inputs
Output is the XOR operation on all input variables
x y z | fodd
0 0 0 | 0
0 0 1 | 1
0 1 0 | 1
0 1 1 | 0
1 0 0 | 1
1 0 1 | 0
1 1 0 | 0
1 1 1 | 1
Odd Function with 3 inputs
Implementation using two XOR gates

## Slide 44: Even Function
Output is 1 if the number of 1's is even in the inputs (complement of odd function)
Output is the XNOR operation on all inputs
w x y z | feven
0 0 0 0 | 1
0 0 0 1 | 0
0 0 1 0 | 0
0 0 1 1 | 1
0 1 0 0 | 0
0 1 0 1 | 1
0 1 1 0 | 1
0 1 1 1 | 0
1 0 0 0 | 0
1 0 0 1 | 1
1 0 1 0 | 1
1 0 1 1 | 0
1 1 0 0 | 1
1 1 0 1 | 0
1 1 1 0 | 0
1 1 1 1 | 1
Even Function with 4 inputs
Implementation using two XOR gates and one XNOR