## Slide 1: Combinational Circuit
COE 233
Digital Logic and Computer Organization
Dr. Muhamed Mudawar
King Fahd University of Petroleum and Minerals

## Slide 2: Presentation Outline
Half-Adder, Full-Adder, and Ripple-Carry Adder
Decoders, Implementing Functions with Decoders
Multiplexers
Design Examples

## Slide 3: Combinational Circuit
A combinational circuit is a block of logic gates having:
inputs:
outputs:
Each output is a function of the input variables
Each output is determined from present combination of inputs
Combination circuit performs operation specified by logic gates

Combinational
Circuit

inputs
outputs

## Slide 4: Half Adder
A half adder adds two bits: a and b
Two output bits:
Carry bit: cout = a · b
Sum bit: sum = a  b
a b | cout | sum
0 0 | 0 | 0
0 1 | 0 | 1
1 0 | 0 | 1
1 1 | 1 | 0
Truth Table
b
a
cout
sum
Half
Adder
a
b
sum
cout

## Slide 5: Full Adder
A full adder adds 3 bits: a, b, and c
Two output bits:
Carry bit: cout
Sum bit: sum
Sum bit is 1 if odd input of 1’s
sum = (a  b)  c (odd function)
Carry bit is 1 if the input of 1’s is 2 or 3
cout = a·b + (a  b)·c
a b c | cout | sum
0 0 0 | 0 | 0
0 0 1 | 0 | 1
0 1 0 | 0 | 1
0 1 1 | 1 | 0
1 0 0 | 0 | 1
1 0 1 | 1 | 0
1 1 0 | 1 | 0
1 1 1 | 1 | 1
Truth Table
c
Full
Adder
a
b
sum
cout

## Slide 6: Full Adder Implementation
Half
Adder
a
b
Half
Adder
c
sum
cout
A full adder can be implemented as two half-adders and an OR gate
Full Adder
cout
a
b
c
sum

## Slide 7: Binary Addition
Start with the least significant bit (rightmost bit)
Add each pair of bits
Include the carry in the addition
0
0
0
1
1
1
0
1
0
0
1
1
0
1
1
0
+
(54)
(29)
(83)
1
carry
0
1
2
3
4
bit position:
5
6
7
1
1
1
0
1
0
1
0
0
1
1

## Slide 8: Ripple Carry Adder
Adds two n-bit numbers: A = {An-1, …, A0} and B = {Bn-1, …, B0}
Uses identical copies of a full adder to build a large n-bit adder
Iterative design: the cell is a full adder
Carry propagation: carry-out of cell i becomes carry-in to cell i +1
ci
Full
Adder
Ai
Bi
Si
ci+1
c0
Full
Adder
A0
B0
S0
c1
Full
Adder
A1
B1
S1
c2
Full
Adder
A2
B2
S2
...
cn-1
Full
Adder
An-1
Bn-1
Sn-1
cn
c3

## Slide 9: Next . . .
Half-Adder, Full-Adder, and Ripple-Carry Adder
Decoders, Implementing Functions with Decoders
Multiplexers
Design Examples

## Slide 10: Binary Decoders
Given a n-bit binary code, there are 2n possible code values
The decoder has an output for each possible code value
The n-to-2n decoder has n inputs and 2n outputs
Depending on the input code, only one output is set to logic 1
The conversion of input to output is called decoding
n to 2n
Decoder


n Inputs
2n Outputs
A decoder can have less than 2n outputs if some input codes are unused

## Slide 11: Examples of Binary Decoders
Inputs | Outputs |  |  |  |  |  |  | 
a2 a1 a0 | d0 | d1 | d2 | d3 | d4 | d5 | d6 | d7
0 0 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 0 1 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0
0 1 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0
0 1 1 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0
1 0 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0
1 0 1 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0
1 1 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0
1 1 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1
Inputs | Outputs |  |  | 
a1 a0 | d0 | d1 | d2 | d3
0 0 | 1 | 0 | 0 | 0
0 1 | 0 | 1 | 0 | 0
1 0 | 0 | 0 | 1 | 0
1 1 | 0 | 0 | 0 | 1
Truth
Tables
2-to-4
Decoder
2 Inputs
4 Outputs
a1
a0
d0
d1
d2
d3
0
1
2
3
1
0
3-to-8
Decoder
8 Outputs
3 Inputs
a2
a1
a0
d0
d1
d2
d3
d4
d5
d6
d7
0
1
2
3
4
5
6
7
1
0
2

## Slide 12: Decoder Implementation
Each decoder output is a minterm
3-to-8 Decoder
2-to-4
Decoder
Inputs | Outputs |  |  | 
a1 a0 | d0 | d1 | d2 | d3
0 0 | 1 | 0 | 0 | 0
0 1 | 0 | 1 | 0 | 0
1 0 | 0 | 0 | 1 | 0
1 1 | 0 | 0 | 0 | 1

## Slide 13: Using Decoders to Implement Functions
A decoder generates all the minterms
A Boolean function can be expressed as a sum of minterms
Any function can be implemented using a decoder + OR gate
Note: the function must not be minimized
Example: Full Adder sum = ∑(1, 2, 4, 7), cout = ∑(3, 5, 6, 7)
Inputs | Outputs | 
a b c | cout | sum
0 0 0 | 0 | 0
0 0 1 | 0 | 1
0 1 0 | 0 | 1
0 1 1 | 1 | 0
1 0 0 | 0 | 1
1 0 1 | 1 | 0
1 1 0 | 1 | 0
1 1 1 | 1 | 1
3-to-8
Decoder
a
b
c
d0
d1
d2
d3
d4
d5
d6
d7
2
1
0
sum
cout

## Slide 14: Using Decoders to Implement Functions
Good if many output functions of the same input variables
If number of minterms is large  Wider OR gate is needed
Use NOR gate if number of maxterms is less than minterms
Example: f = ∑(2, 5, 6), g = ∏(3, 6)  g' = ∑(3, 6), h = ∑(0, 5)
Inputs | Outputs |  | 
a b c | f | g | h
0 0 0 | 0 | 1 | 1
0 0 1 | 0 | 1 | 0
0 1 0 | 1 | 1 | 0
0 1 1 | 0 | 0 | 0
1 0 0 | 0 | 1 | 0
1 0 1 | 1 | 1 | 1
1 1 0 | 1 | 0 | 0
1 1 1 | 0 | 1 | 0
3-to-8
Decoder
a
b
c
d0
d1
d2
d3
d4
d5
d6
d7
2
1
0
f
g
h

## Slide 15: BCD to 7-Segment Decoder
Seven-Segment Display:
  Made of Seven segments: light-emitting diodes (LED)
  Found in electronic devices: such as clocks, calculators, etc.
BCD to 7-Segment Decoder
  Called also a decoder, but not a binary decoder
  Accepts as input a BCD decimal digit (0 to 9)
  Generates output to the seven LED segments to display the BCD digit
  Each segment can be turned on or off separately
BCD to
7-Segment
Decoder
I3
I2
I1
I0
a
b
c
d
e
f
g

## Slide 16: BCD to 7-Segment Decoder
Specification:
  Input: 4-bit BCD (I3, I2, I1, I0)
  Output: 7-bit (a, b, c, d, e, f, g)
  Display should be OFF for Non-BCD input codes.
  Implementation can use:
  A binary decoder
  Additional gates
BCD input I3 I2 I1 I0 | 7-Segment Output a b c d e f g
0 0 0 0 | 1 1 1 1 1 1 0
0 0 0 1 | 0 1 1 0 0 0 0
0 0 1 0 | 1 1 0 1 1 0 1
0 0 1 1 | 1 1 1 1 0 0 1
0 1 0 0 | 0 1 1 0 0 1 1
0 1 0 1 | 1 0 1 1 0 1 1
0 1 1 0 | 1 0 1 1 1 1 1
0 1 1 1 | 1 1 1 0 0 0 0
1 0 0 0 | 1 1 1 1 1 1 1
1 0 0 1 | 1 1 1 1 0 1 1
1010 to 1111 | 0 0 0 0 0 0 0
Truth Table

## Slide 17: Implementing a BCD to 7-Segment Decoder
I3 I2 I1 I0 | a b c d e f g
0 0 0 0 | 1 1 1 1 1 1 0
0 0 0 1 | 0 1 1 0 0 0 0
0 0 1 0 | 1 1 0 1 1 0 1
0 0 1 1 | 1 1 1 1 0 0 1
0 1 0 0 | 0 1 1 0 0 1 1
0 1 0 1 | 1 0 1 1 0 1 1
0 1 1 0 | 1 0 1 1 1 1 1
0 1 1 1 | 1 1 1 0 0 0 0
1 0 0 0 | 1 1 1 1 1 1 1
1 0 0 1 | 1 1 1 1 0 1 1
1010 – 1111 | 0 0 0 0 0 0 0
Truth Table
a
b
c
d
f
e
g
Input > 9
NOR gate is used for 0's
I2
I1
I0
I3
4-to-10
Binary
Decoder
0
1
2
3
4
5
6
7
8
9

## Slide 18: Next . . .
Half-Adder, Full-Adder, and Ripple-Carry Adder
Decoders, Implementing Functions with Decoders
Multiplexers
Design Examples

## Slide 19: Multiplexers
Selecting data is an essential function in digital systems
Functional blocks that perform selecting are called multiplexers
A Multiplexer (or Mux) is a combinational circuit that has:
  Multiple data inputs (typically 2n) to select from
  An n-bit select input S used for control
  One output Y
The n-bit select input directs one of the data inputs to the output
Mux
d0
d1
d2
.
.
.
Y
2n Inputs
n
S
d2n–1

## Slide 20: Examples of Multiplexers
2-to-1 Multiplexer
if (S == 0) Y = d0 ;
else Y = d1;
Logic expression:
4-to-1 Multiplexer
if (S1S0 == 00) Y = d0 ;
else if (S1S0 == 01) Y = d1;
else if (S1S0 == 10) Y = d2;
else Y = d3;
Logic expression:
Mux
1 0
S1S0
d0
d1
d2
d3
0
1
2
3
Inputs |  |  | Output
S | d0 | d1 | Y
0 | 0 | X | 0 = d0
0 | 1 | X | 1 = d0
1 | X | 0 | 0 = d1
1 | X | 1 | 1 = d1
Inputs |  |  |  |  |  | Output
S1 | S0 | d0 | d1 | d2 | d3 | Y
0 | 0 | 0 | X | X | X | 0 = d0
0 | 0 | 1 | X | X | X | 1 = d0
0 | 1 | X | 0 | X | X | 0 = d1
0 | 1 | X | 1 | X | X | 1 = d1
1 | 0 | X | X | 0 | X | 0 = d2
1 | 0 | X | X | 1 | X | 1 = d2
1 | 1 | X | X | X | 0 | 0 = d3
1 | 1 | X | X | X | 1 | 1 = d3
Mux
d0
d1
Y
S
0
1

## Slide 21: Implementing Multiplexers
Enabling
AND Gates
Enabling
AND Gates
Y
d0
d1
S
d1
Y
d2
S0
d0
d3
S1
Mux
d0
d1
S
0
1
Mux
1 0
S1S0
d0
d1
d2
d3
0
1
2
3

## Slide 22: Building Larger Multiplexers
Larger multiplexers can be built hierarchically using smaller ones
Building 4-to-1
Mux using three
2-to-1 Muxes
Building 8-to-1 Mux
using two 4-to-1 Muxes
and a 2-to-1 Mux
Y
Mux
d0
d1
S0
Mux
d2
d3
S0
Mux
S1
0
1
0
1
0
1
8-to-1 Mux
Y
2 1 0
S2S1S0
d0
d1
d2
d3
d4
d5
d6
d7
0
1
2
3
4
5
6
7
Y
Mux
S2
0
1
Mux
d4
d5
S1S0
d6
d7
0
1
2
3
1 0
Mux
d0
d1
S1S0
d2
d3
0
1
2
3
1 0

## Slide 23: Multiplexers with Vector Input and Output
The inputs and output of a multiplexer can be n-bit vectors
2-to-1 Multiplexer with n bits
Inputs and output are n-bit vectors
Using n copies of a 2-to-1 Mux
4-to-1 Multiplexer with n bits
Inputs and output are n-bit vectors
Using n copies of a 4-to-1 Mux
Mux
S
A [n–1:0]
n
B [n–1:0]
n
Y [n–1:0]
n
0
1
n
Mux
A [n–1:0]
n
B [n–1:0]
n
C [n–1:0]
n
D [n–1:0]
n
Y [n–1:0]
0
1
2
3
S1S0
1 0

## Slide 24: Next . . .
Half-Adder, Full-Adder, and Ripple-Carry Adder
Decoders, Implementing Functions with Decoders
Multiplexers
Design Examples

## Slide 25: 2-by-2 Crossbar Switch
A 2×2 crossbar switch is a combinational circuit that has:
Two n-bit Inputs: A and B
Two n-bit outputs: X and Y
1-bit select input S
Implement the 2×2 crossbar switch using multiplexers
Solution: Two n-bit multiplexers are used
if (S == 0) { X = A; Y = B; }
else { X = B; Y = A; }
2×2
Crossbar
Switch
n
A[n-1:0]
n
B[n-1:0]
X [n-1:0]
n
Y [n-1:0]
n
S
S
A[n–1:0]
n
B[n–1:0]
n
Mux
0
1
Mux
0
1
X [n-1:0]
n
Y [n-1:0]
n

## Slide 26: Addition and Subtraction with Same Adder
Same adder can be used to compute: (A + B) and (A – B)
Two operations: OP = 0 (ADD), OP = 1 (SUBTRACT)
Subtraction (A – B) is computed as: A + (2's complement of B)
2's complement of B = (1's complement of B) + 1
n-bit Adder
n
A [n-1:0]
S [n-1:0]
n
n
n
B [n-1:0]
c0
OP
cn
n-bit input vectors
n-bit output vector
n XOR
gates
OP = 0 (ADD)
B XOR 0 = B
S = A + B + 0 = A + B
OP = 1 (SUBTRACT)
B XOR 1 = 1's complement of B
S = A + (1's complement of B) + 1
S = A + (2's complement of B)
S = A – B

## Slide 27: Arithmetic and Logic Unit (ALU)
Can perform many functions
Most common ALU functions
Arithmetic functions: ADD, SUB (Subtract)
Logic functions: AND, OR, XOR, etc.
We will design a simple ALU with 8 functions
The function F is coded with 3 bits as follows:
Function | ALU Result | Function | ALU Result
F = 000 (ADD) | R = A + B | F = 100 (AND) | R = A & B
F = 001 (ADD + 1) | R = A + B + 1 | F = 101 (OR) | R = A ¦ B
F = 010 (SUB – 1) | R = A – B – 1 | F = 110 (NOR) | R = ~(A ¦ B)
F = 011 (SUB) | R = A – B | F = 111 (XOR) | R = (A ^ B)
ALU
F[2:0]
3
n
A[n-1:0]
n
B[n-1:0]
R [n-1:0]
n
V C
ALU Symbol

## Slide 28: Designing a Simple ALU
n
B[n-1:0]
n-bit Adder
n
n
c0
n
n XOR
gates
n
n
n
n AND
gates
n
n
n XOR
gates
n
n OR
gates
n
n
n
F[2:0] = 3-bit Function code
cn-1
cn
A[n-1:0]
Result = R[n-1:0]
V
C
V = Overflow
C = Carry output
mux
3
2
1
0
0
1
n
mux
1
0
n