## Slide 1: Memory Elements and Units
COE 233
Digital Logic and Computer Organization
Dr. Muhamed Mudawar
King Fahd University of Petroleum and Minerals

## Slide 2: Presentation Outline
Introduction to Sequential Circuits
Latches
Flip-Flops and Registers
Memory Units

## Slide 3: Combinational versus Sequential
Two classes of digital circuits
  Combinational Circuits
  Sequential Circuits
Combinational Circuit
  Outputs = F(Inputs)
  Function of Inputs only
  NO internal memory
Sequential Circuit
  Outputs is a function of Inputs and internal Memory
  There is an internal memory that stores the state of the circuit
  Time is very important: memory changes with time
Combinational
Circuit
Inputs
Outputs

## Slide 4: Sequential Circuits
A Sequential circuit consists of:
Memory elements:
  Latches or Flip-Flops
  Store the Present State
Combinational Logic
  Produces the Outputs
  Produces the Next State
  Next state = memory input (not stored yet)
Synchronous sequential circuits use a clock signal
  The clock signal is an input to the memory elements
  The clock determines when the memory should be updated
Clock
Combinational
Logic
Memory
Elements
Inputs
Outputs
Next
State
Present
State

## Slide 5: The Clock
Clock is a periodic signal = Train of pulses (1's and 0's)
The same clock cycle repeats indefinitely over time
Positive Pulse: when the level of the clock is 1
Negative Pulse: when the level of the clock is 0
Rising Edge: when the clock goes from 0 to 1
Falling Edge: when the clock goes from 1 down to 0
Time
Clock cycle
Clock cycle
Positive
Pulse
Negative
Pulse

## Slide 6: Clock Cycle versus Clock Frequency
Clock cycle (or period) is a time duration
  Measured in seconds, milli-, micro-, nano-, or pico-seconds
  1 ms = 10-3 sec, 1 µs = 10-6 sec, 1 ns = 10-9 sec, 1 ps = 10-12 sec
Clock frequency = number of cycles per second (Hertz)
  1 Hz = 1 cycle/sec, 1 KHz = 103 Hz, 1 MHz = 106 Hz, 1 GHz = 109 Hz
Clock frequency = 1 / Clock Cycle
  Example: Given the clock cycle = 0.5 ns = 0.5 ×10-9 sec
  Then, the clock frequency = 1/(0.5×10-9) = 2×109 Hz = 2 GHz
Time
Clock cycle
Clock cycle
Clock cycle

## Slide 7: Memory Elements
Memory can store and maintain binary state (0's or 1's)
  Until directed by an input signal to change state
Main difference between memory elements
  Number of inputs they have
  How the inputs affect the binary state
Two main types:
  Latches are level-sensitive (the level of the clock)
  Flip-Flops are edge-sensitive (sensitive to the edge of the clock)
Flip-Flips are used in synchronous sequential circuits
Flip-Flops are built with latches

## Slide 8: Next . . .
Introduction to Sequential Circuits
Latches
Flip-Flops and Registers
Memory Units

## Slide 9: SR Latch
A latch is a memory element that can store 0 or 1
An SR Latch can be built using two cross-coupled NOR gates
Two inputs: (Set) and (Reset)
Two outputs: and

## Slide 10: SR Latch Operation
Q
Q
S (Set)
R (Reset)
0
1
0
1
Set Operation
Q
Q
S (Set)
R (Reset)
0
0
0
1
Store Operation
Q
Q
S (Set)
R (Reset)
1
0
1
0
Reset Operation
Q
Q
S (Set)
R (Reset)
0
0
1
0
Store Operation

## Slide 11: SR Latch Invalid Operation
Q
Q
S (Set)
R (Reset)
1
1
0
0
Invalid Operation
Q
Q
S (Set)
R (Reset)
10
10
01
01
Race Condition
Q
Q
S (Set)
R (Reset)
0
0
1 or 0
0 or 1
Unknown State
S = R = 1 should never be used
If S and R change from 1  0 simultaneously then race condition (oscillation) occurs
Final Q and Q are unknown

## Slide 12: SR Latch with Clock Input
Q
Q
S (Set)
R (Reset)
CR
CS
C (Clock)
An additional Clock (enable) input signal C is used
Clock controls when the state of the latch can be changed
When C=0, the S and R inputs have no effect on the latch
The latch will remain in the same state, regardless of S and R
When C=1, then normal SR latch operation

## Slide 13: D Latch with Clock Input
One data input , and , No undefined state
Clock controls when the state of the latch can be changed
When C=0, the D input has no effect on the latch
The latch will remain in the same state, regardless of D
When C=1, latch is enabled, reset if D is 0 and set if D is 1
Q
Q
D (Data)
CR
CS
C (Clock)
R
S

## Slide 14: Graphic Symbols for Latches
A bubble appears at the complemented output
Indicates that is the complement of

## Slide 15: Problem with Latches
A latch is level-sensitive (sensitive to the level of the clock)
As long as the clock signal is high …
Any change in the value of input appears in the output
Output keeps changing its value during a clock cycle
Final value of output is uncertain
Due to this uncertainty, latches are NOT used as memory elements in sequential circuits

## Slide 16: Next . . .
Introduction to Sequential Circuits
Latches
Flip-Flops and Registers
Memory Units

## Slide 17: Flip-Flops
A Flip-Flop is a better memory element for sequential circuits
Solves the problem of latches in synchronous sequential circuits
A latch is sensitive to the level of the clock
However, a flip-flop is sensitive to the edge of the clock
A flip-flop is called an edge-triggered memory element
It changes it output value at the edge of the clock
Time
Rising edge
Falling edge
Rising edge
Falling edge
High
Level
Low
Level

## Slide 18: Edge-Triggered D Flip-Flop
Built using two latches in a master-slave configuration
A master latch (D-type) receives external inputs
A slave latch (SR-type) receives inputs from the master latch
Only one latch is enabled at any given time
  When Clk=0, the master is enabled and the D input is latched (slave disabled)
  When Clk=1, the slave is enabled to generate the outputs (master is disabled)
Outputs change when Clk changes from 0 to 1
Master
Slave
Clk

## Slide 19: D Flip-Flop Timing Diagram
The diagram shows the timing of a positive-edge D Flip-Flop
The master latch changes its output Qm when the clock C is 0
The rising edge of the clock triggers the D Flip-Flop

## Slide 20: Negative Edge-Triggered D Flip-Flop
Similar to positive edge-triggered flip-flop
The first inverter at the Master C input is removed
Only one latch is enabled at any given time
  When Clk=1, the master is enabled and the D input is latched (slave disabled)
  When Clk=0, the slave is enabled to generate the outputs (master is disabled)
Outputs change when Clk changes from 1 to 0
Master
Slave
Clk

## Slide 21: Graphic Symbols for Flip-Flops
A Flip-Flop has a similar symbol to a Latch
The difference is the arrowhead at the clock input
The arrowhead indicates sensitivity to the edge of the clock
A circle at the Clk input indicates negative edge-triggered FF
Flip
Flop
Flip
Flop

## Slide 22: Register
A register is a circuit capable of storing data
An -bit register consists of Flip-Flops and stores bits of data
Common clock: data is loaded in parallel at the same clock edge
Common reset: All Flip-Flops are reset in parallel
4-bit
Register

## Slide 23: Register Enable
Question: How to control the loading of data into a register?
Solution: Introduce an Enable control signal
If the register is enabled, load the data into the register
Otherwise, do not change the value of the register
Question: How to implement register enable?
n-bit Register

## Slide 24: Implementing Register Enable
Solution: Add a mux (multiplexer) at the input of the register
If is 1 then If is 0 then
0
1
0
1
0
1
0
1

## Slide 25: Next . . .
Introduction to Sequential Circuits
Latches
Flip-Flops and Registers
Memory Units

## Slide 26: Memory Units
A memory unit is a device that can store binary information
It is a large group of cells, each capable of storing one bit
Two types of memory units: Volatile and Non-Volatile
Random-Access Memory (RAM) is volatile
ROM, Flash, and FPGA are non-volatile
Memory Unit
Volatile
Non-Volatile
RAM
SRAM
DRAM
ROM
Flash
FPGA
Needs power supply to retain bits
Does not need power supply to retain bits

## Slide 27: Random-Access Memory
Large array of storage cells, capable of storing many 0's and 1's
Random Access: bits can be accessed randomly
Memory is addressable
Memory address consists of k bits
Can address 2k words in memory
Each word consists of n bits
Memory capacity = 2k × n bits
Two control functions: Read and Write
Read: Data_out  Memory [Address]
Write: Memory [Address]  Data_in
Memory
Unit
2k × n bits
n
Data_in
n
Data_out
k
Address
Read
Write

## Slide 28: Memory Capacity
Each memory location is a group of n bits, which is read/written
Byte = 8-bit data
Half-word = 16-bit data = 2 bytes
Word = 32-bit data = 4 bytes
The memory capacity is specified in bytes
1 KB (Kilo Byte) = 210 = 1024 bytes (more than thousand = 103)
1 MB (Mega Byte) = 220 Bytes (more than million = 106)
1 GB (Giga Byte) = 230 Bytes (more than billion = 109)
1 TB (Tera Byte) = 240 Bytes (more than trillion = 1012)
The memory locations can be accessed (addressed) randomly

## Slide 29: Memory Address and Content
Example of a RAM
Address = 10 bits
210 addresses
From 0 to 1023
Data = 16 bits
Memory capacity =
210 × 16 bits =
16 Kbits = 2 KBytes
Memory can be addressed randomly
Memory can be read and written
16-bit data

## Slide 30: Example of a Small 4×3 Memory Array
2-bit Address  4 wordlines (rows), each storing 3 bits
The decoder enables one wordline (row) at a time
The data are read on the bitlines (columns)
Each wordline in the memory array can be read and written

## Slide 31: Read-Only Memory (ROM)
Address consists of k bits  2k memory addresses
At each memory address, there is a word consisting of n bits
The n-bit word appears at the data output of the ROM
ROM does not have data inputs or a write operation
ROM
2k × n bits
Data_out
k
Address
n
ROM memory is useful for implementing Boolean Functions
Also useful for storing permanent data

## Slide 32: Types of ROMs
ROM may be programmed in four different ways
Mask Programming: done by circuit manufacturer (not by user)
Programmable Read-Only Memory (PROM)
  Fuses in the PROM are blown using a high-voltage pulse
  Can be programmed only once (irreversible)
3. Electrically Erasable PROM (EEPROM)
Can be erased with an electric signal
Flash memory is similar to EEPROMs but has additional circuitry to erase blocks of memory

## Slide 33: ROM Internal Structure (32 x 8-bit)
5-bit Input  5-to-32 binary decoder (Only one line is selected)
Each line = 8 bits  8-bit Data output
0
1
2
3
.
.
.
28
29
30
31
I4
I3
I2
I1
I0
D7 D6 D5 D4 D3 D2 D1 D0
5-to-32 decoder
32×8 = 256 connections
Bits are stored at the intersection
The 32×8 = 256 intersections are programmable

## Slide 34: Implementing a Combinational Circuit
Implementing a Combinational Circuit with a ROM is easy
Store the truth table of the circuit by programming the ROM
I4 I3 I2 I1 I0 | F7 F6 F5 F4 F3 F2 F1 F0
0 0 0 0 0 | 0 0 1 1 1 0 0 0
0 0 0 0 1 | 1 0 0 0 0 1 1 0
0 0 0 1 0 | 0 1 0 1 1 0 0 1
0 0 0 1 1 | 1 0 1 1 0 0 1 0
· · · | · · ·
1 1 1 1 1 | 0 0 1 0 0 0 1 0
Truth Table with Five Inputs and Eight output functions
Inputs are used as Address lines to the ROM

## Slide 35: Programming a ROM
Every 1 in the truth table  X connection is logic-1
Every 0 in the truth table  No X connection is logic-0
Example: At address 00011 = (decimal 3), the word 10110010 is stored
0
1
2
3
.
.
.
28
29
30
31
I4
I3
I2
I1
I0
1 0 1 1 0 0 1 0
5-to-32 decoder
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
00111000
10000110
01011001
10110010
01000001
11001100
10110011
00100010
0
0
0
1
1

## Slide 36: Example: Square Function
Design a square function with a minimum size ROM
Input X = 3-bit number, Output Y = X2
Solution: Derive the Truth Table
X2 X1 X0 | Square | Y5 Y4 Y3 Y2 Y1 Y0
0 0 0 | 0 | 0 0 0 0 0 0
0 0 1 | 1 | 0 0 0 0 0 1
0 1 0 | 4 | 0 0 0 1 0 0
0 1 1 | 9 | 0 0 1 0 0 1
1 0 0 | 16 | 0 1 0 0 0 0
1 0 1 | 25 | 0 1 1 0 0 1
1 1 0 | 36 | 1 0 0 1 0 0
1 1 1 | 49 | 1 1 0 0 0 1

## Slide 37: Minimum-Sized ROM Table
Output Y0 is identical to input X0  No need to store in ROM
Similarly, Output Y1 is always 0  No need to store in ROM
ROM table  Only need to store Y5, Y4, Y3, and Y2 in ROM
X2 X1 X0 | Y5 Y4 Y3 Y2 | Y1 Y0
0 0 0 | 0 0 0 0 | 0 0
0 0 1 | 0 0 0 0 | 0 1
0 1 0 | 0 0 0 1 | 0 0
0 1 1 | 0 0 1 0 | 0 1
1 0 0 | 0 1 0 0 | 0 0
1 0 1 | 0 1 1 0 | 0 1
1 1 0 | 1 0 0 1 | 0 0
1 1 1 | 1 1 0 0 | 0 1
8 × 4
ROM
X2
X1
X0
Y5
Y4
Y3
Y2
Y1
Y0
0
Minimal ROM
Size = 23 × 4 bits