## Slide 1: MIPS Arithmetic and Logic Instructions
COE 233
Logic Design and Computer Organization
Dr. Muhamed Mudawar
King Fahd University of Petroleum and Minerals

## Slide 2: Instruction Categories
Integer Arithmetic (our focus in this presentation)
  Arithmetic, logic, and shift instructions
Data Transfer
  Load and store instructions that access memory
  Data movement and conversions
Jump and Branch
  Flow-control instructions that alter the sequential sequence
Floating Point Arithmetic
  Instructions that operate on floating-point numbers and registers
Miscellaneous
  Instructions that transfer control to/from exception handlers
  Memory management instructions

## Slide 3: R-Type Instruction Format
Op: operation code (opcode)
  Specifies the operation of the instruction
  Also specifies the format of the instruction
  Up to 26 = 64 opcodes  Not sufficient to define all instructions
funct: function code – extends the opcode
  Up to 26 = 64 functions can be defined for the same opcode
  MIPS uses opcode 0 to define many R-type instructions
Three Register Operands (common to many instructions)
  Rs, Rt: first and second source operands
  Rd: destination operand
  sa: the shift amount used by shift instructions
Op6
Rs5
Rt5
Rd5
funct6
sa5

## Slide 4: R-Type Integer Add and Subtract
Instruction | Meaning | Op | Rs | Rt | Rd | sa | func
add $t1, $t2, $t3 | $t1 = $t2 + $t3 | 0 | $t2 | $t3 | $t1 | 0 | 0x20
addu $t1, $t2, $t3 | $t1 = $t2 + $t3 | 0 | $t2 | $t3 | $t1 | 0 | 0x21
sub $t1, $t2, $t3 | $t1 = $t2 – $t3 | 0 | $t2 | $t3 | $t1 | 0 | 0x22
subu $t1, $t2, $t3 | $t1 = $t2 – $t3 | 0 | $t2 | $t3 | $t1 | 0 | 0x23
add, sub: arithmetic overflow causes an exception
  In case of overflow, result is not written to destination register
addu, subu: arithmetic overflow is ignored
addu, subu: compute the same result as add, sub
Many programming languages ignore overflow
  The + operator is translated into addu
  The – operator is translated into subu

## Slide 5: Carry versus Overflow
Carry is useful when adding (subtracting) unsigned integers
  Carry indicates that the unsigned sum is out of range
Overflow is useful when adding (subtracting) signed integers
  Overflow indicates that the signed sum is out of range
Range for 32-bit unsigned integers = 0 to (232 – 1)
Range for 32-bit signed integers = -231 to (231 – 1)
11111 1 1 11 1
1000 0100 0000 0000 1110 0001 0100 0001
1111 1111 0000 0000 1111 0101 0010 0000
1000 0011 0000 0001 1101 0110 0110 0001
+
Example 1: Carry = 1, Overflow = 0 (NO overflow)
Unsigned sum is out-of-range, but the Signed sum is correct

## Slide 6: More Examples of Carry and Overflow
Example 2: Carry = 0, Overflow = 1
01111 1 11 1
0010 0100 0000 0100 1011 0001 0100 0100
0111 1111 0111 0000 0011 0101 0000 0010
1010 0011 0111 0100 1110 0110 0100 0110
+
Unsigned sum is correct, but the Signed sum is out-of-range
Example 3: Carry = 1, Overflow = 1
1 11 1 11 1
1000 0100 0000 0100 1011 0001 0100 0100
1001 1111 0111 0000 0011 0101 0000 0010
0010 0011 0111 0100 1110 0110 0100 0110
+
Both the Unsigned and Signed sums are out-of-range

## Slide 7: Using Add / Subtract Instructions
Consider the translation of: f = (g+h)–(i+j)
Programmer / Compiler allocates registers to variables
Given that: $t0=f, $t1=g, $t2=h, $t3=i, and $t4=j
Called temporary registers: $t0=$8, $t1=$9, …
Translation of: f = (g+h)–(i+j)
addu $t5, $t1, $t2 # $t5 = g + h
addu $t6, $t3, $t4 # $t6 = i + j
subu $t0, $t5, $t6 # f = (g+h)–(i+j)
Assembler translates addu $t5,$t1,$t2 into binary code
000000
Op
01001
$t1
01010
$t2
01101
$t5
00000
sa
100001
addu

## Slide 8: Logic Bitwise Instructions
Instruction | Meaning | Op | Rs | Rt | Rd | sa | func
and $t1, $t2, $t3 | $t1 = $t2 & $t3 | 0 | $t2 | $t3 | $t1 | 0 | 0x24
or $t1, $t2, $t3 | $t1 = $t2 ¦ $t3 | 0 | $t2 | $t3 | $t1 | 0 | 0x25
xor $t1, $t2, $t3 | $t1 = $t2 ^ $t3 | 0 | $t2 | $t3 | $t1 | 0 | 0x26
nor $t1, $t2, $t3 | $t1 = ~($t2¦$t3) | 0 | $t2 | $t3 | $t1 | 0 | 0x27
x
0
0
1
1
y
0
1
0
1
x and y
0
0
0
1
x
0
0
1
1
y
0
1
0
1
x or y
0
1
1
1
x
0
0
1
1
y
0
1
0
1
x xor y
0
1
1
0
x
0
0
1
1
y
0
1
0
1
x nor y
1
0
0
0
NOT instruction is not needed, because
not $t1, $t2 is equivalent to: nor $t1, $t2, $t2

## Slide 9: Logic Bitwise Instructions
AND instruction is used to clear bits: x and 0  0
OR instruction is used to set bits: x or 1  1
XOR instruction is used to toggle bits: x xor 1  not x
Examples:
Given: $t1 = 0xabcd1234 and $t2 = 0xffff0000
and $t0, $t1, $t2
# $t0 = 0xabcd0000
or $t0, $t1, $t2
# $t0 = 0xffff1234
xor $t0, $t1, $t2
# $t0 = 0x54321234
nor $t0, $t1, $t2
# $t0 = 0x0000edcb

## Slide 10: I-Type Instruction Format
Constants are used quite frequently in programs
I-Type: Instructions with Immediate Operands
16-bit immediate constant is stored inside the instruction
  Rs is the source register number
  Rt is now the destination register number (for R-type it was Rd)
Examples of I-Type ALU Instructions:
  Add immediate: addi $t1, $t2, 5 # $t1 = $t2 + 5
  OR immediate: ori $t1, $t2, 5 # $t1 = $t2 | 5
Op6
Rs5
Rt5
immediate16

## Slide 11: I-Type ALU Instructions
Instruction | Meaning | Op | Rs | Rt | Immediate
addi $t1, $t2, 25 | $t1 = $t2 + 25 | 0x8 | $t2 | $t1 | 25
addiu $t1, $t2, 25 | $t1 = $t2 + 25 | 0x9 | $t2 | $t1 | 25
andi $t1, $t2, 25 | $t1 = $t2 & 25 | 0xc | $t2 | $t1 | 25
ori $t1, $t2, 25 | $t1 = $t2 ¦ 25 | 0xd | $t2 | $t1 | 25
xori $t1, $t2, 25 | $t1 = $t2 ^ 25 | 0xe | $t2 | $t1 | 25
lui $t1, 25 | $t1 = 25 << 16 | 0xf | 0 | $t1 | 25
addi: overflow causes an arithmetic exception
  In case of overflow, result is not written to destination register
addiu: same operation as addi but overflow is ignored
Immediate constant for addi and addiu is signed
  No need for subi or subiu instructions  Use negative immediate
Immediate constant for andi, ori, xori is unsigned

## Slide 12: Examples of I-Type ALU Instructions
Given that registers $t0, $t1, $t2 are used for A, B, C
Expression | Equivalent MIPS Instruction
A = B + 5; | 
C = B – 1; | 
A = B & 0xf; | 
C = B ¦ 0xf; | 
C = 5; | 
A = B; | 
addiu $t0, $t1, 5
addiu $t2, $t1, -1
andi $t0, $t1, 0xf
ori $t2, $t1, 0xf
addiu $t2, $zero, 5
addiu $t0, $t1, 0
No need for subiu, because addiu has signed immediate
Register $zero has always the value 0
Rt = $t2
Op = addiu
Rs = $t1
-1 = 0b1111111111111111

## Slide 13: 32-bit Constants
I-Type instructions can have only 16-bit constants
What if we want to load a 32-bit constant into a register?
Can’t have a 32-bit constant in I-Type instructions 
  The sizes of all instructions are fixed to 32 bits
Solution: use two instructions instead of one 
Suppose we want: $t1 = 0xAC5165D9 (32-bit constant)
  lui: load upper immediate
Op6
Rs5
Rt5
immediate16
lui $t1, 0xAC51
ori $t1, $t1, 0x65D9
0xAC51
$t1
Upper
16 bits
0x0000
Lower
16 bits
0xAC51
$t1
0x65D9

## Slide 14: Pseudo-Instructions
Introduced by the assembler as if they were real instructions
Facilitate assembly language programming
Pseudo-Instruction | Equivalent MIPS Instruction
move $t1, $t2 | 
not $t1, $t2 | 
neg $t1, $t2 | 
li $t1, -5 | 
li $t1, 0xabcd1234 | 
The MARS tool has a long list of pseudo-instructions
addu $t1, $t2, $zero
nor $t1, $t2, $zero
sub $t1, $zero, $t2
lui $t1, 0xabcd
ori $t1, $t1, 0x1234
addiu $t1, $zero, -5

## Slide 15: Shift Operations
Shifting is to move the 32 bits of a number left or right
sll means shift left logical (insert zero from the right)
srl means shift right logical (insert zero from the left)
sra means shift right arithmetic (insert sign-bit)
The 5-bit shift amount field is used by these instructions
shift-in 0
. . .
shift-out
sll
32-bit value
. . .
shift-in 0
shift-out
srl
. . .
shift-in sign-bit
shift-out
sra

## Slide 16: Shift Instructions (R-type only)
sll, srl, sra: shift by a constant amount
  The shift amount (sa) field specifies a number between 0 and 31
sllv, srlv, srav: shift by a variable amount
  A source register specifies the variable shift amount between 0 and 31
  Only the lower 5 bits of the source register is used as the shift amount
Instruction | Meaning | Op | Rs | Rt | Rd | sa | func
sll $t1,$t2,10 | $t1 = $t2 << 10 | 0 | 0 | $t2 | $t1 | 10 | 0
srl $t1,$t2,10 | $t1 = $t2 >>> 10 | 0 | 0 | $t2 | $t1 | 10 | 2
sra $t1,$t2,10 | $t1 = $t2 >> 10 | 0 | 0 | $t2 | $t1 | 10 | 3
sllv $t1,$t2,$t3 | $t1 = $t2 << $t3 | 0 | $t3 | $t2 | $t1 | 0 | 4
srlv $t1,$t2,$t3 | $t1 = $t2 >>>$t3 | 0 | $t3 | $t2 | $t1 | 0 | 6
srav $t1,$t2,$t3 | $t1 = $t2 >> $t3 | 0 | $t3 | $t2 | $t1 | 0 | 7

## Slide 17: Shift Instruction Examples
$t1 = 0x0000abcd
$t1 = 0xcd123400
Given that: $t2 = 0xabcd1234 and $t3 = 16
sll $t1, $t2, 8
sra $t1, $t2, 4
$t1 = 0xfabcd123
srlv $t1, $t2, $t3
Rt = $t2
Op
Rs = $t3
Rd = $t1
sa
srlv
01010
000000
01011
01001
00000
000110
srl $t1, $t2, 4
$t1 = 0x0abcd123

## Slide 18: Binary Multiplication
Shift Left Instruction (sll) can perform multiplication
  When the multiplier is a power of 2
You can factor any binary number into powers of 2
Example: multiply $t0 by 36
  $t0*36 = $t0*(4 + 32) = $t0*4 + $t0*32
sll $t1, $t0, 2 # $t1 = $t0 * 4
sll $t2, $t0, 5 # $t2 = $t0 * 32
addu $t3, $t1, $t2 # $t3 = $t0 * 36

## Slide 19: Your Turn . . .
sll $t1, $t0, 1 # $t1 = $t0 * 2
sll $t2, $t0, 3 # $t2 = $t0 * 8
sll $t3, $t0, 4 # $t3 = $t0 * 16
addu $t4, $t1, $t2 # $t4 = $t0 * 10
addu $t5, $t4, $t3 # $t5 = $t0 * 26
Multiply $t0 by 26, using shift and add instructions
Hint: 26 = 2 + 8 + 16
Multiply $t0 by 31, Hint: 31 = 32 – 1
sll $t1, $t0, 5 # $t1 = $t0 * 32
subu $t2, $t1, $t0 # $t2 = $t0 * 31

## Slide 20: Integer Multiplication in MIPS
Multiply instructions
  mult Rs, Rt Signed multiplication
  multu Rs, Rt Unsigned multiplication
32-bit multiplication produces a 64-bit Product
Separate pair of 32-bit registers
  HI = high-order 32-bit of product
  LO = low-order 32-bit of product
MIPS also has a special mul instruction
  mul Rd, Rs, Rt Rd = Rs × Rt
  Copy LO into destination register Rd
  Useful when the product is small (32 bits) and HI is not needed
Multiply
Divide
$0
HI
LO
$1
.
.
$31

## Slide 21: Integer Division in MIPS
Divide instructions
  div Rs, Rt Signed division
  divu Rs, Rt Unsigned division
Division produces quotient and remainder
Separate pair of 32-bit registers
  HI = 32-bit remainder
  LO = 32-bit quotient
  If divisor is 0 then result is unpredictable
Moving data from HI, LO to MIPS registers
  mfhi Rd (Rd = HI)
  mflo Rd (Rd = LO)
Multiply
Divide
$0
HI
LO
$1
.
.
$31

## Slide 22: Integer Multiply and Divide Instructions
Instruction | Meaning | Format |  |  |  |  | 
mult Rs, Rt | HI, LO = Rs ×s Rt | Op = 0 | Rs | Rt | 0 | 0 | 0x18
multu Rs, Rt | HI, LO = Rs ×u Rt | Op = 0 | Rs | Rt | 0 | 0 | 0x19
mul Rd, Rs, Rt | Rd = Rs ×s Rt | 0x1c | Rs | Rt | Rd | 0 | 2
div Rs, Rt | HI, LO = Rs /s Rt | Op = 0 | Rs | Rt | 0 | 0 | 0x1a
divu Rs, Rt | HI, LO = Rs /u Rt | Op = 0 | Rs | Rt | 0 | 0 | 0x1b
mfhi Rd | Rd = HI | Op = 0 | 0 | 0 | Rd | 0 | 0x10
mflo Rd | Rd = LO | Op = 0 | 0 | 0 | Rd | 0 | 0x12
mthi Rs | HI = Rs | Op = 0 | Rs | 0 | 0 | 0 | 0x11
mtlo Rs | LO = Rs | Op = 0 | Rs | 0 | 0 | 0 | 0x13
×s = Signed multiplication, ×u = Unsigned multiplication
/s = Signed division, /u = Unsigned division
NO arithmetic exception can occur

## Slide 23: Signed Integer Division
Simplest way is to remember the signs
Convert the dividend and divisor to positive
  Obtain the 2's complement if they are negative
Do the unsigned division
Compute the signs of the quotient and remainder
  Quotient sign = Dividend sign XOR Divisor sign
  Remainder sign = Dividend sign
Negate the quotient and remainder if their sign is negative
  Obtain the 2's complement to convert them to negative

## Slide 24: Signed Integer Division Examples
Positive Dividend and Positive Divisor
  Example: +17 / +3 Quotient = +5 Remainder = +2
Positive Dividend and Negative Divisor
  Example: +17 / –3 Quotient = –5 Remainder = +2
Negative Dividend and Positive Divisor
  Example: –17 / +3 Quotient = –5 Remainder = –2
Negative Dividend and Negative Divisor
  Example: –17 / –3 Quotient = +5 Remainder = –2
The following equation must always hold:
Dividend = Quotient × Divisor + Remainder